## Slide 1
3GPP TSG RAN Meeting #98-e
Electronic Meeting, December 12 – 16, 2022
RP-223142
Views on Coverage Enhancement and UE location verification for Rel-18 NR NTN
Agenda item: 9.3.2.7
Source: CATT
Document for: Decision

## Slide 2: Background: Description in WID
WID description(RP-222654)
<omitted>
4.1.1 Coverage enhancement
<omitted>
Have a 1-TU 6-month study phase focusing on the following (to derive clear & limited scope):
  Evaluate the coverage performance and identify the candidate physical radio channels that have coverage issues specific to NTN with following target services taking into account the studies in TR38.830 where appropriate, as well as general coverage enhancement techniques specified in Rel-18 [RAN1,RAN2,RAN4]
    VoIP and low-data rate services for commercial handset terminals
The following items are shown as examples of areas to consider in the RAN2 study.
  Improved performance of low-rate codecs in link budget limited situation including reducing RAN protocol overhead for VoNR
    NOTE: Intent is not to introduce a new codec.
RAN to determine by RAN#97 (for RAN1 items) and RAN#98 (for RAN2 items) whether the study phase has identified any need for NTN-specific coverage enhancements in Rel-18. If needed, the set of NTN-specific work item objectives will be further updated.
<omitted>
4.1.3 Network verified UE location
Pending on the conclusion of the RAN SI FS_NR_NTN_netw_verif_UE_loc study item, study and evaluate, if needed, solutions for network to verify UE reported location information [RAN2,RAN1,RAN3].
RAN is expected to determine by RAN#98 whether the study has identified any need for Network verified UE location specification support in Rel-18.
<omitted>

## Slide 3: Discussion(1/2)
For coverage enhancement
In RAN2#120e meeting, the following agreements have been achieved:
Agreements
RAN2 doesn’t consider using shorter PDCP SN for VoNR in NTN.
Using RLC TM mode for VoNR in NTN is not supported.
RAN2 doesn’t consider MAC enhancement to reduce MAC header size for VoNR in NTN.
Agreements
RAN2 will not specify signalling whereby the RAN knows the UE’s frame aggregation information in a voice packet
The objective related to RAN protocol overhead reduction for VoNR in current WID should be removed.
In Rel-17 IoT NTN, to support long PRACH, PUCCH and PUSCH transmission caused by repetition, segment based UE pre-compensation mechanism is introduced. If coverage enhancement is used for NR NTN, the same issue of TA pre-compensation during the repetition is also valid. This issue has a little discussion in RAN2#120e meeting, but no conclusion was achieved.
Proposal 1: RAN does not support protocol overhead reduction and should study the impact of repetition transmission, including to apply segment based UE pre-compensation for coverage enhancement scenario, taking the conclusion of Rel-17 IoT NTN as a baseline.

## Slide 4: Discussion(2/2)
For Network verified UE location
  RAN1，RAN2，RAN3 studied the methods on UE location verification base on the pre-study output in TR 38.882.
    RAN2 and RAN3 discussed and assumed the existing positioning architecture could be reused to support the UE location verification, it‘s core network to perform the UE location verification by triggering the LCS service. The evaluation and selection of the positioning methods are pending to RAN1.
    RAN1 discussed the potential positioning mechanisms, and some agreements have been achieved, as below:
Agreement
The following 3GPP defined RAT dependent positioning methods shall be considered as starting point for the study on Network verified UE location in case of NGSO based NTN deployment:
  Multi-RTT
  DL/UL-TDOA
Agreement
For the evaluation of time based positioning methods, further evaluation results taking into account satellite movement between TX and RX measurements should be provided.
Conclusion:
For network verification of UE location in NR NTN with single satellite in view with multi-RTT positioning:
From RAN1 perspective, if the UE’s Rx-Tx time difference measurements report can be assumed to be trusted, multi-RTT positioning method using Rx-Tx time difference measurements can meet the accuracy requirement of less than 10km with 90% confidence, in case of:
  At least LEO600 based deployment
  Earth fixed cells
  Earth moving cell at least if UE dwell time within the cell is enough to perform at least two RTT measurements
Conclusion
For network verification of UE location in NR NTN with single satellite in view with DL-TDOA positioning: From RAN1 perspective, if the UE’s RSTD measurements report can be assumed to be trusted, DL-TDOA positioning method can meet the accuracy requirement of less than 10km with 90% confidence, in case of:
  At least LEO600 based deployment
  Earth fixed cells
  Earth moving cell at least if UE dwell time within the cell is enough to perform at least two RSTD measurements
Proposal 2: If it is concluded in RAN#98e meeting to support Network verified UE location in Rel-18, the related objective need to be updated accordingly.

## Slide 5: Proposals(1/2)
Propose to update the WID as following:
<omitted>
4.1.1 Coverage enhancement
<omitted>
The detailed objectives are for NTN:
  To specify PUCCH enhancements for Msg4 HARQ-ACK (e.g. repetition) [RAN1, RAN4]
  To study DMRS bundling for PUSCH taking into account NTN-specifics (e.g. time-frequency pre-compensation) and, if necessary, specify enhancements to the Rel-17 procedures [RAN1]
  When repetition transmission scheme is used for PUCCH and PUSCH enhancement, study and specify the segmented UE pre-compensations for PUCCH and PUSCH enhancements [RAN1, RAN2]
Have a 1-TU 6-month study phase focusing on the following (to derive clear & limited scope):
  Evaluate the coverage performance and identify the candidate physical radio channels that have coverage issues specific to NTN with following target services taking into account the studies in TR38.830 where appropriate, as well as general coverage enhancement techniques specified in Rel-18 [RAN1,RAN2,RAN4]
    VoIP and low-data rate services for commercial handset terminals
The following items are shown as examples of areas to consider in the RAN2 study.
  Improved performance of low-rate codecs in link budget limited situation including reducing RAN protocol overhead for VoNR
    NOTE: Intent is not to introduce a new codec.
RAN to determine by RAN#97 (for RAN1 items) and RAN#98 (for RAN2 items) whether the study phase has identified any need for NTN-specific coverage enhancements in Rel-18. If needed, the set of NTN-specific work item objectives will be further updated.
<omitted>

## Slide 6: Proposals(2/2)
Propose to update the WID as following:
<omitted>
4.1.3 Network verified UE location
Pending on the conclusion of the RAN SI FS_NR_NTN_netw_verif_UE_loc study item, study and evaluate, if needed, solutions for network to verify UE reported location information [RAN2,RAN1,RAN3].
RAN is expected to determine by RAN#98 whether the study has identified any need for Network verified UE location specification support in Rel-18.
Specify network verified UE location mechanism with single satellite, considering at least Multi-RTT and DL-TDOA. [RAN1, RAN2, RAN3]
Note: Coordination with SA2 maybe needed, e.g. make aware of the ephemeris info in the LMF.
<omitted>