## Slide 1
3GPP TSG RAN Meeting #98-e
Electronic Meeting, December 12 – 16, 2022
RP-223143
Discussion on the IoT NTN enhancement WI objective updates
Agenda item: 10.2.1
Source: CATT
Document for: Decision

## Slide 2: Background: Description in WID
WID description(RP-221554)
<omitted>
4.1.1 IoT-NTN Performance Enhancements in Rel-18 to address remaining issues from Rel-17
This work considers Rel-17 IoT-NTN as baseline as well as Rel-17 NR-NTN outcome and the further IoT-NTN performance enhancements objectives are listed below:
- Disabling of HARQ feedback to mitigate impact of HARQ stalling on UE data rates [RAN1,RAN2]
- Study and specify, if needed, improved GNSS operations for a new position fix for UE pre-compensation during long connection times and for reduced power consumption. Simultaneous GNSS and NTN NB-IoT/eMTC operation is not assumed. [RAN1]
NOTE: The need for RAN4 Core requirements for this objective will be identified after the conclusion on the need for improvements.
4.1.2 Mobility enhancements
The following mobility enhancements objectives are listed.
  - Support of neighbour cell measurements and corresponding measurement triggering before RLF, using Rel‑17 (TN) NB-IoT, eMTC as a baseline. [RAN2]
  - Re-use the solutions introduced in Rel-17 NR NTN for mobility enhancements for eMTC, with minimum necessary changes to adapt them to eMTC [RAN2]
- Define UE RRM core requirements for the above mobility enhancement features [RAN4].
4.1.3 Further enhancement to discontinuous coverage
Potential enhancement to discontinuous coverage resulting from SA2 study (FS_5GSAT_Ph2).

## Slide 3: Discussion(1/2)
For performance Enhancements in Rel-18
In RAN1#109e, RAN1#110 , RAN1#110bis , and RAN1#111, , lots of agreements have been achieved, for example:
Agreements
Further study on whether there is a need for potential enhancements on the following for long connection time
  UE triggered GNSS measurement.
  Network triggered GNSS measurement.
Agreements
GNSS assistance information that UE reports to eNB at least consists of:
  GNSS position fix time duration for measurement
  GNSS validity duration
Agreement
When eNB triggers UE to make GNSS measurements, UE re-acquires GNSS position fix
Agreement
Support eNB to at least aperiodically trigger UE to make GNSS measurement.
Agreement
If eNB aperiodically triggers UE to make GNSS measurement, a MAC CE is used.
The UE may re-acquire GNSS autonomously (when configured by the network) if UE does not receive eNB trigger to make GNSS measurement
Agreement
UE reports GNSS position fix time duration for measurement at least during the initial access stage
  • which message carries this information is up to RAN2
Observation 1: RAN1 has concluded the necessity of GNSS measurement enhancement during long connection times, and some RAN2 work is needed. So the objective need to be updated accordingly.

## Slide 4: Discussion(2/2)
For mobility enhancement
In RAN2#120e meeting, the following agreement was achieved:
Agreements:
RAN2 doesn’t introduce neighbour cell ephemeris in Rel-17 IoT-NTN, neither for eMTC not for NB-IoT. RAN2 agrees to support this in Rel-18, with details FFS.
The objectives of the current WID needed to be updated to cover this issue.
For further enhancement to discontinuous coverage
  SA2 has finished the study of the SI FS_5GSAT_Ph2, two key issues related to discontinuous coverage have been identified, and about 23 solutions have been given（TR 23.700-28 V1.1.0 (2022-10)）.
Observation 2: RAN WGs can start the study to address the two key issues and relative solutions mentioned in the TR 23.700-28, or we just wait for the further progress of SA2.

## Slide 5: Proposals
Propose to update the WID as following:
<omitted>
4.1.1 IoT-NTN Performance Enhancements in Rel-18 to address remaining issues from Rel-17
This work considers Rel-17 IoT-NTN as baseline as well as Rel-17 NR-NTN outcome and the further IoT-NTN performance enhancements objectives are listed below:
- Disabling of HARQ feedback to mitigate impact of HARQ stalling on UE data rates [RAN1,RAN2]
- Study and specify, if needed, improved GNSS operations for a new position fix for UE pre-compensation during long connection times and for reduced power consumption. Simultaneous GNSS and NTN NB-IoT/eMTC operation is not assumed. [RAN1,RAN2]
NOTE: The need for RAN4 Core requirements for this objective will be identified after the conclusion on the need for improvements.
4.1.2 Mobility enhancements
The following mobility enhancements objectives are listed.
  - Support of neighbour cell measurements and corresponding measurement triggering before RLF, using Rel‑17 (TN) NB-IoT, eMTC as a baseline. [RAN2]
  Re-use the solutions introduced in Rel-17 NR NTN for mobility enhancements for eMTC, with minimum necessary changes to adapt them to eMTC [RAN2]
  Introduce neighbour cell ephemeris in serving cell system information, for eMTC and NB-IoT [RAN2]
- Define UE RRM core requirements for the above mobility enhancement features [RAN4].
4.1.3 Further enhancement to discontinuous coverage
Potential enhancement to discontinuous coverage resulting from SA2 study (FS_5GSAT_Ph2).
The following further discontinuous coverage enhancements objectives are listed.
  - Support further mobility management enhancement with discontinuous satellite coverage [RAN2, RAN3]
  - Support power saving enhancement for UE in discontinuous coverage [RAN2, RAN3]
  Notes: the output of SA2 SI (FS_5GSAT_Ph2) can be started as a baseline.