## Slide 1: Discussion on study for ambient IoT
NTT DOCOMO, INC.
3GPP TSG RAN #98-e
E-meeting, December 12th - 16th, 2022
Agenda Item: 9.2.3
Document for: Decision
RP-223161

## Slide 2: Background
New SID: Study on Ambient IoT
  SID (RP-222685) was approved at the RAN#97-e meeting.
  The followings are excerpted from SID objectives
Identify the suitable deployment scenarios and their characteristics, at least for the use cases/services agreed in SA1’s “Study on Ambient power-enabled internet of Things”, comprising among at least the following aspects
  Indoor/outdoor environment
  Basestation characteristics, e.g. macro/micro/pico cells-based deployments
  Connectivity topologies, including which node(s) , e.g. basestation, UE, relay, repeater, etc. can communicate with target devices
  TDD/FDD, and frequency bands in licensed or unlicensed spectrum
  Coexistence with UEs and infrastructure in frequency bands for existing 3GPP technologies
  Device originated and/or device terminated traffic assumption
NOTE: There can be more than one deployment scenario identified for a use case, and a deployment scenario may be common to more than one use case.
NOTE: Where more than one deployment scenario is identified for a use case, the trade-offs between them should also be studied.
NOTE: The study shall not prioritize deployment aspects that should be coordinated with SA, e.g. public or private network, with or without CN connection.
NOTE: A representative use case can be studied for a group of use cases that have similar requirements.
Formulate a set of RAN design targets based on the identified deployment scenarios and their characteristics for the relevant use cases, at least including
    Power consumption
    Complexity
    Coverage
    Data rate
    Positioning accuracy
NOTE: The requirements from SA1 on the relevant use cases shall be taken into consideration.
NOTE: The study shall aim to provide better coverage compared to existing non-3GPP technologies for the relevant use cases.
NOTE: Other RAN design targets in relation to connection density, mobility, security, latency, reliability etc. may be discussed, if necessary for the relevant use cases.
NOTE: Detailed definitions of the RAN design targets should be discussed during the study.
…

## Slide 3: Suitable deployment scenarios
Connectivity topologies and involved nodes
  Connectivity Topologies
    Possible scenario:
      Opt.1: Ambient IoT device can directly connect with base station.
      Opt.2: Ambient IoT device can connect with reader device.
        This scenario is practical in terms of the expected communication range for ambient IoT devices.
        It can avoid large impacts on the interface between the base station and the reader device.
    Proposal: At least the scenario that the ambient IoT device can connect with reader device, i.e., relay-like topology, should be considered.
  Details for reader device
    Possible assumptions for reader device: IAB, repeater, handheld UE, etc.
      It is preferable that a reader device can flexibly address the short communication range of ambient IoT device.
      Large number of reader devices may be required to ensure the coverage for ambient IoT devices considering the short communication range for ambient IoT device.
    Proposal: At least handheld UE which has mobility should be considered for reader device.
BS
Reader
Ambient IoT
device
Opt.1
Opt.2

## Slide 4: Suitable deployment scenarios
Connectivity topologies and involved nodes (Cont.)
  Interface for reader device and ambient IoT device
    Possible interface between reader device and ambient IoT device: New interface, existing NR-based (e.g., SL), not specify in 3GPP, etc.
    Impacts on NR would depend on whether/how to define the interface for ambient IoT device.
    Proposal: Regarding whether/how to define the interface for ambient IoT device, impacts on NR need to be further studied.
Device originated/terminated traffic assumption
  It needs to be further discussed to identify for which use case(s) device terminated traffic is required and whether to support such use case(s).
  Proposal: At least device originated traffic should be assumed.
    FFS: Device terminated traffic
 | New interface | Existing NR-based | Not specify in 3GPP
Spec impacts | High | Middle | Low
NW impacts | FFS | FFS | FFS

## Slide 5: RAN design targets
Coverage:
  It is unclear whether the term “coverage” means whole coverage as NW or the communication range b/w reader device and ambient IoT device
  Proposal: For the coverage for ambient IoT devices, the following two aspects should be discussed.
      Whole coverage as NW which aims larger coverage than non-3GPP technology
      Communication range between reader device and ambient IoT device
Data rate:
  SID states ambient IoT shall not aim to replace 3GPP LPWA
  Use cases in TR22.840 require up to [5]kbps
  Proposal: Peak rate lower than LPWA, e.g., up to 5kbps, can be the starting point for the target.
Positioning accuracy:
  Total positioning accuracy : BS-Reader & Reader-ambient IoT device
    BS-Reader: existing positioning feature can be reused
    Reader-ambient IoT device: FFS
  Proposal: At least positioning accuracy between reader and ambient IoT device should be studied.
BS
Reader
Ambient IoT
device
Whole coverage as NW
BS
Reader
Ambient IoT
device
Reuse
Existing
positioning
Need to
be studied