## Slide 1
Source: LG Uplus, KT, SKT, ETRI
3GPP TSG-RAN #97-e RP-222245
E-meeting, 12th - 16th September 2022
Summary of UAM contribution

## Slide 2: Contents
Background
Possible Solutions
Analysis of Solutions
WID revisions (RP-222226, RP-222246)
Proposals

## Slide 3: 1. Background
Issues on a legacy device in the aerial vehicle
Rel-18 device would adopt the feature of measurement report based on the altitude. However, legacy devices will not have the feature and, hence, network will not be able to do proper network management for them.
NRT will be distorted by wrong neighbour cell report by legacy device in the air due to different channel characteristics.
New spectrum for UAM is the easiest way for network management but would not be available for legacy devices.
UAM commercial service in Korea
UAM commercial service will be launched in the end of 2024 by government.
As comparing to UAV, UAM should consider a service scene where the legacy devices such as Rel-15/16/17 ride the aerial vehicle.
* https://www.ericsson.com/en/blog/2017/11/how-mobile-networks-can-support-drone-communication

## Slide 4: 2. Possible solutions

## Slide 5: 3. Analysis of solutions
Table 1: Analysis of candidate solutions handling legacy device riding aerial vehicle
Solution | Redeeming throughput degradation | Preventing NRT distortion | UAM dedicated spectrum | UE Power Saving | NSA | Specification
Mobile IAB | Support | Support | Available | Available | Not Support | Measurement report triggered by altitude in mobile IAB MT Provisioning mapping information between UE ID and flying state to AMF/MME/donor gNB Preventing ground cell reselection
Application | Support | Not Support | Not Available | Not Available | Support | Provisioning flying state information of a legacy UE among AF/UDM/PCF/AMF/MME Provisioning flying state information of a legacy UE between AMF(or MME) and gNB (or eNB)

## Slide 6: 4. Proposals
Proposal 1: It is proposed to insert mobile-IAB-based solution for UAM into mobile IAB WI.
Proposal 2: It is proposed to add the requirement of legacy devices in UAM into NR UAV WI.
Proposal 3: It is proposed to ask SA2 to proceed application-server-based solution development by TEI18 via Liaison

## Slide 7: 5. Mobile WID revision (RP-222226)
3 Justification
The support for Mobile Integrated Access and Backhaul (IAB) builds on the architecture and protocols derived in the Rel-17 WI NR_IAB_enh, which provided IAB improvements on various aspects such as robustness, load-balancing, spectral efficiency, and end-to-end performance.
The work on Mobile IAB in Rel-18 should focus on the scenario of mobile-IAB-nodes mounted on ground or aerial vehicles providing 5G coverage/capacity enhancement to onboard and/or surrounding UEs.
In Rel-18, mobile IAB supports the following functionality, applicable to FR1 and FR2:
In-band and out-of-band backhauling.
The mobile IAB-node should have no descendent IAB-nodes, i.e., it serves only UEs.
Solutions should support UE HO and DC.
The MT of a mobile IAB-node should support UAV features for UAM service.
4 Objective
4.1 Objective of SI or Core part WI or Testing part WI
The detailed objectives of the WI are listed as follows:
Define Procedures for migration/topology adaptation to enable IAB-node mobility, including inter-donor migration of the entire mobile IAB-node (full migration) [RAN3, RAN2]
Enhancements for mobility of an IAB-node together with its served UEs, including aspects related to group mobility. No optimizations for the targeting of surrounding UEs. [RAN3, RAN2]
Note: Solutions should avoid touching upon topics where Rel-17 discussions already occurred and where the topic was excluded from Rel-17, except for enhancements that are specific to IAB-node mobility.
Mitigation of interference due to IAB-node mobility, including the avoidance of potential reference and control signal collisions (e.g. PCI, RACH). [RAN3, RAN2]
The MT of IAB-node equipped with UAV features [RAN2]
As for UAM use case, define procedures for the DU of IAB-node to provide flying state information of a UE riding the aerial vehicle. [RAN3]

## Slide 8: 6. NR UAV WI revision (RP-222246)
3 Justification
==== Addition of UAM requirement====
Further, the legacy device (i.e. a Rel-15/16/17 device and a non-UAV Rel-18 device) riding an aerial vehicle has to be considered for UAM (Urban Aerial Mobility) commercialization. For this scenario, the best performance for the UEs could not be achieved since network cannot obtain actual measurement report from the legacy devices. However, the flying state information can be delivered to access network through core network from application server, which information will be generated by the application of the legacy devices. By the flying state information, the access network can provide a legacy UE for appropriate solutions such as HO parameter optimization, CoMP operation, beam steering, etc. It could also prevent the disruption of the operation of a network designed for terrestrial UEs, e.g. erroneous ANR operation by the measurement report from the legacy devices in the aerial vehicle.
4 Objective
4.1 Objective of SI or Core part WI or Testing part WI
==== Addition of flying stat====
5. Specify the provisioning method of flying state information delivered from 5GC, which information will help access node (both LTE and NR) to provide proper solution to the legacy devices (Rel-15/16/17 device and a non-UAV device in Rel-18) as riding in aerial vehicle and will be also transferred to a target gNB during HO procedure [RAN3].

## Slide 9: 7. LS to SA2 (RP-222281)
1 Overall Description
====Omitted====
To solve this problem, we would like to consult SA2 whether application-server-based solution can be supported through TEI-18. Legacy device would send the information about flying to AF (UTM) by application. AF delivers the information to AMF/MME through UDR/PCF. With the corresponding N2 (S1) signalling from AMF/MME, gNB/eNB could cope with dedicated radio configuration for the legacy device. RAN can confirm this flying state information is useful for network to provide a proper solution (e.g. HO parameter optimization, Beam direction change, CoMP operation, etc). Hence, RAN kindly asks SA2 to proceed solution development in TEI18.
2 Actions
To SA2
ACTION: RAN respectfully asks SA2 to take the above information into account and provide RAN with reply whether above work can be done as TEI18 within Release-18 timeframe.

## Slide 10
Thank you