## Slide 1: On WI scope for NR network energy saving
Ericsson
3GPP TSG RAN meeting #98
Electronic Meeting
December 12 - 16, 2022 Agenda Item: 9.1.1
RP-223188

## Slide 2: Introduction
Outcome of the NW energy saving study (SID in RP-221443) is captured in TR38.864 approved in R1-2213007 at RAN1#111
TU allocation for NW energy saving SI
  RAN1 (1 TU, 4 meetings), RAN2 (1 TU, 3 meetings), RAN3 (0.5 TU, 3 meetings), RAN4 (No discussion)
Discussion is expected in RAN#98 on possible WI on NW energy saving
  TU details
    RAN1/2/3 : planned allocation in RP-221925
    RAN4 : planned allocation in RP-220980

## Slide 3: Rel-18 SI discussion
RAN1 discussion
  BS power consumption modeling and evaluation methodology
    Discussed from May to October and details finalized in October RAN1 meeting
  NW energy saving techniques and evaluations
    Limited opportunity for discussion and cross-verification of evaluation results for many techniques
    Evaluation results based on agreed methodology discussed in one meeting together with TR updates (November)
RAN2/3 discussion
  Discussion on techniques and input for TR from August to November

## Slide 4: Conclusions from TR
Spatial domain technique C-1 recommended for WI in TR
Time/frequency techniques
  No recommended technique in TR, some identified as “beneficial for network energy savings”
Power domain technique
  No recommended technique in TR, one (D-1) identified as “beneficial for network energy savings”
Spatial domain technique C-2 identified as having “potential to provide large network energy saving gain”

## Slide 5: Views on WI objectives
Support WI objectives based on techniques C-1 and D-1
  These UE-specific signaling enhancements provide evolution path for existing NW energy saving mechanisms
  E.g. C-1 : specify signaling enhancements for spatial domain adaptation, i.e. signaling to update the active CSI-RS configurations for CSI reporting, CSI-RS (re)configuration for CSI reporting and enhancements to CSI measurement/reporting
  E.g. D-1 : specify signaling of modified power ratio for CSI-RS wrt other channels/signals to provide adaptation of power ratio values and enhancements to CSI measurements/reporting
  Proposed TUs for RAN4 shown below : Updates : (1) for RD, yellow shows updates relative to RP-220980 and (2) removal of UE RF TUs
Continue study for other techniques in Q1’2023
  WGs to discuss/evaluate detailed technique/combination of techniques with aim to identify clearly defined proposal(s) for WI phase
  Revisit in RAN#99 to check progress and identify potential additional WI objectives

## Slide 7
Annex

## Slide 8: Discussion for Time/frequency domain techniques (1/2)
A-1-1: Use simplified version of SSB, such as only PSS, only PSS and SSS without PBCH, or PSS and SSS with partial PBCH
A-1-2: Transmission occasion of one or more common signals/channels (which are SIB1 and SSB) are skipped
A-1-3: Configuration/adaptation of longer periodicity of common signals and/or uplink random access opportunities
A-1-4 (Paging enhancement): configuration/adaptation of transmission patterns of Paging
A-1-5 (RACH): adapting common signal RACH
A-1-6: Scheduling of SIB1 by SSB, without PDCCH for SIB1
A-3:UE wake up signal (WUS) for gNB: UE requests transitioning of a cell from no or reduced transmission/reception activity to active transmission or reception of a channel/signal
A-4 (DTX/DRX): Providing mechanisms informing UE whether the cell stays inactive. This may include enhancements to UE DRX configuration, e.g. to align/omit DRX cycles or start offsets of DRX….. During a cell DTX/DRX, the cell may have no transmission/reception or only keep limited transmission/reception
A-5-1: For non-CA, the UE may obtain system information from other associated carriers/cells and synchronize from other associated carriers/cells and/or synchronize from signal(s) transmitted on the cell
A-5-2: SSB/SIB1 transmission at the serving cell can be triggered on-demand, e.g. by the UE
B-1-1: Inter-band CA with SSB-less SCell. The synchronization is acquired from other cell with SSB transmission or same cell with simplified signal transmission, also in order for fast activation and deactivation of SCell
B-1-2: Dynamic PCell switching in which a common primary cell may be dynamically indicated for a group of UEs
B-2: Enhancements to enable UE group-common or cell-specific BWP configuration and/or switching

## Slide 9: Discussion on Time/frequency domain techniques (2/2)
  Combinations are needed to have functional scheme for several techniques
    e.g. (A-1-1 (Light-SSB) or Discovery signal) + A-3 (UE WUS) + A-5-2 (on-demand SSB/SIB1 transmission) + possibly A-1-3 (longer periodicity of common signals/channels), ……
  Some may work individually (e.g. A-1-3, A-1-4, A-1-5,…)
  Legacy UEs cannot access a carrier (e.g. A-1-1, A-1-2, A-1-6, A-5-1 (at least some sub-techniques), A-5-2, B-1-1, …..)
    Impact on overall system performance when certain carriers are inaccessible to legacy UEs
    Limitations on use of a carrier as PCell/PSCell/SCell for legacy UEs depending on the technique
    Impact on SI acquisition, initial access, RRM/RLM measurements, and mobility
  Clear differentiation over existing specification needed
    E.g. existing specification allows e.g. alignment of DRX across multiple UEs, variable SIB1 transmission repetition periodicity, etc