## Slide 1: Ambient IoT - Deployment Scenarios - Device Characteristics
MediaTek Inc.
3GPP TSG RAN#98e RP-223239
Electronic December 13th-17th 2022 Agenda Item 9.2.3

## Slide 2: Introduction
New RAN-level SID approved at RAN#97e: RP-222685
RAN#98e targets
  Initial discussion on suitable deployment scenarios and their characteristics
  Initial discussion on device categorization
A fundamental requirement for Ambient IoT as formulated in the objective is:
  The study shall provide clear differentiation, i.e. addressing use cases and scenarios that cannot otherwise be fulfilled based on existing 3GPP LPWA IoT technology e.g. NB-IoT including with reduced peak Tx power
SA1 TR22.840 v0.3.0 is available in S1-223508
  The TR contains 28 use cases but no consolidated potential requirements or KPIs at this time

## Slide 3: Snapshot of SA1 use cases [1/2]
Use case | Comm. Trigger | Comm. range | Indoor / Outdoor | Mobility
Automated warehousing | MT | 30m | Indoor | 5-10km/h
Medical Inventory mgmt and positioning | MT | 50m 200m | Indoor Outoor | Static / walking <6km/h
Substations in smartgrid | MT | [50-200m] | Outdoor | N/A
NPN for logistics | MT | ? | ? | ?
Automobile manufacture | MT | <30m | Indoor | N/A
Smart home sensors | MT | [10-30m] | Indoor | Stationary
Airport terminal / shipping | MT? | FFS | FFS (Outdoor?) | N/A
Finding remote lost item | MO to UE | 50m 100m | Indoor Outdoor | N/A N/A
LCS | MT | N/A | Indoor Outdoor | 5km/h ≤20km/h
Ranging | MT | 10m IC/PC/OOC | Indoor (home) | Static (<1m/s)
Online modif of medical instruments status | MT | 50m 200m | Indoor Outdoor | Static / walking <6km/h
Personal belonging finding | MT | 10m 100m | Indoor Outdoor | Static Static
BS machine room environmental supervision | MT | 30m | Indoor | N/A
Use case | Comm. Trigger | Comm. range | Indoor / Outdoor | Mobility
Indoor positioning in shopping centre | MT | 10m | Indoor | N/A
Smart laundry | MT | N/A | N/A | N/A
Automated supply distrib. | MT | N/A | N/A | N/A
Device (de)activation | MT | N/A | N/A | N/A
Fresh food supply chain | MT | N/A | N/A | N/A
Forest Fire Monitoring | MO | [150m-FFS] | Outdoor | N/A
Smart Agriculture | MT | 30-100m | Indoor | Static
Museum Guide | MT | [30m] | Indoor | [3km/h]
Smart grazing dairy farming | MT | FFS | Outdoor | N/A
Smart pig farm | MT | 250m | Indoor | N/A
Manhole cover safety | MT | FFS | Outdoor? | N/A
Smart bridge health monitoring | MT | FFS | Outdoor? | N/A
Elderly health care | MT | ? | ? | ?
End-to-end logistics | MT | ? | Indoor/Outdoor | ?
Pressure-powered switch | MO | ? | ? | ?

## Slide 4: Snapshot of SA1 use cases [2/2]
Communication trigger
Observation 1: the vast majority of use cases in SA1 draft TR are such that the target device is systematically triggered before communicating i.e. it does not otherwise communicate
Observation 2a: for the remaining 3 use cases, the device initiates communication
  To nearby UE(s) only [Finding remote lost item]
  To the 5G system itself [Forest fire monitoring]
  To the 5G system itself [Pressure switch]
Observation 2b:
  The use case on forest fire monitoring and pressure switch are readily addressable with existing 3GPP IoT technology
  The use case on finding remote lost item is already available today (using e.g. BTLE)
Proposal
  In view of the above it is proposed to focus the RAN study only on MT-triggered communication i.e. the Ambient IoT device does not communicate unless triggered by a DL signal
Communication range:
Observation 3: most communication ranges among the use cases are 50m or less (typ 30m or less)
Observation 4a: among use cases with range of 100m and above we can observe the following
  Substations in smartgrid (250m)
  Finding remote lost item / personal belonging finding (100m)
  Online modification of medical instrument status (200m)
  Smart agriculture
  Smart pigfarm
Observation 4b:
  The last two (smart agriculture and pigfarm) could be addressed with denser reader devices, keeping the range below 50m
  The other two (substations in smartgrid and online modification of medical instrument status) can be addressed with existing IoT technology
Proposal
  In view of the above it is proposed to focus the RAN study on range of 50m or less

## Slide 5: Deployment Scenarios [1/3]
Ambient-IoT radio
  is a local radio operating only between Reader Device and Tag
  over licensed spectrum (under full MNO control) or unlicensed spectrum
The Reader Device:
  can be handheld, mounted to infrastructure (e.g. base station) etc.
  may or may not be battery constrained (depending on the scenario)
  can (but does not necessarily need to) connect to an Ambient-IoT server.
  The connection between a Reader device and the Ambient-IoT Server is not in scope of 3GPP (it can rely on *any* transport incl. 3GPP conn.)
The Tag:
  may only connect to a Reader Device with Ambient-IoT Radio
  has no active connection to any Ambient-IoT server
  Any data exchange between the Tag and Server is via the Reader Device (e.g. Tag signature, configuration, data reporting). It is not in scope of 3GPP
Amb-IoT Reader Device
Amb-IoT Tags
Amb-IoT Radio
(Local)
Amb-IoT Server

## Slide 6: Deployment Scenarios (examples) [2/3]
Reader Device
(with 3GPP TN/NTN connectivity)
Tags
Amb-IoT Radio
(Local)
Uu
(w/ radio resource control & coord. signaling for Amb-IoT)
e/gNB
(e.g. NR/RedCap/LPWAN)
Reader Device
(with non-3GPP connectivity)
Tags
Amb-IoT Radio
(Local)
Non-3GPP
Non-3GPP Access
(e.g. WiFi)
Reader Device
(Base-station mounted)
Tags
Amb-IoT Radio
(Local)
Reader Device
Tags
Amb-IoT Radio
(Local)

## Slide 7: Device characteristics
See appendix – as previously proposed

## Slide 8: Appendix – RP-222335
RP-2223335: Passive IoT, not another 3GPP LPWA, MediaTek Inc., Deutsche Telekom, RAN#97e, September 2022

## Slide 9: Background
Initial Proposal: RAN Rel-18 WS, Jun/2021
  RWS-210453
Related 3GPP Activity
  [SA1] Rel-19 Stage 1 Study ongoing
    (link) – started Dec’21
    TR 22.840 (link)
    Related but not 1:1 mapped
    It is important that RAN output feeds into SA1 study
  [SA2] Rel-18: No work ongoing or planned
    Rel-18 already over-packed
  [RAN] Rel-18: No work ongoing
    Email discussion RP-212688 (RAN#93e - #94e)
    Further discussions took place at RAN#96
Focus on use cases that cannot otherwise be fulfilled based on existing 3GPP LPWA IoT technology (incl. with reduced peak Tx power)
x 1 Gbps | Day
x 10 Mbps | Days
x 1 Mbps | Year
x 10 kbps | Years
x 1 kbps | (N/A)
NR
RedCap
LTE-M
NB-IoT
Passive IoT

## Slide 10: Our View Very focused RAN-level study – NO new 3GPP LPWAN
Passive IoT – “Passive IoT Tag”
Power consumption 1 – 10µW
Complexity Ultra-low ≈ commercial sub-GHz RFID
Coverage 10 – 30 m
Characteristics Device “Tag” constraints drive the tech NOT vice-versa Sticker form-factor ca. 5cm x 5cm “Disposable” Battery-less PIoT Tag Small coverage: Reader UE can “manage” PIoT Tag Device-device interface only, between Reader UE & PIoT Tag e/gNB <Uu> Reader UE <PIoT Radio> PIoT Tag Spectrum for PIoT Radio Very limited set of bands and global operation If Licensed spectrum: PIoT resources controlled + coordinated by e/gNB if available or by Reader UE configuration.* DL triggered communication only Security: Reader UE <> PIoT Device
NR/LPWAN Uu
(incl. PIoT radio resource control & coord. signaling)
e/gNB
(e.g. NR/RedCap/LPWAN)
Reader UE e.g. handheld/hub
(e.g. NR/RedCap/LPWAN + PIoT)
PIoT Tags (PIoT)
PIoT Radio
(Local)
PIoT: Passive IoT
NOTE *: Subset of existing control signaling framework for Uu control/coord. of SL operation could be leveraged

## Slide 11: Thank You!