## Slide 1
Further enhancement of RAN slicing in Rel-18
3GPP TSG RAN#98
Electronic Meeting, December 12 - 16, 2022
Source: ZTE, Sanechips
Agenda: 9.1.3
RP-223267

## Slide 2: Rel-18 network slicing progress in SA2
SA2 has completed the Rel-18 FS_eNS_Ph3 study in TR 23.700-41.
A follow up WI has been approved in SA2 (S2-2210684) to address the following issues
  Key Issue #1: Support of Network Slice Service continuity
  Key Issue #2: Support of providing VPLMN network slice information to a roaming UE
  Key Issue #3: Network Slice Area of Service for services not mapping to existing TAs boundaries and Temporary network slices
  Key Issue #4: Support of NSAC involving multi service Area
  Key Issue #5: Improved support of RAs including TAs supporting Rejected S-NSSAIs
  Key Issue #6: Improved network control of the UE behaviour

## Slide 3: Key issues in FS_eNS_Ph3 with RAN impact (1)
Key issues in new WID on further enhancement of RAN Slicing for NR in SA2 | RAN impact
Key Issue#1: Support of Network Slice Service continuity | For an existing PDU Session transfer from the old S-NSSAI to an alternative S-NSSAI, in order to ensure service continuity: The SMF may determine that the PDU session needs to be retained and the slice resource cannot be repartitioned. In this case the SMF may send the alternative S-NSSAI to the UE in the PDU Session Modification Command, to the UPF in the N4 message and to the RAN in N2 message.
Key issue#3:Network Slice Area of Service for services not mapping to existing TAs boundaries and Temporary network slices | How the handover can be optimized to prevent the UE from leaving the slice service area (or entering into the slice service area) will be considered during normative phase based on RAN (e.g. Conditionally Allowed NSSAI should be introduced in NG-C, Xn interface)? NG-RAN should inform AMF the slice availability information (e.g. with time/location information).

## Slide 4: Key issues in FS_eNS_Ph3 with RAN impact (1)
Key issues in new WID on further enhancement of RAN Slicing for NR in SA2 | RAN impact
Key issue#5:Improved support of RAs including TAs supporting Rejected S-NSSAIs | For Partly allowed S-NSSAI: If a requested S-NSSAI is not supported in the current TA but supported in other TAs part of the RA, or the requested S-NSSAI is supported in the current TA but not supported in all other TAs of the RA, the AMF (for supporting UEs) may indicate to the UE that some S-NSSAIs are allowed only in some TAs of the RA by indicating the TAs where these are supported and also registered. If so, the UE assumes it can use the connectivity for the slices in the TAs where it is indicated to be supported. In this approach, the Allowed NSSAI is still uniformly supported in the RA but the additional IE sent to the UE e.g. Partially Allowed S-NSSAI is not uniformly supported in the RA. The AMF sends the Partially/Conditionally Allowed S-NSSAI to NG-RAN in the same messages as the Allowed NSSAI is sent.

## Slide 5: Proposal on further enhancement of RAN slicing in Rel-18
Observation: Clear impact on RAN can be seen from the key issues and solutions in Rel-18 FS_eNS_Ph3 study in SA2.
Proposal: A WI is required in Rel-18 to address the corresponding impact on RAN with the following objectives:
  RAN impacts of SA2 slicing enhancement in Rel-18:
    Specify the solutions to support of Network Slice Service continuity for inter RA Mobility scenario. [RAN3]
    Specify the solutions to support Network Slice Area of Service for services not mapping to existing TAs boundaries and Temporary network slices. [RAN3]
    Specify the solutions to support improved support of RAs including TAs supporting Rejected S-NSSAIs.[RAN3]

## Slide 6: Thanks!