## Slide 1: Rel-18 Expanded and Improved Positioning WI Scope
3GPP TSG RAN Meeting #98-e RP-223336
e-meeting, December 12 – 16, 2022
Agenda Item: 9.1.1
Source: FUTUREWEI
Document for: Discussion and decision

## Slide 2: Outline
In this contribution we discuss WI Positioning scoping
The contribution has two parts:
  The first part deals with Sidelink Positioning checkpoint on bandwidth requirements and unlicensed spectrum usage
  The second part discusses the overall WI scoping (SL positioning, LPHAP, RedCap, PRS/SRS BW aggregation, integrity, CPP)

## Slide 3: SL Positioning Checkpoint
One of the objectives of the Expanded and improved NR positioning study item was specified in SID (RP-222616) and concerns whether the unlicensed spectrum should be considered for sidelink positioning:
  Evaluate bandwidth requirement needed to meet the identified accuracy requirements [RAN1],
  ...
  Note: When the bandwidth requirements have been determined and the study of sidelink communication in unlicensed spectrum has progressed, it can be reviewed whether unlicensed spectrum can be considered in further work. Checkpoint at RAN#98 to see if sufficient information is available for this review.

## Slide 4: RAN1 findings and recommendation
During Q4, 2022, companies studied and presented their evaluations of the performances for various use cases, scenarios, and positioning methods
The findings and recommendations were captured in the following agreement:
Agreement (R1-2212950)
Capture the following as part of the Conclusions section of TR 38.859:
  Evaluation results reported as part of the study indicate that, depending on sources, use-cases, scenarios, assumptions, and positioning methods used, the identified target requirements can be satisfied with different values of SL-PRS bandwidth choices.
    For FR1 spectrum:
      For certain sources and combinations of use-cases, scenarios, assumptions, and positioning methods, some target requirements can be satisfied with SL-PRS bandwidths of 20 MHz or 40 MHz.
      For certain sources and other combinations of use-cases, scenarios, assumptions, and positioning methods, some target requirements require SL-PRS bandwidth of 100 MHz or may not be satisfied even with SL-PRS bandwidth of 100 MHz.
    For FR2 spectrum, based on submitted results from up to two sources:
      For certain sources and combinations of use-cases, scenarios, assumptions, and positioning methods, some target requirements can be satisfied with SL-PRS bandwidth of 200 MHz.
      For certain sources and combinations of use-cases, scenarios, assumptions, and positioning methods, some of the target requirements may not be satisfied even with SL-PRS bandwidth of 400 MHz.
  From RAN1’s perspective, it is recommended that SL-PRS bandwidths of up to 100 MHz are supported by the specifications in FR1 spectrum.
Note: The above recommendations are based on the evaluations in licensed and ITS spectra.

## Slide 5: Discussion
It was shown that in FR1 the SL positioning requirements can be satisfied with SL-PRS BW of up to 100 MHz
The SL positioning study focused on FR1 (ITS and licensed), which has the most use cases (including V2X, public safety, commercial, IIoT)
The evaluation of FR2 SL positioning performance was only optionally considered (only 2 sources reported evaluation results) and most of the evaluations show that the requirements may not be satisfied even with 400 MHz
Aggregation of unlicensed spectrum for SL positioning implies the existence of CA solutions for SL
The PRS/SRS bandwidth aggregation agenda item showed feasibility only for contiguous carriers, which may not be the case for BW aggregation of licensed and unlicensed spectrum

## Slide 6: SL Positioning Checkpoint Proposals
Proposal 1: In R18, SL positioning work should not consider unlicensed spectrum-based solutions (for FR1 or FR2).
Proposal 2: Deprioritize SL positioning work for FR2.

## Slide 7: Overall WI scoping: Improved accuracy, integrity, and power efficiency
The objective on improved accuracy, integrity, and power efficiency in the SID (RP-222616) contains four different topics:
  Study solutions for Integrity for RAT dependent positioning techniques [RAN2, RAN1]:
    Identify the error sources, [RAN1, RAN2].
    Study methodologies, procedures, signalling, etc for determination of positioning integrity for both UE-based and UE-assisted positioning [RAN2]
    Focus on reuse of concepts and principles being developed for RAT-Independent GNSS positioning integrity, where possible.
  Study solutions for accuracy improvement based on PRS/SRS bandwidth aggregation for intra-band carriers considering e.g. timing errors, phase coherency, frequency errors, power imbalance, etc [RAN4]:
  Study solutions for accuracy improvement based on NR carrier phase measurements [RAN1, RAN4]
    Reference signals, physical layer measurements, physical layer procedures to enable positioning based on NR carrier phase measurements for both UE-based and UE-assisted positioning [RAN1]
    Focus on reuse of existing PRS and SRS, with new reference signals only considered if found necessary
  Study the requirements on LPHAP as developed by SA1 and evaluate whether existing RAN functionality can support these power consumption and positioning requirements. Based on the evaluation, and, if found beneficial, study potential enhancements to help address any limitations [RAN2, RAN1]
    Study is limited to a single representative use case (use case 6 as defined TS 22.104). The choice of selected use case can be reviewed at the start of the study.
    Study is limited to enhancements to RRC_INACTIVE and/or RRC_IDLE state

## Slide 8: TR 38.859 Recommendations (R1-2213017)
7.3 Sidelink Positioning Solutions
Sidelink positioning is recommended for normative work.
7.4 Integrity for RAT-Dependent Positioning Techniques
Both UE-based and LMF-based integrity for RAT-Dependent Positioning Techniques are recommended for normative work.
7.5 PRS/SRS Bandwidth Aggregation
As part of the current study, PRS/SRS bandwidth aggregation for intra-band contiguous carriers is studied by RAN4. Based on the study, PRS/SRS bandwidth aggregation for intra-band contiguous carriers is concluded as feasible for single chain Tx/Rx architectures at both the UE and gNB.
7.6 NR Carrier Phase Positioning
Based on the study, it is concluded that it is feasible to use existing DL PRS and SRS signals to obtain the carrier phase measurements for achieving a horizontal accuracy of up to a few centimeters at least at 50% under certain conditions, including the PRU(s) being located in LOS with TRP(s), and the locations of the PRU(s) and TRPs known with centimeter-level accuracy, in the agreed evaluation assumptions.
7.7 Low Power High Accuracy Positioning
Based on the evaluation, it is concluded that enhancements to meet the target battery life in Rel-18 are necessary.
The following enhancements for LPHAP are recommended for normative work: [text omitted]
From RAN2’s perspective, LPHAP is recommended for normative work
7.8 Positioning of UEs with Reduced Capabilities
From RAN1’s perspective, for positioning of RedCap UEs, support of PRS frequency hopping and SRS frequency hopping are recommended for normative work.
During the normative work, the complexity of the corresponding capabilities for RedCap UEs should be addressed for the introduction of appropriate capabilities for RedCap UEs.

## Slide 9: WID Scope proposal
During several meetings RAN1 companies analyzed and debated multiple options and proposals and then reached consensus for the TR recommendations based on the agreement's texts.
As a starting point of WID discussion, we would like to see all the recommendations being treated equally as they reflect the RAN1 group preference.
Proposal 3: Rel-18 Expanded and Improved Positioning WI should support RAN1 recommendations first

## Slide 10: Discussion
SL positioning for FR1 (7.3, recommended)
  Strong support from RAN1 for normative work
  Multiple evaluations for various use cases and scenarios showed feasibility of the accuracy requirements in FR1
LPHAP (7.7, recommended)
  LPHAP study demonstrated that the battery life (6-12 months) requirements may be fulfilled with relatively low specs changes (such as SRS enhancements, DRX enhancements and paging skipping)
  LPHAP has a strong support for normative work from RAN1 and RAN2
RedCap (7.8, recommended)
  Supported by RAN1 for normative work
  Requires relatively little spec changes (such as support of SRS hopping)
PRS/SRS Bandwidth Aggregation (7.5)
  The PRS/SRS Bandwidth Aggregation study concluded feasibility for single-chain Tx/Rx architectures at both the UE and gNB and the bandwidth aggregation for intra-band contiguous carriers
Integrity for RAT-Dependent Positioning Techniques (7.4, recommended)
  Supported by RAN1 for normative work
  It may require substantial work compared with other topics given the large number of potential error sources that were considered in the study phase
CPP (7.6)
  Carrier Phase Positioning (CPP) evaluations show centimeter accuracy only in 50% and in very restrictive conditions of LOS between PRU(s) and TRP(s), ideal conditions including very precise known PRUs/TRPs locations.
  The CPP evaluations imply very limited applicability/benefits of CPP in real world scenarios and high sensitivity to errors

## Slide 11: WI Scoping Proposals
Based on the above observations we propose for R18 Expanded and improved positioning WI scope:
Proposal 4: Prioritize FR1 SL positioning with SL-PRS bandwidth of up to 100 MHz based solutions
Proposal 5: Prioritize Low Power High Accuracy Positioning
Proposal 6: Support RedCap positioning
Proposal 7: Support Integrity techniques (discuss further how to manage the workload on error sources)
Proposal 8: Consider PRS/SRS Bandwidth Aggregation
Proposal 9: Discuss further the support of NR Carrier Phase Positioning