## Slide 1: [98e-11-Ambient-IoT] Extended round summary and GTW proposal
3GPP TSG RAN Meeting #98e
Electronic Meeting, December 12-16, 2022
Document for: Discussion and Decision
Agenda Item: 9.2.3
Source: Moderator (Huawei)
RP-223451

## Slide 2
Proposals for endorsement after the Extended Round
For agreement:
Proposal 4-3b-v2, in section 5.3.6 (Co-deployment)
Proposal 5-1a-extended, in section 6.1.6 (Energy harvesting text)
Proposal 5-3b-v2, in section 6.2.6 (Device categorization)
For working assumption:
Proposal 5-2a-extended for working assumption, in section 6.2.6 (Energy storage)
For approval:
Approve SID revision RP-223396, in section 8 (no comments received)
SR to be handled on slide 5

## Slide 3
Topic 4-4: Connectivity topology
Connectivity topology is one characteristic of a deployment scenario
Proposal 4-4 at start of Extended Round –
  Define the following topologies as starting points for the next meeting:
    Topology (1): BS <-> Ambient IoT device
      NOTE 1: Includes the possibility of BS Rx and BS Tx in different BSs
    Topology (2): BS <-> intermediate node <-> Ambient IoT device
      NOTE 1: Intermediate node can be relay, IAB, UE, repeater, etc. which is capable of ambient IoT
    Topology (3): BS <-> assisting UE <-> Ambient IoT device <-> BS
      FFS: If the two BS can be different
    Topology (4): UE <-> Ambient IoT device
    FFS: Topology (5) UE <-> Ambient IoT device <-> {BS or UE}
    NOTE: For potential topology (5), discuss its relation with other topologies, its necessity, etc. in RAN#99.
    NOTE: For all topologies: The Ambient IoT device may be provided with carrier wave from another node(s) either inside or outside the topology
    NOTE: For all topologies: The links in each topology may be bidirectional or unidirectional
    FFS: Whether to consider combination of different topologies in the study.
    FFS: BS, UE, or assisting UE could be multiple BSs, UEs or assisting UEs, respectively.
Comment to address from Ericsson:
  “We would like to make the possibility for an Ambient IoT device to communicate via intermediate assistance NW node in one direction but directly with BS in the other direction more explicit. This case can be covered, e.g., by generalizing “assisting UE” to “assistance node” in Topology (3) and adding a similar note for Topology (3) as for Topology (2).
  “Furthermore, we agree with MediaTek and ZTE that it would be good to indicate the end points for the communications, e.g., by underlining the end points.”

## Slide 4
Topic 4-4: Connectivity topology
Moderator reply:
Since by now it should be clear that topologies (2) and (3) are distinguished at least by respectively in (2) not having, or in (3) having direct link between the BS and device, it might be OK to make Ericsson’s change for assisting UE to assisting node, which is also liked by ZTE.
On underlining endpoints, this is more complicated because e.g. topology 3 is triangular (or polygonal), and end points are of questionable meaning before possible down-select within topology 3. Further, we have the FFS on combinations, which might be contradicted if we define an ‘end’point now. The suggestion would be to raise this as a further detail in the next meeting.
On the other hand, nearly all other companies are OK to take these further points under the FFSs and NOTEs in the next meeting to delve into more details.
Moderator suggests this updated proposal for a try on GTW, and otherwise ask to rely on next meeting’s discussion to handle the comment.
Proposal 4-4v2: Define the following topologies as starting points for the next meeting:
  Topology (1): BS <-> Ambient IoT device
    NOTE 1: Includes the possibility of BS Rx and BS Tx in different BSs
  Topology (2): BS <-> Intermediate node <-> Ambient IoT device
    NOTE 1: Intermediate node can be relay, IAB, UE, repeater, etc. which is capable of ambient IoT
  Topology (3): BS <-> assisting nodeUE <-> Ambient IoT device <-> BS
    NOTE 1: Assisting node can be relay, IAB, UE, repeater, etc. which is capable of ambient IoT
    FFS: If the two BS can be different
  Topology (4): UE <-> Ambient IoT device
  FFS: Topology (5) UE <-> Ambient IoT device <-> {BS or UE}
  NOTE: For potential topology (5), discuss its relation with other topologies, its necessity, etc. in RAN#99.
  NOTE: For all topologies: The Ambient IoT device may be provided with carrier wave from another node(s) either inside or outside the topology
  NOTE: For all topologies: The links in each topology may be bidirectional or unidirectional
  FFS: Whether to consider combination of different topologies in the study.
  FFS: BS, UE, or assisting nodeUE could be multiple BSs, UEs or assisting nodesUEs, respectively.

## Slide 5
Status Report and List of Agreements
No comments were received to the SR in RP-223395, so it can be noted.

## Slide 6
Endorsements at end of final round (declared by Chair)
Proposal 1-v2, in section 2.6. (Agree TR skeleton)
  TR skeleton is available in inbox in RP-223526
Proposal 2, in section 3.6 (Handling of SA1 use cases)
Conclusion 3-2 and Proposal 3-1 in section 4.6 (Deployment scenarios table)
In Section 4 (Deployment scenario characteristics)
  Proposal 4-1v2, in section 5.1.6 (Environment)
  Proposal 4-2 in section 5.2.5 (Basestation characteristic)
  Proposal 4-3a in section 5.3.5 (on in-band, guard-band, standalone band)
  Proposal 4-5, in section 5.5.5 (Spectrum)
  Conclusion 4-6 in section 5.6.5 (Traffic assumption)

## Slide 8
Topic 4-4 annex: Connectivity topology
Just for information, these figures are generalized ways to show Topology 2 and Topology 3.
Please do not be worried. They are not for agreement today.
Topology (2)
Topology (3)