## Slide 1: Moderator’s summary for discussion [98e-15-R18-Multicarrier]
Moderator (NTT DOCOMO, INC.)
3GPP TSG-RAN Meeting #98-e
Electronic Meeting, December 12-16, 2022
Agenda Item: 9.3.1.2
RP-223455

## Slide 2: Conclusion on additional RAN1 TU for Q1 2023
It is confirmed by RAN/RAN1 chairs that additional 1 TU is allocated to Rel-18 MC enh WI for RAN1 in Q1 2023 (RAN1#112 meeting) by using one of RAN1 reserved TUs.

## Slide 3: Background of the discussion for GTW
At the last RAN1 meeting, the issue on UL/SUL indicator in DCI format 0_X was extensively discussed.
  RAN1 agreed to support UL/SUL indicator field in DCI format 0_X, but no consensus was achieved between Alt.1(0~1 bit, i.e., for single cell configured with SUL) and Alt.2(0~4 bits, i.e., for each cell configured with SUL).
In RP-222921, it is proposed to discuss and conclude the issue on UL/SUL indicator in DCI format 0_X at this RAN plenary.
  During initial round discussion, 12 companies agreed to discuss and conclude the issue at this plenary while 4 companies suggested to discuss the issue in WG meeting.
The issue has been discussed in intermediate and final rounds of [98e-15-R18-Multicarrier], but the situation has not been changed from the last RAN1 meeting.
  RAN1 chair and WI rapporteur expressed concern on the risk of repeating the same discussion again in RAN1 if RAN cannot conclude this issue, and they argued that RAN1 should be able to focus on other remaining issues to complete this WI in Q1 2023.

## Slide 4: Proposal for GTW
Down select one of following alternatives to conclude this issue
Alt.1: UL/SUL indicator in a DCI format 0_X for multi-cell PUSCH scheduling is 1 bit (when it is present), which is for one serving cell within the set of co-scheduled cells (i.e., Type 1C).
Alt.2: UL/SUL indicator in a DCI format 0_X for multi-cell PUSCH scheduling is sum of {0, 1} bits for each cell in the set configured for the DCI format 0_X (i.e., Type 2)
    The number of bit (i.e., 0 or 1) for a cell in the set is determined according to the existing mechanism defined in TS 38.212 for UL/SUL indicator field.
[Alt.3: UL/SUL indicator field is excluded from a DCI format 0_X. (only if RAN cannot converge on either Alt.1 or Alt.2)]

## Slide 5: Appendix
  Initial round feedback summary
  RAN guidance/discussion is necessary/helpful: Nokia, ZTE, Qualcomm, CATT, NTT DOCOMO, Xiaomi, Intel, LG, MediaTek, vivo, Lenovo, Ericsson (12)
  RAN guidance/discussion is not necessary: Huawei, China Telecom, CMCC, China Unicom (4)
  Intermediate round feedback summary
  Alt. 1 (0~1 bit, type 1C) Support: Nokia, Qualcomm, Spreadtrum, Intel, Ericsson, Vodafone (6) ,
    Objection: Samsung, Huawei (2)
  Alt. 1’ (0~1 bit, type 1A) Support: Samsung (1)
  Alt. 2 (0~4 bits, Type 2) Support: New H3C, Huawei, Spreadtrum, vivo, CATT, China Telecom, Xiaomi, China Unicom, CMCC (9)
    Objection: Samsung, Qualcomm (2)
  Alt.3 (omit) Support: Nokia, Samsung, Qualcomm, NTT DOCOMO, Ericsson (5)
    Objection: Huawei, vivo, CATT, Xiaomi, CMCC, Vodafone (6)
  Final round feedback summary
  Support Alt.2: CMCC, China Telecom, New H3C, vivo, China Unicom, Huawei, CATT, Xiaomi, Spreadtrum (9)
  Objection to Alt.2: Qualcomm, Nokia, Ericsson, LG, Samsung (5)
  Suggest to exclude this field from DCI format 0_X if consensus cannot be reached (Alt.3): RAN1 chair, Nokia, Ericsson, LG, NTT DOCOMO