## Slide 1: Moderator's summary for discussion [98e-13-R18-AIML-Air]
Source: Moderator(RAN1 VC, CMCC)
RP-223507
3GPP TSG RAN#98-e
12th – 16th, December 2022
Agenda Item: 9.2.8

## Slide 2: Outline
Issue 1 – For the representative sub use cases
  Some company propose to confirm RAN1 agreed Representative sub use cases in this meeting, and one company proposes to remove some RAN1 agreed representative sub use case
  Company proposal “For BM-Case1 and BM-Case2, beams in Set A and Set B should be in the same Frequency Range”
Issue 2 – For work arrangement in RAN1 and RAN2
  Is there need to discuss and provide further RAN guidance on the focus of RAN1 and RAN2 for AI/ML for air interface? If your answer is yes, how to avoid deadlock between RAN1 and RAN2 due to “who should first discuss these ”?

## Slide 3
Issue 1 – For the representative sub use cases
Proposal 1: Confirm the following representative sub use cases according to RAN1 agreements for the initial set of use case as below
  CSI feedback enhancement
    Spatial-frequency domain CSI compression using two-sided AI model
    Time domain CSI prediction using UE sided model
  Beam management
    Spatial-domain DL beam prediction for Set A of beams based on measurement results of Set B of beams
    Temporal DL beam prediction for Set A of beams based on the historic measurement results of Set B of beams
  Positioning accuracy enhancements for different scenarios
    direct AI/ML positioning
    AI/ML assisted positioning
Question 1: Is there any strong concern on proposal “For BM-Case1 and BM-Case2, beams in Set A and Set B should be in the same Frequency Range”

## Slide 4: Status of Issue 1
To proposal 1, 27 of 33 companies are fine to endorse proposal 2.1-1, and the other 6 think it is out of RAN’s discussion. Indeed, all the presentative sub use cases are agreed in RAN1, and there is no check point set for RAN checking, but some companies show concern on related RAN1 agreements, in this sense, moderator thinks it not bad to endorse this proposal in this meeting.
To question 1, vast majority of companies believe it should be discussed in RAN1, let’s leave it to RAN1, and end the discussion on it in this meeting.

## Slide 5
Issue 2 – For work arrangement in RAN1 and RAN2
Question 2: Is there need to discuss and provide further RAN guidance on the focus of RAN1 and RAN2 focus for AI/ML for air interface? If your answer is yes, how to avoid deadlock between RAN1 and RAN2 due to “who should first discuss these ”?
Proposal 2: Leave the work arrangement about what to be discussed or what to be prioritized to WGs.
Status and Observations:
  All companies agree to leave the work arrangement about what to be discussed or what to be prioritized to WGs
  But worthwhile to note RAN2 chair’s comment “AI/ML is a new topic, this is just a SI and for Sis WG usually extend into other groups’ areas, so responsibility confusion is expected. RAN2 will attempt to make progress. There will likely be some overlap with RAN1. Hopefully no conflict, especially with the reason that “RAN1 is working on this”……”, from moderator’s observation, RAN1 faces the same issues, hopefully, it should be a common understanding that “Some WG is working on this” should not be frequently used for blocking some of the discussion in this uncultivated territory.

## Slide 6: Wrap up
Proposal 1: Confirm the representative sub use cases according to RAN1
Proposal 2: No RAN guidance on the issue of “For BM-Case1 and BM-Case2, beams in Set A and Set B should be in the same Frequency Range” to RAN1
Proposal 3: Leave the work arrangement about what to be discussed or what to be prioritized to WGs.