## Slide 1: Moderator's summary for discussion [98e-19-R18-eRedCap]
Source: Moderator(RAN1 VC, CMCC)
RP-223539
3GPP TSG RAN#98-e
12th – 16th, December 2022
Agenda Item: 9.3.1.7

## Slide 2: Outline 1 – Pending issues in WID
Issue 1. UE peak rate reduction as a standalone feature:
  Yes: Apple, CMCC, Intel, Sierra, Qualcomm
  No: Futurewei, Huawei, Nokia, Nordic, Spreadtrum, Xiaomi, ZTE
  No for Rel-18 but maybe for Rel-17: CATT
  UE BB bandwidth reduction and UE peak rate reduction not independent features: Ericsson
  Also open to removing the UE peak rate reduction objective: Futurewei
Issue 2. Additional separate early indication:
  Yes, already in Msg1: Apple, DCM
  Yes, both Msg1 and Msg3: Futurewei, Huawei, Qualcomm
  Yes, at least Msg3, maybe also Msg1: Ericsson, Nokia, Nordic
  Yes, Msg3 but not Msg1: CATT, Intel, MediaTek
  Yes, Msg1 and/or Msg3: Xiaomi, ZTE
  Maybe Msg3 but not Msg1: CMCC, Vivo
  Decide in WG: Ericsson, Sierra
Issue 3. Other restrictions of the WI (e.g., connectivity restrictions, band, etc.):
  At least restrictions of no CA and DC: DCM
  Inheriting Rel-17 restrictions: Nordic, Xiaomi

## Slide 3: Outline 2 – Other proposals for updating WID
Issue 4. Minimum target (downlink) peak data rate:
  6 Mbps: DCM, Nordic, Spreadtrum
  6-10 Mbps: Ericsson, ZTE
  10 Mbps: CATT, Nokia
Issue 5. Miscellaneous
  M-1: Specify an SI indication to indicate whether a UE can camp on the cell/frequency or not: Sierra
  M-2: UE complexity (peak rate) reduction in FR2: Ericsson, Spreadtrum, opposed by Futurewei
  M-3: Support NCD-SSB for RedCap UEs in idle/inactive state: Vivo
  M-4: Make UE capability filtering by the UE optional: Qualcomm
  M-5: Specify support for lower UE power class: Vivo
  M-6: An additional separate initial BWP is not needed: Ericsson (can be decided in WG)
  M-7: Clarification on the objective for UE BB bandwidth reduction: CATT
  M-8: RAN paging only for Enhanced eDRX: xiaomi

## Slide 4: Status after the intermediate round - 1
For Issue 1. UE peak rate reduction as a standalone feature:
Proposal
PR1 is supported as an add-on for both Rel-17 Redcap capable UE and Rel-18 eRedcap capable UE
  R17 RedCap + R18 PR1 should be of the single R17 UE type
    No early identification for differentiating between UE supporting R17 Redcap and UE supporting R17 Redcap + R18 PR1
  R18 + BW3/PR3 + R18 PR1 should be of the single R18 UE type
    No early identification for differentiating between UE supporting R18 + BW3/PR3 and UE supporting R18 + BW3/PR3 + R18 PR1
Yes: CATT, Sierra, Qualcomm, Apple, NTT DOCOMO, New H3C, vivo, Meta, Intel, CMCC (10)
NO: Huawei, Nodic, Futurewei, MTK, Spreadtrum, Lenovo, LGE, Ericsson, ZTE, Vodafone, Sony, Sequans, China Telecom (13)
Not strong: Samsung, Panasonic
Observations:
Compared to the last round’s proposal and discussion, this proposal has resolved the concern on more UE types, however, opponent companies comment that 3GPP should define dual approaches to meet the same target peak data rate, so some companies would drop R18 PR1 than support standalone R18 PR1
Some companies have misunderstood the proposal which does not impose anything on R17 specification
Some companies propose to downselect between BW3/PR3 and standalone PR1 or only add-on

## Slide 5: Status after the intermediate round - 2
For Issue 2. Additional separate early indication:
Proposal
Update the WID by adding objective: Support additional separate early indication(s) (RAN1, RAN2)
How to support is decided by WGs
Observation: seems agreeable to all
Issue 3. Other restrictions of the WI (e.g., connectivity restrictions, band, etc.):
Proposal
For restriction of the WI (e.g., connectivity restriction, band, etc), keep the objective as it is, i.e., inheriting Rel-17 restrictions on Redcap
Observation:
seems agreeable to all but one company，who wants to add one more note This WI focuses on SA mode and single connectivity with operation in a single band at a time.”

## Slide 6: Status after the intermediate round - 3
Issue 4. Minimum target (downlink) peak data rate:
Observations from initial round
10Mbps: CATT, vivo, Huawei, Futurewei, Sierra, Meta, Samsung, Apple, Lenovo, MTK, LGE, NEC, Panasonic, Sony, Sequans (15)
6Mbps: Spreadtrum, vivo, Nodic, NTT DOCOMO, ZTE, New H3C, Intel (7)
Fine to either of the two values, and other single value: Ericsson, Qualcomm, OPPO, Vodafone, Nokia (5)
Proposal
Keep the minimum target peak rate as 10Mbps.
Issue 5. Miscellaneous
Observations from initial round
For from M-1 to M-5, 12 of 22 companies comment in favor of without exception to the Chair's guidance in this meeting "Considering the overall situation and the need for Rel-18 timeline discussion, there is no plan to discuss or approve new project proposals or up-scoping proposals, unless previously arranged."
Close the discussion on from M-1 to M-8 in this RAN meeting in this meeting.
Proponent companies of from M-1 to M-5 can bring them up in next meeting.

## Slide 7: Status after the final round – For Issue 1
Proposal for Issue 1 - UE peak rate reduction as a standalone feature
Proposal
Downselect one from the below options in this meeting
Option 1: PR1 is supported as an add-on for both Rel-17 Redcap capable UE and Rel-18 eRedcap capable UE
    R17 RedCap + R18 PR1 should be of the single R17 UE type
      No early identification for differentiating between UE supporting R17 Redcap and UE supporting R17 Redcap + R18 PR1
    R18 + BW3/PR3 + R18 PR1 should be of the single R18 UE type
      No early identification for differentiating between UE supporting R18 + BW3/PR3 and UE supporting R18 + BW3/PR3 + R18 PR1
Option 2: Support PR1 only with UE BB bandwidth reduction
Option 3: No PR1
Option 4: Support standalone PR1 only, aborting BW3/PR3 (overturn existing agreements)
Option 5: Others (Anything missing and different from above 4 options)

## Slide 8: Status after the final round – For Issue 1
Option 1:
Acceptable: Sierra, CATT, Qualcomm, NTT DOCOMO, vivo, Apple, Panasonic, CMCC, Intel, Ericsson
Object/No: MTK, T-Mobile, Spreadtrum, LGE, Nodic, T-Mobile, ZTE, Sequans
Option 2:
Acceptable: MTK, Futurewei, CATT, Huawei, NTT DOCOMO, vivo, Spreadtrum, Lenovo, Panasonic, Nokia, New H3C, LGE, Nodic, Vodafone, Samsung, ZTE, Sequans, Ericsson, Sony
Object/No: Sierra, T-Mobile, Qualcomm, Apple
Option 3:
Acceptable: MTK, Futurewei, Sierra, CATT, Huawei, vivo, Spreadtrum, Lenovo, Apple, Panasonic, Nokia, LGE, Nodic, Vodafone, Samsung, ZTE, Ericsson, Sony
Object/No: T-Mobile, Qualcomm, NTT DOCOMO, CMCC, T-Mobile, Sequans,
Option 4:
Acceptable: Sierra, CATT, Qualcomm, Spreadtrum, Vodafone, Ericsson
Object/No: MTK, T-Mobile, NTT DOCOMO, vivo, Panasonic, CMCC, Nokia, Nodic, T-Mobile, ZTE, Intel, Sequans
Observations:
At least Option 4 should be avoided. Option 3 seems contradictary with the claim from companies that IoT device is sensitive, we should keep rational to it. Between Option 1 and Option 2, moderator would like to make the last try in this meeting with proposal 5.1-1, otherwise, it looks that we will have to figure out smarter solution till next RAN meeting.

## Slide 9: Status after the final round – For Issue 2
For Issue 2. Additional separate early indication:
Proposal
Downselect one from the below options in this meeting
Option 1:
  Update the WID by adding objective: Support an additional separate early indication (RAN1, RAN2)
  How to support is decided by WGs
Option 2:
  Update the WID by adding objective: If needed, support an additional separate early indication (RAN1, RAN2)
  How to support is decided by WGs
Observations
Option 1: Futurewei, Sierra, CATT, Huawei, Qualcomm, NTT DOCOMO, vivo, Spreadtrum, Lenovo, Apple, CMCC, Nokia, MTK, LGE, Nodic, Vodafone, ZTE, DT, Intel, Ericsson
Option 2: Futurewei, Sierra, CATT, Qualcomm, vivo, Spreadtrum, Apple, CMCC, NEC, Nokia, MTK, Samsung, Nodic
Neither: T-Mobile, Ericsson
The proposal in the intermediate round, i.e., option 1, is not simply based on counting supporters, in fact it is trying to avoid a back-and-forth discussion between WGs and TSG, since this proposal is not put on the table for the first time and it is not expected that here the majority of companies will change their minds in one quarter. It can be imagined that it will be brought back to RAN if still minority of companies claim that it is not necessary in WGs, unless these companies will change their minds in next quarter even they will not right now.

## Slide 10: Status after the extended round – For Issue 1
Proposal for Issue 1 - UE peak rate reduction as a standalone feature
Proposal
PR1 is supported as an add-on for both Rel-17 Redcap capable UE and Rel-18 eRedcap capable UE
  R17 RedCap + R18 PR1 should be of the single R17 UE type
    No early identification for differentiating between UE supporting R17 Redcap and UE supporting R17 Redcap + R18 PR1
  R18 + BW3/PR3 + R18 PR1 should be of the single R18 UE type
    No early identification for differentiating between UE supporting R18 + BW3/PR3 and UE supporting R18 + BW3/PR3 + R18 PR1
Define value of X and Y in RAN1 to support R17 UE type and R18 UE type with different minimum peak rate to differentiate distinct target.
Agreement (RAN1#111)
UE peak data rate reduction is supported at least as an add-on to UE BB bandwidth reduction,
  The constraint vLayers·Qm·f ≥ 4 is relaxed to vLayers·Qm·f ≥ X.
  FFS: the value of X
If UE peak data rate reduction is supported as a standalone feature,
  The constraint vLayers·Qm·f ≥ 4 is relaxed to vLayers·Qm·f ≥ Y.
  FFS: the value of Y
  Note: Whether this option is supported will be decided in RAN plenary.

## Slide 11: Status after the extended round – For Issue 1
Observations:
Almost an open discussion, more views are presented though quite a few companies persist respective preference. But it is good to see some companies think it will create more fragments in the market, while some companies think it a compromise, then some companies change their positions a bit (two-way flow). In this sense, moderator would like to propose to leave more time to companies to look into it.
Proposal
Taking Proposal 5.1-1 as a framework, RAN tasks RAN1 to investigate the impact of R18 standalone PR1 on UE types, capabilities, and implementations, as well as R17 specifications, etc., and to report it in RAN#99
  Other options will be discussed together in RAN#99

## Slide 12: Wrap up - 1
Proposal for Issue – 1 UE peak rate reduction as a standalone feature
Taking Proposal 5.1-1 as a framework, RAN tasks RAN1 to investigate the impact of R18 standalone PR1 on UE types, capabilities, and implementations, as well as R17 specifications, etc., and to report it in RAN#99
  Other options will be discussed together in RAN#99
Proposal for Issue – 2 Additional separate early indication
Downselect one from the below options in this meeting
Option 1:
  Update the WID by adding objective: Support an additional separate early indication (RAN1, RAN2)
  How to support is decided by WGs
Option 2:
  Update the WID by adding objective: If needed, support an additional separate early indication (RAN1, RAN2)
  How to support is decided by WGs
  Check in RAN#99 RAN#98-e regarding (Pending issues), partially resolved, WID update
Whether UE peak data rate reduction for UE is limited only with UE BB bandwidth reduction or standalone
Whether or not/how a separate early indication can be supported
Other restrictions of the WI (e.g., connectivity restrictions, band, etc.)

## Slide 13: Wrap Up - 2
Issue 5. Miscellaneous
  M-1: Specify an SI indication to indicate whether a UE can camp on the cell/frequency or not: Sierra
  M-2: UE complexity (peak rate) reduction in FR2: Ericsson, Spreadtrum, opposed by Futurewei
  M-3: Support NCD-SSB for RedCap UEs in idle/inactive state: Vivo
  M-4: Make UE capability filtering by the UE optional: Qualcomm
  M-5: Specify support for lower UE power class: Vivo
  M-6: An additional separate initial BWP is not needed: Ericsson (can be decided in WG)
  M-7: Clarification on the objective for UE BB bandwidth reduction: CATT
  M-8: RAN paging only for Enhanced eDRX: xiaomi

## Slide 14: Agreements and Conclusion after Friday’s GTW
For Issue – 1 UE peak rate reduction as a standalone feature
Conclusion
  Revisit in RAN#99 (no additional discussion in RAN1 in 1Q’23)
For Issue – 2 Additional separate early indication
Agreement
Update the WID by adding objective:
  Support additional separate early indication(s) (RAN1, RAN2)
  How to support is decided by WGs