## Slide 1
3GPP TSG RAN Meeting #99 RP-230370
Rotterdam, Netherlands, March 20-23, 2023
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.2.8
Discussion on Rel-18 XR WI scope

## Slide 2
  Background
  WID objectives update on
    XR awareness
    Capacity enhancement
    Coordination with SA2
Contents

## Slide 3
Background
SI progress in RAN2
In RAN#98-e meeting, a WID on Rel-18 XR was approved in RP-223502, with the below minutes:
In 2023Q1, RAN2 had some discussion on XR awareness and made some progress. Besides, the SI progress in RAN2 is:
It could be observed that the Rel-18 SI on XR could be considered as completed. In this contribution, we will discuss the potential WID scope update according to the progress in RAN2.
SI status (Rel-18 XR) RAN2 considers the Rel-18 XR SI complete
Keep the SI open, only for XR awareness, until March. The sole remaining goal of the SI is to refine the WI objective on XR awareness. No need to update the SID, the open items on XR awareness are well understood (as also shown in the several different FFS Editor’s Notes in the TR) Update the WID in March: for XR Awareness, as needed. Impacts to RAN3 will be assessed in March Clarify in the RAN#98e meeting minutes that “The delay of the start of the normative work on XR awareness is not foreseen to have an impact on the Release 18 completion schedule”

## Slide 4
XR awareness
RAN2 progress and conclusions
Regarding the XR awareness, RAN2 made the below conclusions in the TR 38.835 v2.0:
It could be observed that following objectives on XR awareness could be considered during WI phase:
  Provisioning by CN of semi-static information per QoS flow (e.g. PDU set QoS parameters), dynamic information per PDU set (PDU Set information and Identification) and End of Data Burst indication(as per TR 23.700-60) [RAN3, RAN2];
  Specify the support of identifying of PDU sets, Data bursts and PSI at UE [RAN2];
  Specify XR traffic assistance information e.g. periodicity, UL traffic arrival information [RAN2, RAN3];
  Specify signaling for XR awareness to support XR power saving and XR capacity enhancement [RAN2, RAN3].
Provisioning by CN of semi-static information per QoS flow (e.g. PDU set QoS parameters), dynamic information per PDU set (PDU Set information and Identification) and End of Data Burst indication(as per TR 23.700-60 [9]); Identifying by UE of PDU Sets, Data bursts and PSI; Provisioning by UE of XR traffic assistance information e.g. periodicity, UL traffic arrival information (FFS).

## Slide 5
XR awareness
PDU discard
Regarding PDU discard, RAN2 had the below agreements in RAN2#121:
It is better to update the objective on PDU set discard to be more specific:
  Discard operation of PDU Sets based on the PDB/PSDB, PSIHI, PDU set importance [RAN2].
RAN2 thinks PSI can be useful for PDU set-based discard. RAN2 aims to introduce a mechanism to allow UE to handle discarding of packets with different PSI in case of congestion. FFS for other cases. Introduce UL PDU Set Importance. How UE derives this will be handled in UE implementation.

## Slide 6
Capacity enhancements
BSR triggering
In RAN2#120 meeting, there was an agreements on the triggering of BSR:
It is better to update the objective on capacity enhancements to include this part:
  Specify additional BSR triggering conditions to allow timely availability of buffer status information at gNB [RAN2]
RAN2 needs to discuss additional BSR triggering conditions to allow timely availability of buffer status information at gNB. This can be discussed in WI phase.

## Slide 7
In RAN2#120 and RAN3#118 meeting, network exposure of per QoS flow/per DRB congestion information in both DL and UL has been discussed. Both RAN2 and RAN3 confirm that:
  It is feasible for RAN to estimate the congestion information per-QoS flow and per-DRB in downlink and uplink directions.
  It is feasible for RAN to estimate the congestion information per-QoS flow and per-DRB in uplink without UE impacts.
In our understanding, the discussion on network exposure in SA2 would need some inputs from RAN side.
Thus, RAN2 and/or RAN3 should discuss/specify corresponding signaling (e.g. via NG or X2 interface), subject to SA2 progress and requirement e.g. per-QoS flow/per-DRB congestion information.
Coordination with SA2 aspects:

## Slide 8
Conclusions
WID update for Rel-18 XR
Specify the enhancements related to power saving:
DRX support of XR frame rates corresponding to non-integer periodicities (through at least semi-static mechanisms e.g. RRC signalling) (RAN2).
Specify the enhancements related to capacity:
Multiple CG PUSCH transmission occasions in a period of a single CG PUSCH configuration (RAN1, RAN2);
Dynamic indication of unused CG PUSCH occasion(s) based on UCI by the UE (RAN1, RAN2);
BSR enhancements including at least new BS Table(s); (RAN2);
Delay reporting of buffered data in uplink; (RAN2);
Provision of XR traffic assistance information for DL and UL (e.g. periodicity); (RAN2);
Discard operation of PDU Sets based on the PDB/PSDB, PSIHI, PDU set importance (RAN2);
Specify additional BSR triggering conditions to allow timely availability of buffer status information at gNB [RAN2]
Specify the enhancements for XR Awareness (RAN2, RAN3): TBD (detailed objectives will be further clarified at RAN#99 based on the conclusions of TR38.835, and work to be started only after RAN#99)
Provisioning by CN of semi-static information per QoS flow (e.g. PDU set QoS parameters), dynamic information per PDU set (PDU Set information and Identification) and End of Data Burst indication(as per TR 23.700-60) [RAN3, RAN2];
Specify the support of identifying of PDU sets, Data bursts and PSI at UE [RAN2];
Specify XR traffic assistance information for DL and UL e.g. periodicity, UL traffic arrival information [RAN2, RAN3];
Specify signaling for XR awareness to support XR power saving and XR capacity enhancement [RAN2, RAN3].
Coordination with SA2:
Specify corresponding signaling (e.g. via NG or X2 interface), subject to SA2 progress and requirement e.g. per-QoS flow/per-DRB congestion information. [RAN3, RAN2, including coordination and alignment SA2 as required].
Notes: Importance………based scheduling…