## Slide 1: Discussion on a new RAN WI for NPN enhancements
3GPP TSG RAN Meeting #99 RP-230655
March 20th – 23th, 2023
Agenda Item: 9.1.3
Source: Intel Corporation
Document for: Discussion

## Slide 2: Background
SA2 WID [SP-221340] approved at SA#98e – SA2 is currently working on the normative phase of the enhanced Non-Public Network Phase 2 (eNPN_Ph2) in Rel-18.
Among 6 identified key issues, KI#1 and KI#2 have RAN impacts, and SA2 sent LS to R2/R3 [S2-2301437]:
R3#119 discussed together with other SA2 items (eNS_Ph3, TRS_URLLC) and asked for RAN guidance on how to carry out normative RAN works for these SA2 work items in Rel-18 [RP-230037/R3-230954]
According to RAN plenary guidelines on TEI handling [RP-222624] this works requires a RAN WID:
Support for enhanced mobility by enabling support for idle and connected mode mobility between SNPNs without new network selection
Support for non-3GPP access for SNPN.
NG-RAN impacts identified are impacts to NGAP to support equivalent SNPNs, and impacts on cell (re-)selection for objective 1, and NGAP impacts to support selected SNPN (NID) for objective 2.

## Slide 3: eNPN_Ph2 impacts on RAN2 and RAN3
According to SA2 LS to RAN2 and RAN3 [S2-2301437]:
RAN2 impacts are foreseen:
  Only for objective 1, on cell (re-)selection in supporting equivalent SNPNs
  From R2#121 discussions, impacts foreseen on Stage-2 TS 38.300 and Stage-3 TS 38.304 & 38.331 to extend the equivalent PLMN principle to also SNPN for cell reselection and SNPN selection.
RAN3 impacts are foreseen:
  For both objective 1 and 2, to support equivalent SNPNs and selected NID for non-3GPP access
  From R3#119 discussions, stage-3 impacts foreseen on NG/XnAP, e.g. in Mobility Restriction List; including target selected NID for connected/inactive mobility proc. over NG/Xn; and including selected NID in NG Initial UE Message.
Support for enhanced mobility by enabling support for idle and connected mode mobility between SNPNs without new network selection
Support for non-3GPP access for SNPN.
NG-RAN impacts identified are impacts to NGAP to support equivalent SNPNs, and impacts on cell (re-)selection for objective 1, and NGAP impacts to support selected SNPN (NID) for objective 2.

## Slide 4: Rel-18 RAN WI scope for eNPN_Ph2
Considering R3#119/R2#121 discussions, the following objectives are proposed:
RAN3-led WID (RAN2 is secondary)
Impacted Specs: TS 38.300, TS 38.413, TS 38.423, TS 38.304, TS 38.331
No further objectives are deemed necessary to be added to the scope other than as identified by SA2
Expected that 0.5 TU for one or two meeting cycle looks enough to finish the normative works in RAN2/3
Specify the cell (re-)selection for SNPN capable UE to support equivalent SNPNs, following the principles used for equivalent PLMNs [RAN2].
Specify the connected mobility between SNPNs without new network selection [RAN3].
Specify the support for non-3GPP access for SNPN [RAN3].
RAN to discuss the Rel-18 RAN WI work scope and TU for SA2’s eNPN_Ph2,
based on the above assessments.