## Slide 1
3GPP TSG RAN WG1 #109-e R1-2203886
e-Meeting, May 9th – 20th, 2022
Agenda item : 9.1
Source : Samsung
Title : Work plan for Rel-18 Evolved MIMO
Document for : Discussion and Decision

## Slide 2: Workload assessment
AI | Short description | WID objective(s) | Assessment
9.1.1.1 | mTRP enhancements: beam management: Rel-17 TCI extension for multiple beam indication for DL and UL TCI states (mTRP focus), including UL beam indication for STx2P UL PC for sDCI with Rel-17 TCI | 2, 6 beam indication, 7 power control | Medium
9.1.1.2 | mTRP enhancements: Two TAs for mDCI mTRP | 7 two-TA | Small
9.1.2 | CSI: Medium/high-speed: TD channel property reporting, Type-II CB refinement Type-II CB refinement for CJT | 1, 4 Type-II | Medium
9.1.3.1 | DMRS: CP-OFDM DL/UL DMRS 24 orthogonal ports UL DMRS for 4 and more layers | 3, 5 DMRS | Medium
9.1.3.2 | SRS: SRS interference management for TDD CJT SRS for 8Tx | 4 SRS, 5 SRS | Medium
9.1.4.1 | STxMP PUSCH transmission: Precoding indication (SRI and TPMI) for STx2P transmission assuming 2 TRPs, up to 4 layers across 2 panels | 6 precoding indication | Medium
9.1.4.2 | UL 8Tx SRI and TPMI (including codebook): 4 and more layers with 8Tx, and 4 advanced UE types (CPE, FWA, IIoT, Veh) (Codebook: coherence types, full TX power assumptions, different UE types) | 5 | Medium/large

## Slide 3: RAN1#109-e: Tentative goals
Finalize EVM for 9.1.2, 9.1.3.1/2, and 9.1.4.1/2
  Most likely not needed for 9.1.1.1 and 9.1.1.2
  If EVM is needed, reuse EVMs from previous releases whenever applicable/possible
  To be handled by each feature lead (FL)
  Note: The need for EVM implies simulation work (link and/or system) is key for decision making
    Absence of agreed EVM (e.g. in 9.1.1.1/2) doesn’t rule out using simulation results to bolster arguments
According to high-level work scope from WID, define/finalize next-level work scope for each AI
  Limited resource shared by all 7 AIs, i.e. 3 TUs in RAN1, a total of ~10 RAN1 meetings (possibly mixture of eMeetings and F2F)
  Focus on the scope defined in WID, avoid adding out-of-scope issues