## Slide 1: Way Forward on LAA coexistence testing
Qualcomm, Ericsson, Huawei, Nokia
3GPP TSG-RAN WG4 Meeting #79 R4-164971
Nanjing, China 23–27 May 2016

## Slide 2: General overview of RAN4 activity on LAA coexistence tests
RAN4 agreed to define two classes of tests to verify LAA coexistence:
  LBT tests: these are functional tests which verify minimum requirements defined in 3GPP specifications. The LBT core requirements are already captured in TS 36.104 (Chapter 9) while the LBT tests will be defined in Chapter 9 of TS 36.141.
  Multi-node tests: this is a new class of test which whose scope is to verify cross-technology coexistence, with emphasis on coexistence between LAA and Wi-Fi operating in the same spectrum. Multi-node tests will be captured in a new technical report which will be developed by RAN4.

## Slide 3: LBT tests: background information
LBT tests are functional tests which only verify essential LBT functionalities specified in 3GPP specification. As such, these tests will not verify the performance in the presence of Wi-Fi like signal.
RAN4 agreed to align LBT testing procedure with EN 301 893.
RAN4 agreed to test the following requirements [1]:
  Energy Detection (ED) threshold and detection accuracy.
  Maximum Channel Occupancy Time (MCOT).
  Minimum Idle time.

## Slide 4: LBT tests: way forward (1)
Agreed to specify tests with no or static interference
One example test procedure is based on the following block diagram:
MCOT, idle time, and Energy Detection sensing will be tested with a procedure similar to EN 301 893, but adapted to 3GPP nomenclature and format, as in Clause 4.8 in 3GPP TS 36.141.

## Slide 5: LBT tests: way forward (2)
It was agreed to use defer time as the minimum idle time for the corresponding test.
It was agreed to set the interference value for the ED sensing test at (-72dBm+ [4dB])/20MHz

## Slide 6: Multi-node tests: background information
Multi-node tests are cross technology coexistence tests.
Multi-node tests were extensively discussed in RAN# 78bis with the following agreements on the general aspects (way forward from RAN4 #78bis [1]), e.g.:
  Tests should be conductive tests.
  Two DL nodes should be considered.
  Single 20MHz channel should be considered.
It was also agreed to develop a new TR in RAN4 to capture the multi-node tests.

## Slide 7: Multi-node tests: way forward (1)
In RAN4 #79, further agreements on the general aspects of multi-node tests were reached:
  Tests should also cover Wi-Fi to LAA performance. This means that RAN4 will focus on symmetric tests, i.e. the impact from LAA to Wi-Fi and from Wi-Fi to LAA will be considered.
  Signal level at which the receiver victim will see the transmitter aggressor:
    It is agreed to test both below and above ED level (-72dBm/20MHz).
    The precise values to be considered in the tests are FFS.
  Metric:
    it is agreed to use “throughput” as criteria for Priority class 3 and VoIP traffic outage for Priority class 1.
  Number of stations in multi-node tests:
    It is agreed to use one UL node (UE/STA) connected to each DL node (eNodeB/AP).

## Slide 8: Multi-node tests: way forward (2)
Priority classes:
  It is agreed to test only channel access priority class capabilities which are declared by the LAA node.
  It is agreed to test a maximum of two representative priority classes.
Baseline reference for the test and passing criteria
  Several options for the definition of the reference baseline and the passing criteria were discussed but not agreement was reached.
  Further discussion is needed.
A draft skeleton of the Technical Report (TR) for the multi-node tests was proposed and presented in RAN4 #79, documented in R4-164219 [3]. No technical concerns on the structure of the TR emerged during the discussion.

## Slide 9: References
[1] R4-162989, “Way forward on LAA coexistence tests”, Ericsson, Huawei, Qualcomm, Nokia, RAN4 #78bis
[2] R4-164799, “Ad hoc minutes: Rel-13 LAA co-existence testing.Ericsson, RAN4 #79
[3] R4-164219, "Skeleton TR for proposed TR for multi-node tests", Ericsson.
[4] R4-163778, "LBT performance test", Nokia.
[5] R4-163779, "Introduction of LBT performance test for LAA", Nokia.
[6] R4-163937, "Consideration on minimum idle time", Huawei.
[7] R4-163938, "Further consideration on DL LBT test procedure", Huawei.
[8] R4-163939, "Introduction of DL LBT test procedure into TS 36.141", Huawei.
[9] R4-164206, "On LTB tests definition for LAA", Qualcomm Incorporated.
[10] R4-164207, "MCOT, idle time, and channel sensing test for LAA", Qualcomm Incorporated.
[11] R4-164208, "A possible approach to LBT back-off test procedure", Qualcomm Incorporated.
[12] R4-163777, "LAA multi-node test", Nokia.
[13] R4-163940, "Further consideration on multi-node test for LAA", Huawei.
[14] R4-164209, "Additional aspects on multi-node tests", Qualcomm Incorporated.
[15] R4-164218, "Details on multi-node tests for Rel-13 LAA", Ericsson.
[16] R4-164432, "Testing Level of Received Signal for LAA Channel Access Mechanism", CableLabs.