## Slide 1: WF on CSI feedback framework for hybrid beamforming in NR
CMCC, ZTE, ZTE Microelectronics, CATT, Xinwei
3GPP TSG RAN WG1 Meeting #86bis R1-1610727
Lisbon, Portugal 10th - 14th October 2016
Agenda item: 8.1.4.3

## Slide 2: Proposal
For hybrid beamforming, the following CSI reporting operation should at least be supported:
  Step 1: Beam-based CSI/RSRP reporting
    To determine at least analog beam
    Based on UE feedback and/or beam-based reciprocity
      With beam-based reciprocity, TRP/UE can obtain DL/UL Tx beam from its Rx beam by multi-beam reception
  Step 2: Port-based CSI/RSRP reporting
    To determine the precoder for all or part of TXRUs (narrow digital beam) given the reported analog beam
    Based on UE feedback and/or port-based reciprocity
      With port-based reciprocity, TRP/UE can obtain DL/UL CSI based on UL SRS/DL RS
  Step 3: CQI reporting
    To determine CQI for data transmission given the reported analog and digital beam(obtaining assumed PMI)
    Based on UE-specific beamformed CSI-RS transmission using the assumed PMI
Study the association of RSs in the above steps
  E.g. DL and UL RS association
CSI feedback for full digital or full analog beamforming can be a special case of the above framework
Further optimization of the procedure for reciprocity/non-reciprocity can be considered
  E.g. combinations of certain steps