## Slide 1: WF on Interference Measurement Enhancements
CATT, Samsung, CATR, ITRI, InterDigital, KT, KDDI, LG Electronics, ZTE, Xinwei
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, 10th - 14th October 2016
Agenda item: 7.2.2.1.2
R1-1610771

## Slide 2: Background
CSI-IM allows simple, straightforward interference measurement processing at UE
eNB needs to transmit proper signal on CSI-IM to emulate interference of different transmission hypotheses (e.g. MU pairing)
For massive MIMO and a large pool of candidate UEs, the number of MU-MIMO hypotheses grows rapidly
From UE perspective, each CSI-IM has a periodicity of at most 5ms, and is hardwired to a CSI-RS
From eNB perspective, at most 10 CSI-IM (and therefore MU hypotheses) can be used per subframe per cell
Inflexible CSI-IM pooling and MU-CSI emulation for eNB scheduling, even with time-domain measurement restriction on CSI-IM

## Slide 3: Proposal
  Support aperiodic CSI-IM for enhanced interference measurement
    Step 1. RRC configuration of Aperiodic CSI-IM
      Without subframe_config
      Configure a UE with K = {1, 2, .., 4} CSI-IM
    Step 2: One out of K CSI-IM is selected via the UL-related DCI
      A UL grant carrying a CSI request indicates interference measurement on one of K CSI-IM resources for a CSI process for which the CSI is requested
        An indication of aperiodic CSI-IM independent from CSI request is supported
    Only PUSCH-based A-CSI report is supported
    A-CSI-IM is assumed in the same DL subframe as the UL grant
Other interference enhancement mechanism FFS