## Slide 1: WF on S-RSSI measurement interval
CATT, LGE,NTT DoCoMo, ZTE, Xinwei
3GPP TSG RAN WG1 Meeting #87 R1-1613201
Reno, USA 14th - 18th December 2016
Agenda item – 6.2.1.7

## Slide 2: Background
Agreements
  FFS the following aspects till the next meeting
    Scale the SL_RESOURCE_RESELECTION_COUNTER to 2(for 50ms period) or 5 (for 20 ms period)
    S-RSSI measurement interval is (select one of the options at the next meeting)
      100 ms interval is kept (option 1)
      set to the minimum allowed I (option 2)
      set to the resource reservation interval used for transmission of the UE (option 3)
      Combination of allowed intervals {20, 50, 100} with shortened averaging duration (option 4)
    In step2, reselection UE scales the number of reservations of other UE within selection window by 1/i when 0<i<1.

## Slide 3: Background
S-RSSI measurements would be optimistic/pessimistic when actual transmission time interval is not the same as the measurement interval defined in option 1, 2, and 4

## Slide 4: Proposals
S-RSSI measurement interval shall be set to the resource reservation interval used for transmission of the UE when 0<i<1.