## Slide 1: WF on NR NW Initiated Beam Switching
Intel Corporation, Ericsson
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th –18th November 2016
Agenda: 7.1.3.3
R1-1613287

## Slide 2: Agreement from RAN1#86b
NR supports mechanism(s) in the case of link failure and/or blockage for NR
  Whether to use new procedure is FFS
Study at least the following aspects:
  Whether or not an DL or UL signal transmission for this mechanism is needed
    E.g., RACH preamble sequence, DL/UL reference signal, control channel, etc.
  If needed, resource allocation for this mechanisms
    E.g., RACH resource corresponding mechanism, etc.

## Slide 3: Proposal
To provide robustness against beam pair link blocking etc, a UE can be configured to monitor PDCCH in N beam pair links
  N =1,2 supported
  Other values of N are FFS
  Details such as simultaneous monitoring, TDM monitoring, periodicity, search space etc, of the N beam pair links is FFS
Note for the purpose of discussion
  A beam pair link is defined conceptually as a TX beam and RX beam
    The notion of beam pair link is for the sake of discussion and may not appear in specifications
    An RX beam is conceptual and may not appear in specification, it could be specified as a spatial QCL parameter, a RX receive weighting or a receiver configuration meaning a particular set of beamforming weight(s) applied to a particular set of physical antennas and/or antenna panels
    A TX beam is conceptual and may not appear in specification, it may be defined as a particular reference signal such as a (beamformed) CSI-RS