## Slide 1: WF on the combination of DL and UL sTTI length
Huawei, HiSilicon, LGE, ZTE, ZTE Microelectronics
3GPP TSG RAN1 #87
Reno, USA Nov 14 - 18, 2016
Agenda Item: 6.2.10.2.1
R1-1613374

## Slide 2: background
Agreements in RAN1 86bis meeting
For the combination of sTTI for DL and UL, RAN1 chooses one to be supported among the following alternatives.
  Alt 1. {2,2}, {7,7}
  Alt 2. {2,2}, {2,4}, {7,7}
  Alt 3. {2,2}, {2,7}, {7,7}
  Alt 4. {2,2}, {2,4}, {2,7}, {7,7}
  Note: {a,b} denotes {DL sTTI length, UL sTTI length}.
  Note: DL sTTI length is used for sPDCCH and sPDSCH.
  Note: UL sTTI length is used for sPUSCH and sPUCCH corresponding to sPDCCH and sPDSCH, respectively.
RAN1 study the necessity of {2,14} and/or {7,14}

## Slide 3: Proposal
Alt.4 is supported for sTTI WI
  i.e, UE supports the {DL, UL} sTTI length combination of {2,2}, {2,4}, {2,7}, {7,7}