## Slide 1: WF on SLSS and PSBCH contents
LG Electronics, NTT Docomo, Samsung
3GPP TSG RAN WG1 Meeting #87
Reno, US 14th - 18th November 2016
Agenda item: 6.2.1.7
R1-1613401

## Slide 2: Background
Agreements in RAN1 #86bis:
  Rel-12 mechanism is re-used to determine the subframe used for transmissions of SLSS/PSBCH from out-coverage UEs synchronized to SLSS, i.e., two SLSS resources are pre-configured for an out-coverage UE, one is used for SLSS of UE’s syncRef and the other is used for SLSS transmission of the UE.
  Working assumption: An out-coverage UE directly synchronized to GNSS transmits SLSS/PSBCH on the pre-configured sync resource which is one of the two preconfigured sync resources.
    FFS: Out-coverage UE indirectly synchronized to GNSS
    In the other resource, the UE receives PSBCH potentially transmitted from an in-coverage UE.
  FFS whether a UE that selected SLSS ID = 0 as its sync reference transmits SLSS = X (FFS 0 or 168) and PSBCH in a different resource.
  FFS PSBCH content if transmits

## Slide 3: Background
From the working assumption, if UE #1 transmits SLSS/PSBCH on sync resource 1, UE #2 and #3 transmit SLSS/PSBCH on sync resource 2.
UE #2 transmits the updated PSBCH contents on resource 2, but UE #3 transmits the preconfigured PSBCH contents.
Rx UE may not decode PSBCH on sync resource 2 as different PSBCH contents are transmitted with the same RS sequence.
Therefore, the working assumption cannot be confirmed.

## Slide 4: Open issues
SLSS resource/PSBCH contents
SLSS ID when a UE that selected SLSS ID = 0 as its sync reference

## Slide 5: Proposals
Proposal 1: The same sync resource is used for UEs directly synchronized with GNSS. RAN1 assumes that eNB controlled PSBCH contents for in-coverage UE always is aligned with pre-configured PSBCH contents.
  UE directly synchronized to GNSS is not required to monitor PSBCH in the other resource.
Proposal 2: a UE that selecting SLSS ID = 0 with coverage indicator = 1 as its sync reference transmits SLSS = 0 with in-coverage indicator = 0.
  In-coverage indicator is used to differentiate direct GNSS and in-direct GNSS.
  SLSS ID 0 or 168 is used to differentiate 1 hop sync. or more hops for GNSS based synchronization