## Slide 1
Way Forward -
Fractional PRB
ZTE, ZTE Microelectronics, Samsung, Panasonic, Deutsche Telekom, Docomo, Etri
R1-1613447
3GPP TSG RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 7.1.1

## Slide 2
Background
RAN4 #80b (Oct’16)
Agreements:
• Carrier spectrum utilization, denoted by Y, is assumed to be higher than 90% in RAN4 future study and RAN4 requirements should be defined based on this assumption.
– Y may depend on specific numerology and carrier bandwidth. It is FFS how the guard band at the edge of a channel should be defined when different numerologies are frequency multiplied
– Y may depend on the BS/UE implementation complexity and declared capability. It is possible to define different value of Y for different BS/UE capabilities with compliance of related RF requirements, e.g. EVM, ACLR, SEM, etc. It is important to verify both the spectrum and EVM results at the same time in order to ensure well performing and robust system
RAN1 #86 (Aug’16)
Agreement:
• It is recommended that RAN4 should target to support eNB/UE with Y significantly higher than 90% when defining the RAN4 requirements where the specification of Y should consider complexity and latency constraints

## Slide 3
Background
Outcome from RAN1#86b

## Slide 4: Background
  3 areas where fractional PRB shows benefits have been identified
    Mitigation of Inter-numerology-interference (INI), when numerologies are mixed within an NR band
    Impact on LTE performance for LTE/NR co-existence
    Spectrum edge utilization

## Slide 5: Background - Mitigate intra-band INI
  In [1] and [2]
    A few guard tones are enough to mitigate the INI
  Whole PRB as guard will lead to resource waste
    Especially for wide SCS and when multiple numerologies are scheduled at the same time
    => Beneficial to support fractional PRB
Resource utilization efficiency descreases for multiple numerologies with integer guard

## Slide 6: Background - Impact on LTE performance
  In TR 38.913 it has been stated "The New RAT shall be able to co-exist with LTE on adjacent spectrum in the same band in the same geographical area, including collocated deployments of the same or different operators; where the ability to coexist is based upon an agreed maximum degradation of throughput that is found acceptable on LTE.“
  LTE and NR with 60 kHz may co-exist
  Simulation in [1] show: Wide SCS has more INI impact on narrow SCS
  38.913: LTE performance in throughput cannot be decreased below an certain minimum
    => Guard needs to be implemented on NR side
  At least 720 kHz (one PRB at SCS = 60 kHz) would be needed
    => Spectrum waste
    => Beneficial to support fractional PRB

## Slide 7: Background – Band edge utilization
  In RAN4, it has been agreed that spectrum utilization shall be > 90%
  Withouth fractional PRB, this is not possible to satify for certain BW/SCS combinations
  => Support of Fractional PRB is needed to meet RAN4 requirements
(*): Need of such a scenario is FFS itself

## Slide 8: Proposals
  Fractional PRB, less than 12 subcarriers, is supported for NR at least for data
  Fractional PRB is only used when an adjacent full PRB is used with the same numerology.
  No special handling of DMRS (like DMRS location) due to the presence of fractional PRB. To use the closest RS in adjacent full PRB for demodulation should be possible.
  Fractional PRB is applied to OFDM, FFS if DFT-s-OFDM is supported
  For other topics, RAN1 shall strive for keeping the design of the fractional PRB simple and to minimize the standardization impact, e.g.:
    Transport block size handling in the same manner as it would be done for the flexible slot/subslot length
    Transmit power control handling in the same manner as it would be done for flexible scheduling in the number of PRBs

## Slide 9: References
  [1] R1-1611285 About INI and fractional PRB, ZTE, Reno, Nov 2016
  [2] R1-1612445 Guard band Considering Inter-Numerology Interference, Samsung, Reno, Nov 2016
  [3] R1-1612446 Guard band Considering Channel Bandwidth for Mixed Numerologies, Samsung, Reno, Nov 2016
  [4] R1-1611893 Discussion and evaluation results on fractional PRB usage, Panasonic, Reno, Nov 2016
  [5] R1-1612216 Remaining issues on NR frame structure, ETRI, Reno, Nov 2016
  [6] R1-1612714 Frequency-domain aspects of frame structure, NTT Docomo, Reno, Nov 2016