## Slide 1: WF on Synchronization Raster
Qualcomm, …
R1-1613563
3GPP TSG RAN WG1 Meeting #87
Reno, USA, 14-18 November 2016
Agenda item 7.1.2.1

## Slide 2: Background
NR is expected to have deployments in wide frequency bands
In NR, DL cell-specific reference signal similar to LTE CRS might not be broadcast or not often enough especially in TDD subframe structures, making frequency scan very challenging.
Potential NR/LTE waveform confusion since both NR and LTE employ OFDM-based waveforms in DL
In previous sessions, the following was agreed:
Agreements:
The raster for NR synchronization signals can be different per frequency range. At least for frequency ranges where NR supports a wider carrier bandwidth and operation in a wider frequency spectrum (e.g. above 6 GHz), the NR synchronization signals raster can be larger than the 100 kHz raster of LTE.
A joint decision should be made on:
  the supported minimum carrier bandwidth for a NR carrier
  the supported bandwidths of synchronization signals for NR
  the frequency raster for synchronization signals for NR
  the frequency raster for the center of NR carrier (if applicable)

## Slide 3: Proposal
Synchronization raster is larger than 100kHz for <6GHz
Possible frequency locations of synchronization signal are:
  Alt. 1. A subset of possible frequency locations of the center(s) of possible NR carrier(s) in a band
  Alt. 2. A multiple of a reference subcarrier spacing/PRB bandwidth
  Note: Combinations of Alt. 1 and Alt. 2 may be possible
Frequency location of synchronization signal is subcarrier aligned with data/control
For a NR cell, the center frequency for the synchronization signal can be different from the center frequency of the NR carrier