## Slide 1
3GPP TSG RAN WG1 Meeting #87 R1-1613621 Reno, USA, 14th - 18th Nov 2016
Agenda item: 7.1.3.2
WF on Unified CSI-RS Framework
Huawei, HiSilicon, ZTE, ZTE Microelectronics

## Slide 2: Background
Following agreements have been made in RAN1#86bis:
  At least the following RSs are supported for NR downlink
    CSI-RS: Reference signal with main functionalities of CSI acquisition, beam management
  Study CSI-RS resources configuration in 2 steps
    Configure multi sets of CSI-RS resources for one UE
  Support NR CSI-RS pattern with at least the following properties:
    CSI-RS mapped in one or multiple [consecutive] symbols
    FFS: At least CSI-RS located at the earlier part of a slot in some cases
      FFS: before or after the DM-RS agreed to study in RAN1#85
    FFS: CSI-RS located at other part of a slot
    Working assumption: Configurable density of CSI-RS in frequency and/or time domain by UE-specific manner

## Slide 3: Proposal
Study a unified CSI-RS framework to support both beam management and CSI acquisition, with at least the following properties:
  CSI-RS aggregated by one or multiple basic CSI-RS patterns
    The number of basic CSI-RS patterns is configurable
  The basic CSI-RS pattern to contain/support
    Two consecutive symbols
    CSI-RS port number at least up to 32
Support configurable location of CSI-RS in a slot
  FFS: the detail location in a slot
Support configurable density in frequency domain for each CSI-RS resource configuration