## Slide 1: Summary on CA Topics
Samsung
R1-1813877
3GPP TSG RAN WG1#95
Spokane, USA, November 12 – 16, 2018
Agenda item 7.1.3.4

## Slide 2: Timing k for Scell Activation/Deactivation
Resolve the FFS for value of k in FR2
  Same as FR1: k = K1 + 3Nslotsubframe, + 1 - (R1-1812962, R1-1813531)
  1 msec faster in FR2 than FR1: k = K1 + 2Nslotsubframe, + 1 – (R1-1813150)
  Comment: Conclude whether FR2 shall have faster (1 msec) SCell activation/deactivation

## Slide 3: Corrections
Per TS 38.331, when configured, SPS PDSCH is on one cell per CG  no need to consider HARQ-ACK for more than one SPS PDSCH in a PUCCH/PUSCH (R1-1812606)
  Comment: Agree to correct in 38.213
For CA in same or different frequency bands (R1-1813303)
  When UE reports capability of simultaneousRxTxInterBandCA, UE follows slot configuration of “a serving cell”
  When a UE does not report the capability of simultaneousRxTxInterBandCA, UE follows slot configuration of “a serving cell” in the frequency band
  Comment: Agree to capture (not an error case that different cells can have different slot configurations in second sub-bullet) – further details are necessary
    E.g. the ‘a serving cell’ is the PCell or cell with smallest index if PCell is not in the frequency band
    E.g. flexible symbols on PCell mean no Tx/Rx on SCells
HARQ-ACK timing indication when slot boundaries are not aligned - mixture of NCP and ECP (R1-1813531)
  Comment: Use “k=0 corresponds to the last slot of the PUCCH transmission that overlaps with the slot of the PDSCH reception” in 38.213 to solve slot alignment issue due to NCP/ECP mix

## Slide 4: Semi-static/Type-1 Codebook
A UE capable of receiving only one PDSCH per DL slot should report HARQ-ACK per DL slot (R1-1812962, R1-1813150)
  TS 38.213 currently captures HARQ-ACK per UL slot (e.g. does not provide HARQ-ACK per DL slot when UL SCS is smaller than DL SCS)
  Comment: Agree to correct in 38.213
    HARQ-ACK dropping w.r.t. BWP switching
  Keep pseudo-code simple and do not optimize for corner cases with no performance impact  PDSCH occasion pruning should be per DL slot (R1-1812962)
  Agreement is to report HARQ-ACK after BWP switching  PDSCH occasion pruning should be per PDSCH time-resource table rows (R1-1813150)
  Comment: Conclude on level of optimization and respective impact – there are more cases to optimize for various UL/DL SCS and BWP switching scenarios - focus on essential corrections
  HARQ-ACK location for SPS PDSCH release is determined from SLIV and slot of SPS release DCI (R1-1812606, R1-1813202)
  RAN1#94bis conclusion: For semi-static HARQ-ACK codebook, clarify that location of HARQ-ACK for SPS PDSCH release is same as for the SLIV of SPS PDSCH
  Comment: Conclude on need of proposal from R1-1812606/R1-1813202

## Slide 5: Other
For TDD and dynamic/Type-2 HARQ-ACK codebook
  Order set of PDCCH monitoring occasions first in ascending order of start time of search space set for PDCCH monitoring occasion and then in ascending order of start time of PDSCHs scheduled within PDCCH monitoring occasion(s) with same start time (R1-1812183)
  Further order HARQ-ACK bits based on CORESET index and lowest CCE index in case of a same start time of search space sets associated with 2 DL assignments (R1-1812473)
  Comment: No apparent need/benefit for the proposed enhancements – also, DAI functionality is sufficient if 2 DL assignments in same (or fully aligned) CORESET are to be supported
PUCCH/PDSCH slot determination in case of repetitions and impact on Type-1 HARQ-ACK codebook (R1-1813531)
  Comment: No apparent problem – not different than operation without repetitions
PDSCH overlapping by different K1 values (R1-1813531)
  Comment: Previously discussed and concluded (no optimization of pseudo-code – configuration of HARQ-ACK multiplexing was deemed to be atypical for a coverage limited UE)
Limit maximum HARQ-ACK size to 360 bits (modified proposal from R1-1812184)
  Comment: Argument is to contain gNB/UE complexity, avoid code-block segmentation, and HARQ-ACK codebook size larger than 360 bits is atypical, can easily be avoided by gNB, and UE should not have to handle

## Slide 6: References
TDoc | Title | Source | Agenda item
R1-1812183 | Corrections on bandwidth part and CA | Huawei, HiSilicon | 7.1.3.4
R1-1812473 | Remaining issues for carrier aggregation and bandwidth parts | Intel Corporation | 7.1.3.4
R1-1812606 | Corrections to CA and BWP operation | CATT | 7.1.3.4
R1-1812962 | Remaining Issues on BWP and CA | Samsung | 7.1.3.4
R1-1813150 | On maintenance for BWPs and CA | Nokia, Nokia Shanghai Bell | 7.1.3.4
R1-1813202 | Remaining issues on HARQ-ACK of SPS PDSCH release | Sharp | 7.1.3.4
R1-1813303 | Maintenance for carrier aggregation and bandwidth part | NTT DOCOMO, INC. | 7.1.3.4
R1-1813401 | Maintenance for carrier aggregation and bandwidth parts | Qualcomm Incorporated | 7.1.3.4
R1-1813473 | Remaining issues on CA and BWPs | Ericsson | 7.1.3.4
R1-1813531 | Remaining Issues on HARQ-ACK Transmission | WILUS Inc. | 7.1.3.4