## Slide 1: Channel access proposals for NR-Unlicensed
Broadcom, Cisco, HPE, BlackBerry, …
3GPP TSG RAN WG1 Meeting #95 R1- 1813996
Spokane, USA, November 12th – 16th, 2018
Agenda item: 7.2.2.4.1

## Slide 2: Introduction
This presentation discusses the following channel access procedures for NR-U:
Transmissions outside a shared COT: No-LBT and 25us LBT for critical NR-U messages
Transmissions inside a shared COT: No-LBT for UL transmissions
Transmissions inside a shared COT: DL-UL-DL switches when the DL-UL gap exceeds 25us
Transmissions inside a shared COT: Multiple one-shot LBT attempts for granted UL transmissions
Shared COT for Autonomous Uplink (AUL) transmission
UE-to-gNB COT sharing
Multi-carrier channel access

## Slide 3: Transmissions outside a shared COT: No-LBT and 25us LBT
There are proposals that NR-U DRS, RACH, PUCCH etc. should use either no-LBT or 25us LBT outside a shared COT.
Equivalent messages in Wi-Fi such as beacons, probe request/response, association request/response etc. are transmitted with CAT4 LBT.
So, in order to be fair to co-channel Wi-Fi even when fairness is defined in a bidirectional manner as being “mutually fair” for example by ensuring equal opportunity or equal probability of channel access, it is necessary that DRS and RACH/PUCCH etc. in NR-U be also transmitted with CAT4 LBT outside a gNB shared COT.
It has been argued in RAN1 that LAA DRS uses 25us LBT and so NR-U DRS should also use 25us LBT.
  However, during LAA standardization, the decision regarding 25us LBT for LAA DRS was made under the incorrect assumption that equivalent Wi-Fi messages are transmitted using 25us LBT.
  This incorrectness has been pointed out by IEEE 802.11 through multiple LSs sent to RAN1.
  Note also that the clause that DRS be limited to 5% of the total airtime “per device” does not alleviate the concerns regarding aggressive channel access, since for a network with uncoordinated transmission of such messages from multiple devices, the total airtime of messages with 25us LBT can be much higher.
Proposal 1: No-LBT and 25us LBT shall not be used for transmission of any NR-U messages outside a shared COT.
Critical messages in NR-U that are not multiplexed with other lower priority messages/data can be transmitted using CAT4 LBT of the highest priority.

## Slide 4: Transmissions inside a shared COT: no-LBT for NR-U UL
ETSI-BRAN allows no-LBT before a UL transmission if the DL-UL gap is <= 16 us.
Even when DL-UL gaps <= 16us, Wi-Fi uses no-LBT only for short transmissions:
  802.11ac: (Block) ACKs
  802.11ax: UL transmissions with duration <= 128us in most cases and <= 584us in some special cases, including the preamble.
No-LBT transmissions lead to collisions in presence of hidden nodes.
  A Wi-Fi only network is expected to have a much lower incidence of hidden nodes than a NR-U + Wi-Fi network due to an at least 10dB lower detection threshold among Wi-Fi nodes.
    PD at -82dBm (or lower) in a Wi-Fi only network compared to ED at -72dBm or -62dBm in a NR-U + Wi-Fi network
  However, the incidence of hidden nodes in a NR-U + Wi-Fi network will be similar to a Wi-Fi only network if NR-U transmits and receives the Wi-Fi preamble at -82dBm. In this case, the impact of no-LBT may also be similar to a Wi-Fi only network.
A Wi-Fi network is required to implement many other schemes to mitigate collisions that arise due the presence of hidden nodes [1].
Proposal 2: If NR-U uses no-LBT for UL transmissions inside a shared COT in case the DL-UL gap is <= 16us, it must ensure that the impact of no-LBT in an NR-U + Wi-Fi network is similar to that of a Wi-Fi only network by implementing the following:
  The incidence of hidden nodes in an NR-U + Wi-Fi network is similar to the incidence of hidden nodes in a Wi-Fi only network by transmission and reception of a preamble based on the Wi-Fi preamble.
  Implement procedures similar to Wi-Fi in order to mitigate collisions from hidden nodes.
  Restrict no-LBT to short control transmissions.

## Slide 5: Transmissions inside a shared COT : DL-UL-DL switches when DL-UL gap > 25us
In LAA a shared COT cannot have DL-UL-DL switches.
It is being proposed that NR-U should be allowed to have one or more DL-UL-DL switches even when the DL-UL gap is > 25us and only one-shot LBT of 25us is performed ahead of the UL transmission.
However, ETSI-BRAN EN 301 893 does not allow DL-UL-DL switches in a shared COT when the DL-UL gap is > 25us
Proposal 3: An NR-U shared COT shall not have DL-UL-DL switches if the gap between any of the switching points is > 25us.
For gaps <= 25us, the procedure is FFS.

## Slide 6: Transmissions inside a shared COT : Multiple one-shot LBT attempts for granted UL transmissions
The shared COT feature was added to ETSI-BRAN in order to accommodate the UL grant-to-UL transmission delay in LAA.
It is being proposed that an NR-U UE be allowed multiple one-shot LBT attempts within a shared COT for granted UL transmissions.
There are two different interpretations on the number of one-shot LBT attempts that are allowed in ETSI-BRAN within a shared COT for transmissions after a pause.
  Interpretation 1: only a single one-shot LBT is allowed.
  Interpretation 2: multiple one-shot LBT attempts are allowed, but the number of one-shot LBT attempts is limited to the total consecutive time in milliseconds granted to the Responding device for transmission within a shared COT.
Proposal 4: The number of one-shot LBT attempts within a shared COT for granted UL transmissions in NR-U shall be limited to the total consecutive time in milliseconds granted to the UE for transmission within the shared COT.

## Slide 7: Shared COT for Autonomous Uplink (AUL) transmission
The shared COT feature was added in ETSI-BRAN to accommodate the UL grant-to-UL-transmission delay present in scheduled UL LAA.
Such a concession was needed to pause the COT and relax the LBT for only those transmissions which could not have otherwise occurred in the absence of a grant.
So, only those transmissions that cannot happen without an explicit grant within the same COT should utilize the shared COT.
AUL transmissions which can proceed without any grant should not use a shared COT and should instead use CAT4 LBT.
Coexistence with Wi-Fi:
  802.11ac does not use a shared COT.
  802.11ax uses a shared COT only for triggered (granted) UL transmissions, whereas AUL transmissions use CAT4 LBT.
So, in order to be fair to co-channel Wi-Fi even when fairness is defined in a bidirectional manner as being “mutually fair” for example by ensuring equal opportunity or equal probability of channel access, it is necessary that AUL transmissions in NR-U use CAT4 LBT.
Proposal 5: Autonomous Uplink transmissions in NR-U shall use CAT4 LBT.

## Slide 8: UE-to-gNB COT sharing
If UE to gNB COT sharing is allowed without restrictions it can be used to circumvent the principles of fair channel access. Some of the examples are as follows:
The ED threshold used for CAT4 LBT to win a COT is proportional to the maximum transmit power of a device. However, if UE-gNB COT sharing is allowed without restrictions, a COT that is won with a higher ED threshold due to the lower maximum transmit power of a UE can be used by a gNB which has a much higher transmit power and would have otherwise used a lower ED threshold.
It can be used by a gNB to circumvent congestion in its neighbourhood by directing a UE that experiences the least congestion to win the COT and then handover the COT to the gNB for its own transmission. The above procedure can be enabled by the existing LTE/NR specification as the gNB is aware of the congestion around each UE via Layer2 reports.
Proposal 6: For UE to gNB COT sharing, a procedure similar to AUL UE to eNB COT sharing as agreed in RAN1#92 can be considered as a starting point also keeping in mind the restrictions due to differences in the maximum transmit power between the UE and the gNB. For example,
The DL transmission shall be limited to a partial ending subframe of up to 2 OS length
The DL transmit power shall be equal to (or lower) than the transmit power used by the UE to determine the ED threshold for CAT4 LBT.

## Slide 9: Multi-carrier channel access schemes
Multi-carrier channel access schemes are already specified in section 4.2.7.3.2.3 of ETSI-BRAN EN 301 893.
Wi-Fi already follows these schemes
LAA UL too follows these schemes
For fair-coexistence, NR-U must also follow the same schemes as specified by ETSI-BRAN
Proposal 7: Multi-carrier channel access in NR-U shall follow the multi-carrier channel access schemes specified in section 4.2.7.3.2.3 of ETSI-BRAN EN 301 893.

## Slide 10: References
[1] R1-1813565, Proposals for channel access procedures for NR-Unlicensed