## Slide 1: WF for new capability signalling for intra-band EN-DC and NR CA CHTTL
3GPP TSG-RAN WG4 Meeting #88bis R4-1814175 Chengdu, China, 8th – 12th October, 2018

## Slide 2: Backgrounds
Different RF architectures for intra-band EN-DC have been discussed when introducing intra-band EN-DC combinations
It is beneficial for network to differentiate UEs with different capabilities including single uplink/dual uplink support with the assumption of 1PA/2PA architectures [1][2]
  1PA architecture: LTE and NR UL share the same antenna
  2PA architecture: LTE and NR UL use separate antennas
With adding a new capability signalling, it is possible to provide more flexibility in the specification for the general MPR requirement [3]

## Slide 3: Proposals
Wayforward for differentiate requirements with assumption of single PA and dual PA architectures
  A new one bit capability per band per band combination is considered from Rel.15 for intra-band EN-DC, intra-band UL CA and FDM-based ULSUP to enable referring to two sets of requirements with assumption of single PA and dual PA architectures
  At least the following requirements are involved by this capability bit
    A-MPR/MPR and MSD values for dual uplink
      Whether two sets of requirements will be introduced in RAN4 can be further discussed for each specific band combination
    Switching time between LTE UL and NR UL in single switched UL operation mode for intra-band non-contiguous EN-DC
  Other potential capabilities related to intra-band EN-DC can be further discussed

## Slide 4: Reference
  [1R4-1813120 “WF on clarification of single UL and dual UL support for DC_3_n3”, CHTTL, RAN4#88bis
  [2] R4-1812355, “MSD for DC_3_n3 One and Two PA Architectures”, Skyworks, RAN4#88bis
  [3] R4-1812403, “Intra-band EN-DC MPR”, Qualcomm Incorporated, RAN4#88bis