## Slide 1
Rel-16 TEI
Aperiodic CSI-RS Triggering for UE reporting
beamSwitchTiming values of 224 and 336
vivo, ZTE
3GPP TSG RAN WG1 #98 R1- 1909228
Prague, CZ, August 26th – 30th, 2019

## Slide 2
Motivation
For FR2 aperiodic CSI-RS beam switching in Rel-15, UE feature 2-28 reports one of the following values {14, 28, 48, 224, 336};
For the following cases, the default QCL of aperiodic CSI-RS when triggering offset is smaller than the reported 2-28 value is not specified:
  Aperiodic CSI-RS for CSI when UE reports 224 or 336 for both same cell and cross cell triggering;
  Aperiodic CSI-RS for beam management for both same cell and cross cell triggering ;
  For any aperiodic CSI-RS triggering when CORESET is not configured on the serving cell where aperiodic CSI-RS resource is configured;
This may lead to one of the following:
  Larger power consumption: all panels may need to be powered on all the time for smaller triggering offset for CSI-RS for CSI;
  Increased overhead: periodic CSI-RS resource for CSI-RS measurement on another panel, which causes overhead;
  System performance reduction: the CSI may not be accurate due to large delay;

## Slide 3
Scope
For the following cases, further clarify the default QCL of aperiodic CSI-RS when triggering offset is smaller than the reported 2-28 value:
  Aperiodic CSI-RS for CSI when UE reports 224 or 336 for beamSwitchTiming ;
  Aperiodic CSI-RS for beam management for any reported values of beamSwitchTiming;

## Slide 4
Possible Solutions
Two possible solutions that can address above concerns are listed for further discussion in RAN1 #98 in Prague:
  The main difference between Solution1 and Solution2 is
    Solution1: UEs reporting 224 or 336 follow the behavior of UEs reporting one of the values of {14, 28, 48};
    Solution2: 48 is used as the beam switching threshold for UEs reporting 224 or 336;

## Slide 5
Potential Solution1:
Spec impact on section 5.2.1.5.1 in TS 38.214
  If the scheduling offset between the last symbol of the PDCCH carrying the triggering DCI and the first symbol of the aperiodic CSI-RS resources in a NZP-CSI-RS-ResourceSet configured without higher layer parameter trs-Info and without the higher layer parameter repetition is smaller than the UE reported threshold beamSwitchTiming, as defined in [13, TS 38.306], when the reported value is one of the values of {14, 28, 48}.
    if there is any other DL signal with an indicated TCI state in the same symbols as the CSI-RS, the UE applies the QCL assumption of the other DL signal also when receiving the aperiodic CSI-RS. The other DL signal refers to PDSCH scheduled with offset larger than or equal to the threshold timeDurationForQCL, as defined in [13, TS 38.306], aperiodic CSI-RS scheduled with offset larger than or equal to the UE reported threshold beamSwitchTiming when the reported value is one of the values {14,28,48}, periodic CSI-RS, semi-persistent CSI-RS;
    else, when receiving the aperiodic CSI-RS, the UE applies the QCL assumption used for the CORESET associated with a monitored search space with the lowest CORESET-ID in the latest slot in which one or more CORESETs within the active BWP of the serving cell are monitored.
  If the scheduling offset between the last symbol of the PDCCH carrying the triggering DCI and the first symbol of the aperiodic CSI-RS resources is equal to or greater than the UE reported threshold beamSwitchTiming when the reported value is one of the values of {14,28,48}, the UE is expected to apply the QCL assumptions in the indicated TCI states for the aperiodic CSI-RS resources in the CSI triggering state indicated by the CSI trigger field in DCI.

## Slide 6
Potential Solution2:
  Spec impact on section 5.2.1.5.1 in TS 38.214
  If the scheduling offset between the last symbol of the PDCCH carrying the triggering DCI and the first symbol of the aperiodic CSI-RS resources in a NZP-CSI-RS-ResourceSet configured without higher layer parameter trs-Info and without the higher layer parameter repetition is smaller than the minimum value between 48 and the UE reported threshold beamSwitchTiming, as defined in [13, TS 38.306]. , when the reported value is one of the values of {14, 28, 48}.
    if there is any other DL signal with an indicated TCI state in the same symbols as the CSI-RS, the UE applies the QCL assumption of the other DL signal also when receiving the aperiodic CSI-RS. The other DL signal refers to PDSCH scheduled with offset larger than or equal to the threshold timeDurationForQCL, as defined in [13, TS 38.306], aperiodic CSI-RS scheduled with offset larger than or equal to the minimum value between 48 and the UE reported threshold beamSwitchTiming when the reported value is one of the values {14,28,48}, periodic CSI-RS, semi-persistent CSI-RS;
    else, when receiving the aperiodic CSI-RS, the UE applies the QCL assumption used for the CORESET associated with a monitored search space with the lowest CORESET-ID in the latest slot in which one or more CORESETs within the active BWP of the serving cell are monitored.
  If the scheduling offset between the last symbol of the PDCCH carrying the triggering DCI and the first symbol of the aperiodic CSI-RS resources is equal to or greater than the minimum value between 48 and the UE reported threshold beamSwitchTiming when the reported value is one of the values of {14,28,48}, the UE is expected to apply the QCL assumptions in the indicated TCI states for the aperiodic CSI-RS resources in the CSI triggering state indicated by the CSI trigger field in DCI.