## Slide 1: Way Forward on CoMP Feedback Modes
Samsung, DoCoMo, Intel, InterDigital, LGE, NEC, Ericsson

## Slide 2: Proposal
Rel-11 supports the feedback configuration and reporting for simultaneous CA and CoMP.
  Simultaneous CoMP and could be either,
    CoMP on >=1 CC
    CoMP on max 1 CC when CA is configured

## Slide 3: CSI Dropping/Multiplexing/Compression
Dropping rule is supported based on reporting type and CSI process/CC index
  Alt 1: Reporting type  CSI process index  CC index
  Alt 2: Reporting type  CC index  CSI process index
  Alt 3: Reporting type  CSI process index (if CSI process config includes cell index)
  Note: The alternatives could depend on the exact definition of “CSI process”
Follow CA behavior for CSI Multiplexing
  No consensus on CSI Multiplexing for multiple CSI processes with PUCCH Format 3 or PUSCH
Compression schemes suitable for CoMP can be considered on PUCCH Format 2.

## Slide 4: Aperiodic CSI request
For 2-bit CSI request,
  ’00’ state indicates no trigger
  Selection between two or more RRC configured sets of CA+CoMP processes
For 1-bit CSI request
  ’0’ state indicates no trigger
  ‘1’ state - One of the states in the 2-bit case may be reused (e.g., 01)