## Slide 1: Evaluation of uplink performance for co-channel het net
Alcatel Lucent, Alcatel Lucent Shanghai Bell
3GPP TSG RAN WG1 #73 R1-132033
Fukuoka, Japan, 20th – 24th May, 2013
Agenda item: 5.3.2
Notes: 1

## Slide 2
Simulation setup
  LPN power, 30dBm and 37dBm
  8 UEs/Macro geographic area
  50% Hotspot UE dropping (60m radius for 37dBm, 35m radius for 30dBm)
  4 LPN/Macro
  3dB CIO, 0dB LPN UL Padding
  6dB RoT target
  Soft-handover enabled between LPN and Macro
  Outdoor pathloss model

## Slide 3
Detailed statistics
  UE throughput CDF
    Among all the UEs in the system
    Separate the UEs served by LPN and Macro
  Mean, Median and 5% UE throughput for both the baseline and HetNet
  UL UE throughput fairness
    Defined as UE Tput/Average UE Tput (25.896, section 9)
  Average cell RoT CDF (separate Macro and LPN)

## Slide 4: 30dBm LPN power 50% Hotspot UE dropping (35m radius) 4 LPN/Macro 3dB CIO

## Slide 5: UE Tput CDF (All UEs)
 | Uplink Throughput |  |  |  |  |  | Offloading Percentage
 | Mean | Gain | Median | Gain | 5% | Gain | (%)
 | (kbps) |  | (kbps) |  | (kbps) |  | 
Baseline | 244 |  | 215 |  | 75 |  | 37%
HetNet | 808 | 231% | 705 | 228% | 215 | 187% | 

## Slide 6: UE Tput CDF (Separate LPN and Macro UEs)

## Slide 7: UL UE Tput Fairness (All UEs)

## Slide 8: Average Cell RoT

## Slide 9: 37dBm LPN power 50% Hotspot UE dropping (60m radius) 4 LPN/Macro 0dB CIO

## Slide 10: UE Tput CDF (All UEs)
 | Uplink Throughput |  |  |  |  |  | Offloading Percentage
 | Mean | Gain | Median | Gain | 5% | Gain | (%)
 | (kbps) |  | (kbps) |  | (kbps) |  | 
Baseline | 244 |  | 215 |  | 75 |  | 49%
HetNet | 883 | 262% | 855 | 298% | 265 | 253% | 

## Slide 11: UE Tput CDF (Separate LPN and Macro UEs)

## Slide 12: UL UE Tput Fairness (All UEs)

## Slide 13: Average Cell RoT