## Slide 1: WF on LBT category 4 design for LAA
Huawei, Ericsson, CableLabs, Cisco, HiSilicon, Ruckus Wireless, Vodafone
3GPP TSG RAN WG1 Meeting #80bis R1-152383
Belgrade, Serbia, 20th - 24th April 2015
Agenda item: 7.2.4.2
Document for decision

## Slide 2: Working Assumption
If LAA is adopting a LBT category 4 scheme for DL transmission, it will be based on ETSI option B modified to a LBT category 4 scheme except for the following modifications that ensure fairness with Wi-Fi:
  The size of the LAA contention window is variable via dynamic exponential backoff or semi-static backoff between X and Y ECCA slots
    The value of X and Y is a configurable parameter
    FFS: which trigger and rate for adapting the size of the contention window
  Consider minimum ECCA slot size smaller than 20 µs
  The initial CCA (ICCA) can be configurable to be comparable to the defer periods of Wi-Fi (e.g., DIFS or AIFS)
    FFS: Conditions under which initial CCA is used
  When ECCA countdown is interrupted, a defer period (not necessarily the same as ICCA) is applied before transmission after channel becomes idle
    FFS: Continuing count down during defer period
  The defer period is configurable. It can be configured to be comparable to defer periods of Wi-Fi (e.g. DIFS or AIFS).
    FFS: A defer period configured to be zero.
    FFS: how matching is done when multiple UEs are scheduled in a subframe with different QoS, or when a transmission contains no PDSCH (e.g. DRS, CSI-RS), or when a transmission contains UL grants
  FFS: Relationship, if any, between contention window and maximum channel occupancy?
Discuss the values of all the above parameters at RAN1#81
FFS: Applicability of this to DRS
Adaptability of the energy detection threshold can be applied
Defer period: Minimum time that a node has to wait after the channel becomes idle before transmission, i.e., a node can transmit if the channel is sensed to be idle for ≥ defer period.
Companies are encouraged to provide evaluations at RAN1#81 for LBT category 4 schemes in accordance with the above