## Slide 1: WF on PUSCH-like new PUCCH format
NTT DOCOMO, INC.
R1-156124
3GPP TSG RAN WG1 #82bis
Malmo, Sweden, 5th – 9th October 2015
Agenda item 7.2.2.1.1

## Slide 2: Proposals on PUSCH-like new PUCCH format (1)
The PUSCH-like new PUCCH format is designed as follows:
  Alt. 1: No. of DMRS per slot is 2 for normal CP and is 1 for extended CP.
    For normal CP, DMRS is located on #1 and #6 SC-FDMA symbol of each slot.
    For extended CP, DMRS is located on #3 SC-FDMA symbol of each slot.
    Same DMRS symbol(s) generation procedure is applied as in PUCCH format 3.
  Alt. 2: No. of DMRS per slot is 1 for both CP cases.
    For both CP cases, DMRS is located on #3 SC-FDMA symbol of each slot.
    Same DMRS symbol(s) generation procedure is applied as in PUSCH.
      Cell-specific parameters Group-hopping-enabled, n(1)DMRS, and Dss are common between DMRSs for PUSCH and PUSCH-like new PUCCH format.
      UE-specific parameters Disable-sequence-group-hopping and activate-DMRS-with OCC for DMRS on PUSCH-like new PUCCH format are independently configured from those for DMRS on PUSCH.
      UE-specific parameters nRSID and Ncsh_DMRSID for DMRS on PUSCH-like new PUCCH format are independently configurable from those for DMRS on PUSCH.

## Slide 3: Proposals on PUSCH-like new PUCCH format (2)
The PUSCH-like new PUCCH format is designed as follows:
  Inter-slot FH is applied as in legacy PUCCHs, while it can be disabled by higher-layer.
  Shortened PUCCH format is supported.
  Transmit diversity is not supported in Rel. 13.
  For HARQ-ACK/SR only,
    4 PUCCH resources are configured by higher-layer, and one of them is indicated by ARI as for PUCCH format 3.

## Slide 4: Proposals on PUSCH-like new PUCCH format (３)
The PUSCH-like new PUCCH format is designed as follows:
  The PUCCH resource is represented by the following factors.
    Starting PRB index (0-109)
    CS index
      If 2 DMRS/slot is agreed, the CS index field ranges 0-4, and is used to determine cyclic shift value as in Table 5.5.2.2.1-4 of TS 36.211.
      If 1 DMRS/slot is agreed, the CS index field ranges 0-7, and is used to determine cyclic shift value as Cyclic Shift Field in uplink-related DCI format in Table 5.5.2.1.1-1 of TS36.211.
    [The number of PRBs]

## Slide 5: Proposals on PUSCH-like new PUCCH format (4)
The PUSCH-like new PUCCH format is designed as follows:
  For transmit power control of the PUSCH-like new PUCCH format,
    10log10(MPUCCH_PRB) is included with MPUCCH_PRB being the no. of PRBs.
    DF_PUCCH(F) is included with DF_PUCCH(F) is the PF-dependent power offset.
      For the DF_PUCCH(F), one of [8] values is configured by higher-layer.
      FFS: Exact values.
    If joint coding between HARQ-ACK/SR + P-CSI is supported,
      h-function is included, where the h-function is the power offset depending on the number of total UCI bits similar to legacy PUCCH format 3.
      FFS: Exact values.
    If separate coding between HARQ-ACK/SR + P-CSI is supported,
      FFS whether/how to introduce h-function.
      FFS whether existing PUSCH power control formula is applied.