## Slide 1: Rank 3-8 codebook -- summary of RAN1 proposals and performance
3GPP TSG RAN WG1 Meeting #83 R1-156791
Anaheim, USA, 16th – 20th October 2015
Agenda item: 7.2.4.3.1
Title: Rank 3-8 codebook -- summary of RAN1 proposals and performance
Document for: Discussion and Decision
Source: Samsung

## Slide 2
Rank 3-4 Codebook Proposals

## Slide 3: Summary
Companies | Proposal Types
Intel, LGE, Samsung/Ericsson/Docomo/CATT | k = 0,1,..,K-1 parameter to indicate orthogonal beam types K = 2: LGE, Samsung/Ericsson/Docomo/CATT Alt 1 K = 4: Intel K = 8: Samsung/Ericsson/Docomo/CATT Alt 2 Feedback k jointly with i1 (i1,1, i1,2)
Qualcomm, ALU/ASB, ZTE, Huawei/HiSilicon | No k parameter feedback Orthogonal beam type is indicated as part of normal i2 feedback Config parameter determines both beam group and orthogonal beam type
CMCC | 1D orthogonality in longer dim

## Slide 4: Summary
Companies | Rank 3 Codebook size for (N1,N2) = (4,2) and (O1,O2) = (8,8) |  |  |  |  |  |  |  |  |  |  | 
 | Config 1 (#bits) |  |  | Config 2 (#bits) |  |  | Config 3 (#bits) |  |  | Config 4 (#bits) |  | 
 | Total | (i1,1,i1,2,k) | i2 | Total | (i1,1,i1,2,k) | i2 | Total | (i1,1,i1,2,k) | i2 | Total | (i1,1,i1,2,k) | i2
Intel | 12 | (4,3,3) | 2 | 9 | (2,1,2) | 4 | 9 | (2,1,2) | 4 | 11 | (2,3,2) | 4
LGE | 12 | (5,4,1) | 2 | 8 | (2,1,1) | 4 | 8 | (2,1,1) | 4 | 8 | (2,1,1) | 4
Samsung/ Ericsson/ Docomo/CATT k = 0,1 | 11 | (5,4,1) | 1 | 10 | (3,2,1) | 4 | 9 | (2,2,1) | 4 | 10 | (2,3,1) | 4
Samsung/ Ericsson/ Docomo/CATT k = 0-7 | 13 | (5,4,3) | 1 | 12 | (3,2,3) | 4 | 11 | (2,2,3) | 4 | 12 | (2,3,3) | 4
Qualcomm | 12 | (5,4,0) | 2 | 10 | (3,3,0) | 4 | 9 | (2,3,0) | 4 | 9 | (2,3,0) | 4
ALU/ ASB | - | - | - | 11 | (4,3,0) | 4 | 11 | (4,3,0) | 4 | 11 | (4,3,0) | 4
ZTE | 13 | (5,4,0) | 4 | 7 | (2,1,0) | 4 | - | - | - | 9 | (2,3,0) | 4
Huawei/ HiSilicon | - | - | - | 9 | (4,1,0) | 4 | 7 | (2,1,0) | 4 | 9 | (2,3,0) | 4
CMCC | 11 | (5,4,0) | 2 | 9 | (3,2,0) | 4 | 9 | (3,2,0) | 4 | 9 | (3,2,0) | 4
Rank 4 i2 = Rank 3 i2 bits – 1 except ZTE proposal (Rank 4 i2 = Rank 3 i2)

## Slide 5: Rank 3-4 Codebook Proposals (R1-156390)
k parameter feedback with i1
Samsung/Ericsson/Docomo/CATT
Alt 1. Two values: k = 0,1
Alt 2. k = 0-7
Alternate Config 3

## Slide 6: Rank 3-4 Codebook Proposals (R1-156390) – Revision (R1-157427)
k parameter feedback with i1
Samsung/Ericsson/Docomo/CATT
Config | Old |  | New | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
Config | Old |  | New | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
With old parameters and (O1,O2) = (8,8), the effective oversampling factors are (2,2), (4,2), and (4,2) in two dimensions for Config 2, Config 3, and Config 4, respectively.
  Ex) For Config 2, (p1,p2) = (O1/2,O2/2) = (4,4), or the beam spacing is 4 for both dimensions, and hence the effective oversampling factor is (O1/p1,O2/p2) = (2,2).
With the new parameters:
  when O1=8 the effective oversampling factor is the same as legacy (i.e., 4), and;
  when O1=4 the effective oversampling factor is same as the configured one (i.e., 4).
  The effective oversampling factor = 2 results in performance loss when compared with effective oversampling factor = 4.
    Please see performance evaluation slides (Slide 14).
Revision shown in red box

## Slide 7: Rank 3-4 Codebook Proposals
Two options (k=0,1):
  Option 1: orthogonal beams in 1st domain
  Option 2 orthogonal beams in 2nd domain
W1 includes the feedback for option selection
k parameter feedback with i1
LGE

## Slide 8: Rank 3-4 Codebook Proposals
Grid of beams for rank 3 and 4 consists of two orthogonal beam groups (see Fig) selected by index k.
K | 0 | 1 | 2 | 3
Beam group pair | (0,1) | (0,2) | (0,3) | (1,2)
Δ | k |  |  | 
 | 1 | 2 | 3 | 4
δ1,1 | O1 | 0 | O1 | O1
δ1,2 | 0 | O2 | O2 | 0
δ2,1 | 0 | 0 | 0 | 0
δ2,2 | 0 | 0 | 0 | O2
k parameter feedback with i1
Intel

## Slide 9: Rank 3-4 Codebook Proposals
p1= O1/4 is used for beam progression in longer dim
p2 = O2, to select an orthogonal beam in shorter dim
No k parameter feedback
Qualcomm

## Slide 10: Rank 3-4 Codebook Proposals
16 ports
8,12 ports
4 orthogonal beams selected based on Config parameter
No k parameter feedback
ALU/ASB

## Slide 11: Rank 3-4 Codebook Proposals
7 orthogonal beam pairs
For each leading beam, 2 orthogonal beams
1 in longer dim
1 in shorter dim
For each leading beam, 2 orthogonal beams
Both in longer dim
Legacy 8-Tx:
W3 = (0,0,O1), (O1,O1,0)
\tilde W3 = (0,O1,0), (O1,0,O1)
Proposed:
W3 = (0,0,O1), (0,0,O2)
\tilde W3 = (0,O1,0), (0,O2,0)
No k parameter feedback
ZTE

## Slide 12: Rank 3-4 Codebook Proposals
Config 2
Config 3
Config 4
Config 2: orthogonality in shorter dim
Config 4: orthogonality in longer dim
Config 3: orthogonality in shorter, longer and diagonal dim
No k parameter feedback
Huawei/HiSilicon, Alt 1

## Slide 13: Rank 3-4 Codebook Proposals
No Config parameter
Rank 3/4 beam combination are: {[ b0, b2], [ b1, b3], [b4, b6], [b5, b7], [ b0, b4], [ b2, b6], [ b0, b5], [ b2, b7]}
No k parameter feedback
Huawei/HiSilicon, Alt 2

## Slide 14
Performance Comparison
S1 | Samsung/Ericsson/CATT/DOCOMO (k=0-1, Config 3: checker-board)
S2 | Samsung/Ericsson/CATT/DOCOMO (k=0-7, Config 3: checker-board)
S3 | Samsung/Ericsson/CATT/DOCOMO (k=0-1, Config 3: alternate proposal)
S4 | Samsung/Ericsson/CATT/DOCOMO (k=0-7, Config 3: alternate proposal)
Z | ZTE
L | LGE
H | Huawei/HiSilicon
Q | Qualcomm
C | CMCC
A | ALU/ASB
I | Intel

## Slide 15: Results for R1-156390 and its Revision R1-157427
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
1.5 | (4,2,2) | (8,8) | 20% | SU | UMa-200m
 | Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
R1-156390 | S1 | 59.49 | 52.61 | 18.49 | 100.00% | 100.00% | 100.00%
 | S2 | 59.49 | 51.74 | 18.94 | 100.01% | 98.35% | 102.43%
 | S3 | 59.35 | 52.10 | 19.00 | 99.77% | 99.03% | 102.71%
 | S4 | 59.65 | 52.51 | 19.08 | 100.27% | 99.82% | 103.19%
R1-1567427 | S1 | 61.51 | 54.61 | 20.41 | 103.41% | 103.81% | 110.37%
 | S2 | 62.14 | 55.33 | 20.29 | 104.45% | 105.18% | 109.69%
 | S3 | 61.50 | 54.81 | 20.35 | 103.39% | 104.18% | 110.05%
 | S4 | 61.88 | 54.21 | 20.71 | 104.02% | 103.04% | 111.98%
 | Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
R1-156390 | S1 | 58.17 | 52.49 | 20.36 | 100.00% | 100.00% | 100.00%
 | S2 | 58.35 | 52.05 | 19.68 | 100.30% | 99.17% | 96.64%
 | S3 | 58.18 | 52.16 | 20.01 | 100.02% | 99.38% | 98.28%
 | S4 | 58.43 | 52.00 | 19.78 | 100.45% | 99.07% | 97.17%
R1-1567427 | S1 | 60.45 | 55.71 | 21.62 | 103.92% | 106.13% | 106.20%
 | S2 | 60.96 | 55.09 | 20.94 | 104.80% | 104.96% | 102.83%
 | S3 | 60.68 | 55.85 | 20.64 | 104.31% | 106.41% | 101.36%
 | S4 | 60.75 | 55.15 | 21.36 | 104.43% | 105.07% | 104.93%
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
1.6 | (4,2,2) | (8,8) | 20% | SU | UMi-2GHz
Revised (s1,s2) and (p1,p2) parameters show performance gain
Revised parameters are used in S1-S4 proposals in the rest of the SLS results (in upcoming slides)

## Slide 16: 16 port – Wide: SLS Results
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
1.5 | (4,2,2) | (8,8) | 20% | SU | UMa-200m
Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
S1 | 61.51 | 54.61 | 20.41 | 100.00% | 100.00% | 100.00%
S2 | 62.14 | 55.33 | 20.29 | 101.01% | 101.33% | 99.38%
S3 | 61.50 | 54.81 | 20.35 | 99.98% | 100.36% | 99.71%
S4 | 61.88 | 54.21 | 20.71 | 100.59% | 99.26% | 101.46%
Z | 59.63 | 52.89 | 20.00 | 96.94% | 96.84% | 97.99%
L | 59.52 | 52.19 | 18.95 | 96.75% | 95.56% | 92.82%
H | 58.94 | 51.68 | 18.91 | 95.82% | 94.64% | 92.64%
Q | 61.66 | 54.44 | 19.92 | 100.24% | 99.69% | 97.57%
C | 58.94 | 50.58 | 20.50 | 95.81% | 92.62% | 100.44%
A | 60.11 | 53.65 | 20.40 | 97.71% | 98.24% | 99.95%
I | 60.04 | 52.37 | 20.10 | 97.60% | 95.91% | 98.45%
Chart: 
| 1 | 1.0133000000000001 | 0.96840000000000004 | 0.9556 | 0.94640000000000002 | 0.99690000000000001 | 0.92620000000000002 | 0.98240000000000005 | 0.95909999999999995 | 1.0036 | 0.99260000000000004
Y-Values | 1 | 0.9938 | 0.9799 | 0.9282 | 0.9264 | 0.9757 | 1.0044 | 0.9995 | 0.9845 | 0.9971 | 1.0146
50% UPT 
5% UPT 
Chart: 
| Rank 1 | Rank 2 | Rank 3 | Rank 4
S1 | 0.016057 | 0.10071 | 0.2274 | 0.65583
S2 | 0.010932 | 0.089708 | 0.23256 | 0.6668
S3 | 0.014455 | 0.10189 | 0.22954 | 0.65411
S4 | 0.011104 | 0.095478 | 0.22552 | 0.6679
Z | 0.013184 | 0.121 | 0.22374 | 0.64207
L | 0.013423 | 0.11709 | 0.25292 | 0.61657
H | 0.0084251 | 0.11845 | 0.25329 | 0.61983
Q | 0.0092451 | 0.091611 | 0.23732 | 0.66182
C | 0.015533 | 0.12586 | 0.24256 | 0.61605
A | 0.0086911 | 0.10282 | 0.24399 | 0.6445
I | 0.0098264 | 0.1256 | 0.24846 | 0.61612
Rank distribution

## Slide 17: 16 port – Wide: SLS Results
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
1.6 | (4,2,2) | (8,8) | 20% | SU | UMi-2GHz
Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
S1 | 60.45 | 55.71 | 21.62 | 100.00% | 100.00% | 100.00%
S2 | 60.96 | 55.09 | 20.94 | 100.85% | 98.89% | 96.83%
S3 | 60.68 | 55.85 | 20.64 | 100.38% | 100.27% | 95.44%
S4 | 60.75 | 55.15 | 21.36 | 100.49% | 99.00% | 98.80%
Z | 57.58 | 51.34 | 19.94 | 95.25% | 92.16% | 92.19%
L | 59.72 | 54.17 | 20.17 | 98.79% | 97.24% | 93.26%
H | 58.75 | 52.41 | 18.42 | 97.18% | 94.09% | 85.19%
Q | 60.33 | 54.95 | 20.21 | 99.81% | 98.64% | 93.46%
C | 56.71 | 51.63 | 20.16 | 93.81% | 92.68% | 93.22%
A | 59.09 | 53.31 | 20.95 | 97.75% | 95.69% | 96.87%
I | 59.11 | 53.50 | 21.20 | 97.79% | 96.05% | 98.04%
Chart: 
| 1 | 0.9889 | 0.92159999999999997 | 0.97240000000000004 | 0.94089999999999996 | 0.98640000000000005 | 0.92679999999999996 | 0.95689999999999997 | 0.96050000000000002 | 1.0026999999999999 | 0.99
Y-Values | 1 | 0.9683 | 0.9219 | 0.9326 | 0.8519 | 0.9346 | 0.9322 | 0.9687 | 0.9804 | 0.9544 | 0.988
50% UPT 
5% UPT 
Chart: 
| Rank 1 | Rank 2 | Rank 3 | Rank 4
S1 | 0.014094 | 0.12963 | 0.27922 | 0.57706
S2 | 0.011325 | 0.12012 | 0.28284 | 0.58572
S3 | 0.014016 | 0.13033 | 0.28087 | 0.57479
S4 | 0.013006 | 0.12255 | 0.2839 | 0.58054
Z | 0.013987 | 0.14607 | 0.28631 | 0.55363
L | 0.012869 | 0.13955 | 0.29488 | 0.5527
H | 0.013275 | 0.15807 | 0.28027 | 0.54839
Q | 0.012519 | 0.12414 | 0.29455 | 0.56878
C | 0.013049 | 0.17787 | 0.28005 | 0.52903
A | 0.0089907 | 0.14317 | 0.27526 | 0.57257
I | 0.0087749 | 0.17099 | 0.27908 | 0.54115
Rank distribution

## Slide 18: 16 port – Tall: SLS Results
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
1.5 | (2,4,2) | (8,8) | 20% | SU | UMa-200m
Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
S1 | 56.49 | 49.60 | 19.65 | 100.00% | 100.00% | 100.00%
S2 | 57.00 | 50.09 | 19.55 | 100.89% | 100.99% | 99.49%
S3 | 56.92 | 49.07 | 19.81 | 100.75% | 98.95% | 100.83%
S4 | 57.11 | 49.17 | 19.23 | 101.09% | 99.14% | 97.88%
Z | 54.05 | 45.86 | 17.75 | 95.67% | 92.47% | 90.34%
L | 55.49 | 49.15 | 19.45 | 98.22% | 99.10% | 98.96%
H | 53.72 | 46.51 | 17.71 | 95.09% | 93.77% | 90.14%
Q | 56.50 | 48.67 | 18.80 | 100.01% | 98.12% | 95.68%
C | 52.90 | 45.09 | 19.14 | 93.63% | 90.91% | 97.39%
A | 52.14 | 44.49 | 18.08 | 92.29% | 89.70% | 92.02%
I | 56.76 | 48.73 | 19.61 | 100.47% | 98.26% | 99.79%
Chart: 
| 1 | 1.0099 | 0.92469999999999997 | 0.99099999999999999 | 0.93769999999999998 | 0.98119999999999996 | 0.90910000000000002 | 0.89700000000000002 | 0.98260000000000003 | 0.98950000000000005 | 0.99139999999999995
Y-Values | 1 | 0.9949 | 0.9034 | 0.9896 | 0.9014 | 0.9568 | 0.9739 | 0.9202 | 0.9979 | 1.0083 | 0.9788
50% UPT 
5% UPT 
Chart: 
| Rank 1 | Rank 2 | Rank 3 | Rank 4
S1 | 0.017349 | 0.12252 | 0.27053 | 0.5896
S2 | 0.016693 | 0.11987 | 0.27208 | 0.59136
S3 | 0.017928 | 0.1249 | 0.26539 | 0.59178
S4 | 0.017766 | 0.12501 | 0.26701 | 0.59021
Z | 0.019257 | 0.14532 | 0.27396 | 0.56147
L | 0.015636 | 0.13826 | 0.26999 | 0.57611
H | 0.013595 | 0.14346 | 0.27518 | 0.56777
Q | 0.014314 | 0.11672 | 0.27687 | 0.59209
C | 0.01792 | 0.16868 | 0.28357 | 0.52983
A | 0.015994 | 0.14377 | 0.29814 | 0.5421
I | 0.014363 | 0.14729 | 0.25886 | 0.57949
Rank distribution

## Slide 19: 16 port – Tall: SLS Results
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
1.6 | (2,4,2) | (8,8) | 20% | SU | UMi-2GHz
Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
S1 | 57.77 | 51.08 | 20.76 | 100.00% | 100.00% | 100.00%
S2 | 58.10 | 52.04 | 20.92 | 100.57% | 101.86% | 100.74%
S3 | 57.89 | 50.52 | 21.36 | 100.22% | 98.90% | 102.89%
S4 | 57.95 | 51.51 | 20.89 | 100.32% | 100.83% | 100.62%
Z | 55.98 | 48.38 | 20.74 | 96.90% | 94.70% | 99.88%
L | 55.27 | 48.28 | 20.40 | 95.67% | 94.50% | 98.27%
H | 54.70 | 47.43 | 19.41 | 94.69% | 92.84% | 93.50%
Q | 57.87 | 51.00 | 21.39 | 100.18% | 99.83% | 103.00%
C | 55.17 | 47.09 | 20.77 | 95.50% | 92.18% | 100.02%
A | 55.40 | 47.75 | 20.71 | 95.91% | 93.48% | 99.76%
I | 56.54 | 50.06 | 21.25 | 97.88% | 98.00% | 102.34%
Chart: 
| 1 | 1.0185999999999999 | 0.94699999999999995 | 0.94499999999999995 | 0.9284 | 0.99829999999999997 | 0.92179999999999995 | 0.93479999999999996 | 0.98 | 0.98899999999999999 | 1.0083
Y-Values | 1 | 1.0074 | 0.9988 | 0.9827 | 0.935 | 1.03 | 1.0002 | 0.9976 | 1.0234 | 1.0289 | 1.0062
50% UPT 
5% UPT 
Chart: 
| Rank 1 | Rank 2 | Rank 3 | Rank 4
S1 | 0.01059 | 0.15499 | 0.30673 | 0.52769
S2 | 0.009147 | 0.15011 | 0.30338 | 0.53736
S3 | 0.0095268 | 0.15096 | 0.3049 | 0.53461
S4 | 0.010461 | 0.14858 | 0.30145 | 0.53951
Z | 0.0082276 | 0.1755 | 0.28931 | 0.52696
L | 0.01251 | 0.17206 | 0.30732 | 0.50811
H | 0.0089266 | 0.18446 | 0.28471 | 0.52191
Q | 0.0078514 | 0.15267 | 0.29991 | 0.53958
C | 0.011895 | 0.20421 | 0.3059 | 0.478
A | 0.0092357 | 0.1723 | 0.30598 | 0.51248
I | 0.0089211 | 0.18656 | 0.29161 | 0.5129
Rank distribution

## Slide 20: Conclusion
Based on simulation results, we can observe that
  Performance of S1, i.e., Samsung/Ericsson/CATT/DOCOMO with k = 0,1 and Config 3 = checker-board is the best overall when compared to other proposals.
  The performance difference between k = 0,1 and k=0,1,..7, i.e., (S1,S2), and (S3,S4) are marginal.
  The indication of orthogonal beam type with i2 shows performance loss in some proposals and only marginal gain in other proposals. Therefore, the orthogonal beam type should be indicated WB together with (i1,1,i1,2), for example.
Based on the codebook size summary in Slide 4, we can observe that for Config 1, the total number of PMI feedback bits can be
  More than 11 in case of Intel, LGE, and Samsung/Ericsson/Docomo/CATT with k=0-7 proposals
    Note: 11 bits is the limit of PUCCH feedback, and
  Equal to 11 in case of Samsung/Ericsson/Docomo/CATT with k=0,1 proposal.
Proposal: Adopt a rank 3-4 codebook proposed in R1-157427 as Rel-13 class A rank 3-4 codebook.

## Slide 21
Rank 5-8 Codebook Proposals

## Slide 22: Summary
Proposal Types | Companies
Legacy 8-Tx type (no i2 feedback) Config parameter used for indicating an orthogonal beam type | Samsung/Ericsson/Docomo/CATT, ALU/ASB, and CMCC, and are aligned ALU/ASB Config 2,3,4 for 16 ports Config 2 for 8,12 ports CMCC Config 2,4 for 12, 16 ports Samsung/Ericsson/Docomo/CATT Config 2,3,4 for 12, 16 ports
i2 (1-bit) is used for indicating an orthogonal beam type between Square, and 1D orthogonal beams | Huawei/HiSilicon
i2 (2-bit) used for leading beam selection within a beam group of 4 beams Config parameter to select 4 beams Orthogonal beam type: square | LGE

## Slide 23: Summary
Companies | Rank 5-8 Codebook size for (N1,N2) = (4,2) and (O1,O2) = (8,8) |  |  |  |  |  |  |  |  |  |  | 
 | Config 1 (#bits) |  |  | Config 2 (#bits) |  |  | Config 3 (#bits) |  |  | Config 4 (#bits) |  | 
 | Total | (i1,1,i1,2) | i2 | Total | (i1,1,i1,2) | i2 | Total | (i1,1,i1,2) | i2 | Total | (i1,1,i1,2) | i2
Samsung/ Ericsson/ Docomo/CATT | 9 | (5,4) | 0 | 7 | (4,3) | 0 | 7 | (4,3) | 0 | 7 | (4,3) | 0
ALU/ ASB | - | - | - | 5 | (3,2) | 0 | 5 | (3,2) | 0 | 5 | (3,2) | 0
CMCC | - | - | - | 5 | (3,2,0) | 0 | - | - | - | 5 | (3,2,0) | 0
Huawei/ HiSilicon | 1-5 | (0-2,0-2) | 1 | 1-5 | (0-2,0-2) | 1 | 1-5 | (0-2,0-2) | 1 | 1-5 | (0-2,0-2) | 1
LGE | 9 | (5,4) | 0 | 5 | (2,1) | 2 | 5 | (2,1) | 2 | 5 | (2,1) | 2

## Slide 24: Rank 5-8 Codebook Proposals (R1-156390)
Legacy 8-Tx type (no i2 feedback)
Samsung/Ericsson/Docomo/CATT
16 ports
Rank 5-6
Rank 7-8
12 ports
0-bit i2
Config 3 beam pattern is different from other companies.
Config 2 beam numbering is different from other companies.

## Slide 25: Rank 5-8 Codebook Proposals (R1-156390) - Revision (R1-157427)
Legacy 8-Tx type (no i2 feedback)
Samsung/Ericsson/Docomo/CATT
Type | Configuration |  |  |  |  |  | 
Config= 1, 2, 3, 4 | N1=N2 | O1 | 0 | O1 | O2 | 0 | O2
Type | Configuration |  |  |  |  |  | 
Config= 1, 2, 3, 4 | N1=N2 | O1 | 0 | O1 | O2 | 0 | O2
 |  |  |  |  |  | 12 ports |  | 16 ports | 
 | Antenna configuration |  |  |  |  |  |  |  | 
Config = 4 | N1≥N2 | O1 | 0 | 2O1 | 0 | 0 | O2 | 3O1 | 0
 | N1<N2 | 0 | O2 | 0 | 2O2 | O1 | 0 | 0 | 3O2
Config =3 | N1≥N2 | O1 | 0 | 2O1 | O2 | O1 | O2 | 3O1 | O2
 | N1<N2 | 0 | O2 | O1 | 2O2 | O1 | O2 | O1 | 3O2
Config = 1, 2 | Both | O1 | 0 | O1 | O2 | 0 | O2 | 0 | O2
 |  |  |  |  |  | 12 ports |  | 16 ports | 
 | Antenna configuration |  |  |  |  |  |  |  | 
Config = 4 | N1≥N2 | O1 | 0 | 2O1 | 0 | 0 | O2 | 3O1 | 0
 | N1<N2 | 0 | O2 | 0 | 2O2 | O1 | 0 | 0 | 3O2
Config =3 | N1≥N2 | O1 | 0 | 2O1 | O2 | O1 | O2 | 3O1 | O2
 | N1<N2 | 0 | O2 | O1 | 2O2 | O1 | O2 | O1 | 3O2
Config = 1, 2 | Both | O1 | 0 | O1 | O2 | 0 | O2 | 0 | O2
8 port: (N1,N2)=(2,2)
(s1,s2) parameters:
Revision shown in red box
(s1,s2) = (1,1) for Config 1; and
(s1,s2) = for Config 2,3,4
Revision
For 12 ports:

## Slide 26: Rank 5-8 Codebook Proposals
16 ports
8,12 ports
Rank 5-6
Rank 7-8
Rank 5-6
Rank 7-8
0-bit i2
Legacy 8-Tx type (no i2 feedback)
ALU/ASB
Legacy 8-Tx type (no i2 feedback)
CMCC
Same beam numbering as ALU/ASB, CMCC, and Huawei/HiSilicon

## Slide 27: Rank 5-8 Codebook Proposals
Rank 5-6
Rank 7-8
1-bit i2
1-bit i2 feedback
Huawei/HiSilicon
Same beam numbering as ALU/ASB, CMCC, and Huawei/HiSilicon

## Slide 28: Rank 5-8 Codebook Proposals
Config parameter is used for beam grouping (similar to rank 1-2)
Example beam grouping for Config 3
Rank 5-6
Rank 7-8
2-bit i2
2-bit i2 feedback
LGE
Same beam numbering as ALU/ASB, CMCC, and Huawei/HiSilicon

## Slide 29: Conclusion
Based on these proposals, the following should be the design principle of rank 5-8 codebook:
  Follow legacy Rel10 8-Tx design: no i2 feedback
    Aligned with majority of other companies
  Use Config parameter to configure an orthogonal beam type
Proposal: Adopt the rank 5-8 codebook proposal in R1-157427 as Rel-13 class A rank 5-8 codebook.