## Slide 1: WF on ED Threshold for LAA Frequency Reuse
Samsung, ZTE
R1-157708
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th – 22nd November 2015
Agenda item 6.2.3.1

## Slide 2: Background
We have the following agreements about frequency reuse support
At least the following options can be further studied to enable improved freq. reuse for LBE for DL LAA.
  CCA threshold adaptation
  TX start timing alignment
  Signal subtraction from ED or modified ED (excluded from Rel-13 @ RAN1#82)
  Combinations of those options or other alternatives are not precluded

## Slide 3: Proposal (1/2)
When the absence of WiFi is guaranteed by regulation, the following ED threshold adaptation should be applied at eNB,
  Step1: If the eNB identifies the presence of inter-operator LAA signal, the eNB uses maximum ED threshold 1 (Th1)
  Step2: Else the eNB uses maximum ED threshold 2 (Th2)
Note1): Th1<Th2, FFS: Tmax<Th2≤Min[Tmax+10dB, Tregional_max] OR Th2=Tmax
Note2): When doing step1 or not, is up to eNB implementation

## Slide 4: Proposal (2/2)
How to identify the presence of inter-operator LAA signal:
  Opt1) by monitoring muted REs in the reservation signal Opt2) by monitoring muted REs in the PDSCH
  Note on specification impact: muting pattern; To opt1); Necessity of a restriction of leaving some REs blank on reservation signal transmission To opt2); Necessity of a rate matching for scheduled UE