## Slide 1: WF on evaluation methodology for latency reduction
Ericsson
3GPP TSG RAN WG1 #83 R1-157732
Anaheim, USA
15th – 22nd November 2015
Agenda item: 6.2.9.1
Document for decision

## Slide 2: Background
According to the SID, the following aspect should be studied in RAN1
  From RAN1#83: TTI shortening and reduced processing times [RAN1]:
    Assess specification impact and study feasibility and performance of TTI lengths between 0.5ms and one OFDM symbol, taking into account impact on reference signals and physical layer control signaling
    backwards compatibility shall be preserved (thus allowing normal operation of pre-Rel 13 UEs on the same carrier);
RAN1 should perform evaluations in order to understand the feasibility and performance of TTI shortening
  System-level evaluation is needed to identify the technology potential of TTI shortening
  Link-level evaluation is needed to compare the performance of different physical layer design options

## Slide 3: Proposal 1: simulation assumptions for system-level evaluations
Parameter | Assumptions
Layout | Both 7 and 19 Macro eNBs can be used, 3 sectors per site; Small cell scenario 2a as optional
System bandwidth per carrier | 10MHz, 20MHz
Carrier frequency | 2GHz
Inter-site distance | 500m
Total BS TX power (Ptotal per carrier) | 46dBm
TTI length | 1/2/3(4)/7 symbols; other TTI lengths provided by companies
Fast UL Access schemes | Provided by companies
RS and control signaling overhead | Details of RS and control signaling overhead provided by companies
TBS determination | Scalable with TTI length as baseline, according to available REs considering RS and control signaling overhead
HARQ RTT | Scalable with TTI length as baseline; HARQ RTT not scaled with TTI provided by individual company
Scheduler | Proportional fairness
Distance-dependent path loss | ITU UMa[referring to Table B.1.2.1-1 in TR36.814], with 3D distance between an eNB and a UE
Penetration | For outdoor UEs:0dB
 | For indoor UEs: 20dB+0.5din (din: independent uniform random value between [ 0, min(25,d) ] for each link)
Shadowing | ITU UMa according to Table A.1-1 of 36.819 with 3D distance for shadowing correlation distance

## Slide 4
Antenna pattern | 3D, referring to TR36.819
Antenna Height: | 25m
UE antenna Height | 1.5m
Antenna gain + connector loss | 17 dBi
Antenna gain of UE | 0 dBi
Fast fading channel between eNB and UE | ITU UMa according to Table A.1-1 of 36.819
Antenna configuration | 2Tx(eNB) <8Tx(eNB) (optional)>, 2Rx(UE), Cross-polarized
Number of UEs | 10 UEs per macro cell
UE dropping | Randomly and uniformly dropped throughout the macro geographical area. 20% UEs are outdoor and 80% UEs are indoor.
Traffic model | FTP download model 3, File size [100 kB, 500kB, 1 MB, 5MB], Traffic load [20%, 40% 60%]
CSI report period | 10 TTIs between two consecutive reports
CSI report delay | 6 TTIs

## Slide 5
TCP models | TCP Reno model (RFC 2581) - SSThresh 65535 Bytes - Initial window size 1460 Bytes - Max segment size 1460 Bytes
UE receiver | MMSE-IRC; other UE receiver provided by companies
UE noise figure | 9dB
UE speed | 3km/h, 60km/h, 120km/h, 120km/h
Network synchronization | Synchronized
Core, transport and internet network delay | 0ms, 6ms, 10ms
Performance metrics | Mean, 5%, 50% and 95% user perceived throughput Mean, 5%, 50% and 95% user packet delay
    User perceived throughput (UPT) is the average of all its file throughputs
  File throughput = file size/time needed to download the file
    Time needed to download the file starts when the packet is received in the transmit buffer, and ends when the last bit of the packet is correctly delivered to the receiver
  Unfinished files are not incorporated in the UPT calculation.
    User packet delay is the average of all its file delays
      File delay is the time needed to download the file as described above

## Slide 6: Proposal 2: Link-level simulation assumptions for shortened PDSCH
Parameter | Value
Carrier frequency | 2 GHz
System bandwidth | 10 MHz, 20MHz
TTI length | 1/2/3(4)/7 symbols, 1ms as baseline. other TTI lengths provided by companies
Fast UL Access schemes | Provided by companies
Allocated bandwidth | 25 PRBs, 50 PRBs
Channel model | EPA 5Hz, EVA70100Hz, ETU300Hz EPA, EVA, ETU with 3km/h, 60km/h
Antenna configuration | 2Tx(eNB), 2Rx(UE), 8Tx(eNB) optional
Antenna correlation | Uncorrelated
Legacy PDCCH region | 2 OFDM symbols
CP length | Normal
Transmission mode | TM4, TM9
RS configuration | TM4: 2 CRS ports; TM9: 2CRS ports, legacy DMRS pattern for 7 symbols; Detailed DMRS pattern provided by companies for 1/2/3(4) symbols
Receiver type | MMSE-IRC; other UE receiver provided by companies
Channel estimation | Practical
Rank adaptation | Fixed Rank1 provided by companies
Link adaptation | Enabled Disabled provided by companies
Modulation and code rate | 64QAM 5/6, 16QAM 3/4, QPSK 1/3; others provided by companies
PMI | Fixed to the first codebook
TBS detemination | Scale TBS size with TTI length according to available REs considering RS overhead
HARQ retransmission | Provided by companies
Performance metrics | BLER, throughput, MSE of channel estimation (optional)

## Slide 7: Proposal 3: Link-level simulation assumptions for shortened PUSCH
Parameter | Value
Carrier frequency | 2 GHz
System bandwidth | 10 MHz, 20MHz
TTI length | 1/2/3(4)/7 symbols, 1ms as baseline. other TTI lengths provided by companies
Allocated bandwidth | 25 PRBs, 50 PRBs
Channel model | EPA 5Hz, EVA70100Hz, ETU300Hz EPA, EVA, ETU with 3km/h, 60km/h
Antenna configuration | 1Tx(UE), 2Rx(eNB), 8Rx(eNB) as optional
Antenna correlation | Uncorrelated
CP length | Normal
Transmission mode | TM1
DMRS configuration | Detailed DMRS pattern provided by companies
Receiver type | MMSE-IRC; other UE receiver provided by companies
Channel estimation | Practical
Link adaptation | Enabled Disabled provided by companies
Modulation and code rate | 64QAM 5/6, 16QAM 3/4, QPSK 1/3; others provided by companies
TBS detemination | Scale TBS size with TTI length according to available REs considering RS overhead
HARQ retransmission | Provided by companies
Performance metrics | BLER, throughput, MSE of channel estimation (optional)

## Slide 8: Proposal 4: Link-level simulation assumptions for shortened (E)PDCCH
Parameter | Value
Carrier frequency | 2 GHz
System bandwidth | 10 MHz, 20MHz
TTI length | 1/2/3(4)/7 symbols, 1ms as baseline. other TTI lengths provided by companies
Channel model | EPA 5Hz, EVA70100Hz, ETU 300 EPA, EVA, ETU with 3km/h, 60km/h
Antenna configuration | 2Tx(eNB), 2Rx(UE)
Payload size | 40bits, 70bits as starting point; others provided by companies
CP length | Normal
Shortened PDCCH design | Details provided by companies
Receiver type | MMSE-IRC; other UE receiver provided by companies
Channel estimation | Practical
Performance metrics | BLER

## Slide 9: Proposal 5: Link-level simulation assumptions for shortened PUCCH
Parameter | Value
Carrier frequency | 2 GHz
System bandwidth | 10 MHz, 20MHz
TTI length | 2/3(4)/7 symbols, 1 symbol as optional other TTI lengths provided by companies
Channel model | EPA 5Hz, EVA70100Hz, ETU 300 EPA, EVA, ETU with 3km/h, 60km/h
Antenna configuration | 1Tx(UE), 2Rx(eNB)
CP length | Normal
Shortened PUCCH design | Details provided by companies
Receiver type | MMSE-IRC; others provided by companies
Channel estimation | Practical
Performance metrics | For HARQ-ACK: ACK missed detection probability (1%), NACK-to-ACK error probability (0.1%); DTX-to-ACK probability 1%; For CQI: Probability of CQI block error ≤ 1%