## Slide 1: WF on Ych for common messages
Ericsson, Fujitsu, Nokia Networks
R1-157857
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.2

## Slide 2: Proposal
Use the following Ych value for M-PDCCH/PDSCH for paging and MTC-SIB other than SIB1bis:
  If ‘Downlink frequency hopping interval in CE mode B’ is signaled in SIB1bis,
    Use Ych = ‘Downlink frequency hopping interval in CE mode B’
  Otherwise,
    Use Ych = ‘Downlink frequency hopping interval in CE mode A’
Use the following Ych values for M-PDCCH/PDSCH/PUSCH for RAR/Msg3/Msg4:
  In case PRACH CE level 0 or 1 is used for the last PRACH attempt,
    For M-PDCCH/PDSCH, use Ych = ‘Downlink frequency hopping interval in CE mode A’
    For PUSCH, use Ych = ‘Uplink frequency hopping interval in CE mode A’
  In case PRACH CE level 2 or 3 is used for the last PRACH attempt,
    For M-PDCCH/PDSCH, use Ych = ‘Downlink frequency hopping interval in CE mode B’
    For PUSCH, use Ych = ‘Uplink frequency hopping interval in CE mode B’