## Slide 1: WF on remaining issues of random access procedure
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #83 R1-157866
Anaheim, USA, 15 - 22 November, 2015
Agenda Item: 6.2.1.10

## Slide 2: Proposal for NB for M-PDCCH of RAR
Background [RAN1 #83 agreements]
  When more than one narrowband is configured for M-PDCCH for RAR for a PRACH repetition level,
    The narrowband is selected based on the PRACH preamble index (implicit mapping)
Proposal
When two narrowbands are configured for M-PDCCH for RAR for a PRACH repetition level:
  For even/odd preamble index, the M-PDCCH narrowband is the configured first/second narrowband

## Slide 3: Proposals for Msg3/Mg4
Background [RAN1 #83 agreements]
The narrowband index of M-PDCCH for Msg3 re-transmission or Msg4 transmission is determined by down-selecting one of the following (no additional higher-layer impact)
  Alt 1: implicitly derived by the preamble index of the last successful PRACH attempt
  Alt 2: indicated in RAR using 2-bit, as part of the RAR UL grant
  Proposal:
  The narrowband index of M-PDCCH for Msg3 re-transmission or Msg4 transmission is determined by :
  Alt 1: implicitly derived by the preamble index of the last successful PRACH attempt