## Slide 1: WF on dynamic blockage
Qualcomm, Intel, Samsung, Ericsson, …
R1-165462
3GPP TSG RAN1 #85
Nanjing, China, May 23 - 27, 2016
Agenda Item: 7.2.3.1

## Slide 2: Background - I
In R1-161150, the following working assumption is agreed:
  The blockage caused by the static objects and moving objects such as human body and vehicle is such that the blockage attenuation generally increases with frequency.
Further, in R1-161142 the following underlined agreements are also relevant towards the blockage modeling.
  Complexity in terms of description, generating channel coefficients, development complexity and simulation time should be considered.
  The model should be consistent in space, time and frequency.
Further, based on the agreed WF proposals R1-161739 and R1-163473, we have the following additional details on:
  Number of blockers
  Sizes of blocking regions
  Attenuation calculation
  Spatially/temporally consistent blocking model

## Slide 3: Background - II
The following flow is used for channel generation
Note:
  The blockage does not change LOS/NLOS state of a link.
  Temporal variability is on-demand, blockage modeling is an add-on feature.
  Two options (Option A and Option B) are provided to model blockage.

## Slide 4: WF Proposal (Option A) – I
Option A proposes a stochastic geometric model for human and vehicle blocking
Proposal 1: The blockers are modeled as (multiple) angular blocking regions as applied to the AoA/ZoA around the UE.
  Blockage modeling is an optional feature – it can be turned on in InH, UMi, UMa or RMa scenarios to consider the effect of human or vehicular blockage.
Proposal 2: One of the angular blocking regions represents self-blocking (i.e. human/hand holding the UE). This blocking region is not spatially consistent and UE specifically generated.
  This is an optional step.
Proposal 3: The angles and sizes of the angular blocking region (non self-blocking) are generated on a per UE basis according to a statistical process.
  The center of the blocking region is uniformly chosen in the azimuth angle and is fixed in elevation at 90o.
  Size of the blocking region is x degrees in azimuth and y degrees in elevation, where x and y are constants, provided in the following table.

## Slide 5: WF Proposal (Option A) – II
Proposal 4: On number of angularly blocked regions (excluding self-blocking)
  The total number of angularly blocked regions K = 5. (Of these, 1 is self-blocking and 4 are other blockers).
Proposal 5:
  Attenuation is based on a formula describing modified knife edge model
  where
  and
  r is the distance between UE and blocker
  The appropriate signs ( within the atan(.) term) in F(.) is from R1-164193.
Table for Proposals 3, 4 and 5
 | xk | ψk | yk | θk | Loss (in dB) InH | Loss (in dB) UMi | Loss (in dB) UMa | Loss (in dB) RMa
k = 1 (Portrait) | 120o | 260o | 80o | 100o | 30 | 30 | 30 | 30
k = 1 (Landscape) | 160o | 40o | 75o | 110o | 30 | 30 | 30 | 30
k = 2, …, 5 | 2.5o | Uniform in [0o, 360o) | 15o | 90o | Computed using formula |  |  | 
 |  |  |  |  | r = 2 | r = 10 |  | 

## Slide 6: WF Proposal (Option A) – III
Proposal 6: The blocking model is made spatially consistent.
  The blocking parameters (center of blockers and attenuation loss) are generated using the same methods utilized for spatial consistency in the TR.
  The correlation distance for blockers are defined in the table below:
Proposal 7: The blocking model is made temporally consistent
  To model the mobility of the blockage, a linear interpolation approach interpolating two attenuation values obtained at two temporal points is used.
Note: The proposed model parameters here can be modified based on simulation assumptions appropriately, if necessary.
 | UMi |  |  | UMa |  |  | RMa |  | InH
 | LOS | NLOS | O-I | LOS | NLOS | O-I | LOS | NLOS | 
Correlation distance (m) for cluster specific random variables | 10 | 10 | 5 | 10 | 10 | 5 | 10 | 10 | 5

## Slide 7: WF (Option B) – I
Option B proposes a hybrid geometric model for human and vehicle blocking
Proposal 1: The blockers are physically placed on the map with coordinates (xk,yk), where k=1, 2, …, K. Coordinates (xk,yk) can be based on simulation assumptions or randomly chosen.
  Note: Coordinates of blockers can be time-dependent to emulate moving scatterers.
Proposal 2: Number of blockers K is left to simulation assumptions.
  Note: Since blocking is strongly dependent on the distance to the blocker, only nearby blockers need to be considered; e.g., a particular UE.
Proposal 3: The height h and width w of the blockers are simulation assumptions. Recommended dimensions for simulations of typical blockers are provided in the following table:

## Slide 8: WF (Option B) – II
Proposal 4: Attenuation of clusters and paths is based on knife edge model taking into account the sizes of blockers, locations of blockers, locations and AoAs of the UE
  The per-path attenuation is given by
  where
  D1h1|h2|w1|w2 are the projected distances UE-edge from the side and from above according to Figure 1 below
  r is the projected distance to the screen
  The per-path screen edge positions are determined in a coordinate system rotated by the per-path AOA.
Figure 1: Shadowing screen model.

## Slide 9: WF (Option B) – III
Note: The model according to Proposals 1-4 in Option B is consistent in time, frequency, and space.