## Slide 1: Way Forward on V2V PC5 SLSS/PSBCH transmission
3GPP TSG RAN WG1 Meeting #85 R1-165749
Nanjing, China 23rd - 27th May 2016
Agenda Item: 6.2.2.7.2
Huawei, HiSilicon, ITRI, ZTE, OPPO

## Slide 2: Background
  Synchronization issue is more crucial for V2V since vehicles always need to communicate with proximate vehicles for safety reasons.
  It is required to reduce timing clusters as much as possible to avoid timing switching during which vehicles may miss some messages.
  There are areas, such as a tunnel or an underground parking lot, where UEs cannot receive either GNSS or eNB signals.
  Thus a procedure is needed in PC5-based V2V to deliver GNSS timing to out of GNSS coverage area.
  Synchronization can be maintained in the UE for several minutes after GNSS synchronization is lost.
  A synchronization source that has recently lost GNSS synchronization has more precise GNSS timing than the source that has lost GNSS for a longer time or never had GNSS timing.

## Slide 3: Proposal
  When a UE is in GNSS or GNSS-equivalent or eNB coverage, the UE shall transmits synchronization information of GNSS or GNSS-equivalent or eNB timing when a UE is configured by upper layers to do so
  After a UE changes from out of GNSS or GNSS-equivalent or eNB coverage to in GNSS or GNSS-equivalent or eNB coverage, the UE transmits synchronization information of GNSS or GNSS-equivalent or eNB timing when RSRP measurement is below a RSRP-threshold.
    RSRP-threshold is configured by the network.
  After a UE changes from in GNSS or GNSS-equivalent or eNB coverage to out of GNSS or GNSS-equivalent or eNB coverage and if the UE does not detect any SLSS or s-RSRP of the UE selected SLSS is below a s-RSRP-threshold, the UE transmits synchronization information, which is latest derive timing from GNSS or GNSS-equivalent or eNB timing.
    s-RSRP-threshold is configured by the network.