## Slide 1: WF on the CWS adjustment at the UE for Cat-4 LBT
Nokia, Alcatel-Lucent Shanghai Bell, Ericsson, [Broadcom]
3GPP TSG RAN WG1 #85
Nanjing, China, May 23-27, 2016
R1-165948
Agenda 6.2.1.5

## Slide 2: Proposal
  Definition:
    The reference scheduled burst is the most recent contiguous (i.e. without any gap in between) scheduled UL subframe(s) from for the UE
    The reference subframe is the first subframe in the reference scheduled burst where the eNB detects UL transmission from for the UE.
      The reference subframe is empty if the eNB does not detect any transmission within the reference scheduled burst.
The eNB signals one bit for CWS adjustment indication in UL grant to indicate whether the transmission from the UE in the reference subframe has been successfully received.
  If at least one of the TBs are successfully decoded, the CWS adjustment indication bit is set to 0; otherwise, it is set to 1.
  If the reference subframe is empty, the CWS adjustment indication is set to 1.

## Slide 3: Proposal
The UE follows the procedure below for CWS adjustment:
  If the UE did not transmit in the reference scheduled burst due to LBT failure, the CWSs for all the priority classes remain unchanged.
  Otherwise,
    if the CWS adjustment indication bit is 1, the UE shall increase the CWSs for all the LBT priority classes.
    If the CWS adjustment indication bit is 0, the UE shall reset the CWSs for all the LBT priority classes.
  The CWS is reset to the minimum value if the maximum CWS is used for K consecutive LBT attempts for transmission only for the priority class for which maximum CWS is used for K consecutive LBT attempts.
    K is selected by UE implementation from the set of values from (1, …,8).