## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-167949 Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on Beam Management
Huawei, HiSilicon, Potevio

## Slide 2: Background
in RAN1#85, some agreements were achieved for beam management [1]:
Both intra-TRP and inter-TRP beamforming procedures are considered.
Beamforming procedures are considered with/without TRP beamforming/beam sweeping and with/without UE beamforming/beam sweeping, according to the following potential use cases:
  UE movement, UE rotation, beam blocking:
    Change of beam at TRP, same beam at UE
    Same beam at TRP, change of beam at UE
    Change of beam at TRP, change of beam at UE
  Other cases are not precluded
Study beam (e.g. TRP beam(s) and/or UE beam(s)) management procedure (e.g. beam determination and change procedure) with/without prior acquired beam(s) information
  For both data and control transmission/receptions
  The procedures may or may not be the same for data and control.

## Slide 3: Proposal
Study on the following aspects for beam management
  TRP(s) used to transmit beam management RS is transparent to UE
  Beam management procedure based on L1 and L2 procedure
  Beam management procedure based on LF assisted HF
  Beam management includes the following two stages:
    Coarse beam alignment, i.e., periodic beam sweeping without prior acquired beam(s) information
    Fine beam alignment, i.e., periodic/aperiodic beam sweeping with prior acquired beam(s) information
      Strive to handle this procedure within a unified CSI framework in NR
      Fast link recovery procedure due to UE movement/rotation/blockage
        E.g., Monitoring multiple beam pairs for link recovery
      Beam probing based beam refinement/tracking
        E.g., beam selection, or angle estimation

## Slide 4: Proposal
RS design principle of Beam Management
  DL beam management can be based on DL DMRS in addition to DL RS dedicated to CSI acquisition and beam management
  UL beam management can be based on SRS, UL DMRS and energy-efficient UE-specific tracking signals