## Slide 1: WF on System Level Simulation Parameters for mMTC
ZTE, ZTE Microelectronics, Qualcomm,[Nokia],[]…
3GPP TSG RAN WG1 #86 R1-168069
Gothenburg, Sweden
22nd – 26th August 2016
Agenda item: 8.1.2.2
Document for decision

## Slide 2: Background
Traffic model is still not defined in SLS for UL mMTC
NB-IoT uplink report can be used as a reference for traffic model of UL mMTC for NR, where
  average inter-arrival time of the traffic is around 2 hours
  application layer packet sizes are mostly between 20 Bytes and 50 Bytes
In order to identify the schemes to support massive connections and future mMTC traffic
  Smaller average inter-arrival time, e.g. 30 minutes, could be considered in the evaluation

## Slide 3: Proposals
Traffic model is based on NB-IoT MAR model or Poisson distribution with average inter-arrival time of [2] hours
  other inter-arrival time is not precluded.
Link to system mapping should be based on sufficient link level simulations, incl. impact of code/interleaver collision, non-ideal channel estimation, realistic power control etc.
Random access procedure and grant procedure should be reported when presenting results