## Slide 1
WF on SLS evaluation methodologies for autonomous/grant-free/contention-based MA
LG Electronics, ZTE, ZTE Microelectronics
R1-168435
3GPP TSG RAN WG1 #86
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda item 8.1.2.2

## Slide 2: Background – offline discussion results
UL traffic model for mMTC applied to MA is as follows :
Attributes | Value or assumptions
Data packet arrival rate per UE | Poisson arrival with arrival rate λ
Number of UEs per cell | Companies report the number of UEs per cell
Physical layer target payload size | Option 1: Fix: [20, 40,] Bytes (Company reports the used value) Option 2: Variable, e.g., traffic model in NB-IoT Option 3: Random [20, 40, 200] Bytes Other option is not precluded Select option at RAN#86bis Company report the payload size
Simulation Bandwidth | Companies report the simulation bandwidth
Target packet drop rate | 0.01
Packet dropping criteria | Company report criteria

## Slide 3: Proposal
  For the SLS evaluation for autonomous/grant-free/contention-based UL MA applied to mMTC,
  Traffic model with Poisson arrival is used
    Companies are encouraged to report payload size used in the simulation
  At least following performance metrics are used
    Packet drop rate vs. packet arrival rate per cell curve
      Target packet drop rate for comparison of MA schemes is 0.01
      Companies are encouraged to provide packet dropping criteria
    Number of UEs per cell used in the simulation should be reported
    Note: packet arrival rate reflects system loading, e.g. number of arrived packets per cell per sec.

## Slide 4: Appendix
SLS methodologies are as follows:
  Drop N UEs per TRP
    Companies report the “N”
  Perform SLS evaluation varying packet arrival rate
    Obtain packet drop rate vs. arrival rate curve
    Obtain “max. arrival rate” that the system sustains at the “target packet drop rate(0.01) ”
  Note: Packet drop rate is the average percentage that packet is not successfully transferred to eNB in a given packet dropping criteria, e.g. a packet is not successfully transferred to eNB within a given time window [X]ms and/or after maximum [M] re-transmission/repetition