## Slide 1: WF on Spatial Multiplexing Schemes for MU-MIMO
Mitsubishi Electric, InterDigital, Samsung
3GPP TSG RAN WG1 Meeting #86bis R1-1610486 Lisbon, Portugal 10th - 14th October 2016
Agenda item: 8.1.4.2 Multi-antenna scheme

## Slide 2: Background: Recent studies on nonlinear precoding for MU-MIMO
In [1,2], MU-MIMO performance have been investigated in crowded scenarios for co-scheduled and closely located UEs and shown performance gains over linearly precoded systems
Using Tomlinson-Harashima Precoding (THP) based nonlinear precoding, link level simulations results have shown performance gains over linearly precoded systems in crowded scenarios [3]
Modulo operation does not have significant impact on UE complexity [4]
Interests to study nonlinear precoding schemes for NR MU-MIMO are indicated in [5,6]
[1] H. Nishimoto, et al., “Nonlinear Block Multi-diagonalization Precoding for High SHF Wide-band Massive MIMO in 5G”, PIMRC 2016, Valencia, Spain.
[2] X. Wang, et al., “Large Scale Experimental Trial of 5G Mobile Communication Systems―TDD Massive MIMO with Linear and Non-linear Precoding Schemes”, PIMRC 2016, Valencia, Spain.
[3] R1-1610229, “Performance comparison of nonlinear precoding schemes for NR MU-MIMO”, Mitsubishi Electric, Lisbon, Portugal, Oct. 2016.
[4] R1-164027, “Design of massive MIMO for New Radio”, Mitsubishi Electric, Nanjing, China, May, 2016.
[5] R1-167385, “TDD Massive MIMO for NR”, NTT Docomo, 3GPP RAN1#86, Gothenburg, Sweden, Aug. 2016.
[6] R1-1609905, “MIMO transmission schemes for NR”, Inter Digital, 3GPP RAN1#86b, Lisbon, Portugal, Oct. 2016.

## Slide 3: Background: Specification impacts on RS design and signalling
Impacts on RS design: Transparency for DMRS
Nonlinear precoding (NLP) is used for data symbols while linear precoding (without nonlinear precoding) is used for DMRS, as described in [7] and briefly in Appendix 1
  existing precoding methods are used for DMRS: no spec impact, transparency for DMRS is retained, see Appendix 1 and 2 for nonlinear/linear operation at TX and RX
Impacts on signaling
UE capability (signaling from UE to indicate if the UE is able to decode NLP or not) is required
  For UEs who can support only LP, send LP signals
  For UEs that can support NLP, send either LP*1 or NLP, depending on environments
  *1: NLP demodulator can demodulate LP signals as described in Section 3 in R1-166574
  [7] R1-1610227, “Nonlinear precoding schemes for NR MU-MIMO and their specification impact”, Mitsubishi Electric, Lisbon, Portugal, Oct. 2016.

## Slide 4: Proposal
Study performances of nonlinear precoding schemes for MU-MIMO focusing on the following aspects
  Potential nonlinear precoding schemes
  Performance advantages over linearly precoded systems
  Comparison of complexity with respect to linearly precoded systems
  Specification Impacts (e.g., signaling and RS design, etc.)

## Slide 5: Appendix 1: TX and RX with LP and NLP functions
TX
Step 1 Precode signals using THP
Step 2 Perform linear precoding
Underlined operations are new functions for nonlinear precoding
Operations without underlines are conventional linear precoding functions
Conceptual diagram of TX and RX with NLP (THP in this case) for data and LP for RS
Conceptual diagram of TX and RX with LP used for data and RS (current system)
RX
Step 1 Channel estimation via DMRS
Step 2 Decode linearly
Step 3 Use modulo operation after step 2
Underlined operations are new functions for nonlinear precoding
Operations without underlines are conventional linear precoding functions

## Slide 6: Appendix 2: TX and RX with NLP functions, detailed block diagram
TX
RX