## Slide 1: WF on Remaining Issues for Hybrid CSI
Samsung, Ericsson
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, 10th - 14th October 2016
Agenda item: 7.2.2.5.2
R1-1611013

## Slide 2: Background: RAN1#86
Agreement:
Further details on Mechanism 1
  …
  Working assumption: No inter-dependence between CSI calculations across two eMIMO-Types
  Reuse legacy CSI reporting mechanisms with the following refinement
  For PUCCH-based P-CSI
    Report i1(1) and RI(1) in one subframe
      FFS: Using either PUCCH format 2 or 3
    Periodicity of the CSI of 1st eMIMO-Type is an integer multiple of RI(2) periodicity of the 2nd eMIMO-Type.
    Subframe offset of the 1st eMIMO-Type is defined relative to RI(2) subframe offset of the 2nd eMIMO-Type.
      FFS: Whether subframe offset of the 1st eMIMO-Type can be fixed to 0
    Priority rule for collision handling is FFS.
  …

## Slide 3: Proposal 1
Confirm working assumption for mechanism 1:
  No inter-dependence between CSI calculations across two eMIMO-Types

## Slide 4: Proposal 2
Working assumption: Use PUCCH format 3 (PF-3) for CSI reporting of 1st eMIMO-Type
  A PF-3 resource is allocated for CSI reporting and/or A/N
Working assumption: PF resource usage follows legacy-like procedures as follows:
  For N≥1 CC(s):
    CSI-only reporting: Use PF-3 resource allocated for CSI
    A/N-only: If A/N is for Pcell only, use PF-1A/1B resource allocated for A/N. Otherwise use PF-3 resource allocated for A/N
    CSI and A/N collision: multiplex CSI and A/N using PF-3 resource allocated for A/N
      For TDD scenario, the DAI is set to be 1 (i.e. PF-1A/B is used only if for PCell and DAI in DCI format is the first DAI with value 1 that the UE detects)