## Slide 1: WF on UE beam switching
ZTE, ZTE Microelectronics
3GPP TSG RAN WG1 Meeting #87
Reno, USA, 14th –18th November 2016
Agenda: 7.1.2.5
R1-16xxxxx

## Slide 2: Background
Agreements (RAN1#86b):
RACH resource:
  A time-frequency resource to send RACH preamble
Whether UE needs to transmit one or multiple/repeated preamble within a subset of RACH resources can be informed by broadcast system information
  For example, to cover gNB RX beam sweeping in case of NO Tx/Rx reciprocity at the gNB

## Slide 3: Proposal
UE Tx beam(s) for preamble transmission(s) is selected by the UE.
  For the transmission of one preamble, as informed by broadcast system information:
  (For example, to cover the case of Tx/Rx reciprocity at the gNB)
  UE may switch UE Tx beam between subsequent transmissions of one preamble
    (For example, to cover UE Tx beam sweeping in case of NO Tx/Rx reciprocity at the UE)
  For the transmission of multiple/repeated preamble, as informed by broadcast system information:
  Multiple/repeated preambles are transmitted with the same UE Tx beam.
    (For example, to cover gNB RX beam sweeping in case of NO Tx/Rx reciprocity at the gNB)
  UE may switch UE Tx beam between subsequent transmissions of multiple/repeated preambles
    (For example, to cover UE Tx beam sweeping in case of NO Tx/Rx reciprocity at the UE)

## Slide 4: Example: one preamble
UE Tx
beam
time
...
TRP
Rx beam
...
...
...
...
...
one preamble
one preamble
one preamble
Subsequent transmissions of
one preamble

## Slide 5: Example: multiple/repeated preamble
UE Tx
beam
...
time
...
TRP
Rx beam
...
...
...
...
...
...
...
...
...
...
multiple/repeated
preambles
multiple/repeated
preambles
multiple/repeated
preambles
Subsequent transmissions of
multiple/repeated
preambles