## Slide 1: Way forward on initial access and mobility for wider BW operation
NTT DOCOMO, CATT, Ericsson, LG Electronics, MediaTek, OPPO
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R. China 15th – 19th May 2017
R1-1709505

## Slide 2: Background (Issues)
Issue 1: Single or multiple sync signal locations in wideband CC is supported
  For a single SS block in a wideband CC,
    For CA UE and/or non-CA UE with a smaller BW CC, UE-specific UE BW parts may not include SS-block
  For multiple SS blocks in a wideband CC,
    UE behaviors for multiple SS blocks, e.g., RRM measurement, are not clear, especially for UE capable of a single wider BW CC
Issue 2: BW capability is not known to the gNodeB during initial access
Issue 3: Frequency domain resource indexing and granularity, e.g., PRB indexing, RBG definition, are not clear when UEs with different BW capabilities coexist in wideband CC
  In LTE, frequency location is known to UE based on center SS frequency location and system BW. In NR, system BW may not be indicated and SS frequency location is not always at the center frequency of the system BW

## Slide 3: Proposals (Issue 1)
Support single and multiple SS block transmissions in wideband CC
  For a single SS block transmission in wideband CC,
    For non CA UE with a smaller BW capability and potentially for CA UE, the measurement gap for RRM measurement is supported (if it is agreed to allow for a CC not including SS-block)
  For multiple SS block transmissions in wideband CC,
    UE is informed of the presence/parameters of the SS block(s) and parameters necessary for intra-frequency measurement via either RMSI, other system information, or RRC signaling
    FFS: number of SS blocks in wideband

## Slide 4: Proposals (Issue 2)
The maximum bandwidth for CORESET for RMSI scheduling and NR-PDSCH carrying RMSI should be equal to or smaller than a certain DL bandwidth of NR that all UE can support in each frequency range
At least, for one RACH preamble format ,the bandwidth should be equal to or smaller than a certain UL bandwidth of NR that all UE can support in each frequency range
  This implies there could be other RACH preamble format with larger bandwidth than a certain bandwidth of NR that all UE can support

## Slide 5: Proposals (Issue 3)
For frequency location of CORESET for RMSI scheduling and NR-PDSCH for RMSI,
  Alt. 1: The signals are confined within the SS block BW
  Alt. 2: The signals are confined to a certain BW centered around the SS Block
    FFS: certain BW, but at least, it is supported by all the UEs
  Alt. 3: The signals are confined to channel BW configured by PBCH
Decide among the following three candidates
  Alt. 1 for CORESET and Alt. 2 for NR-PDSCH for RMSI
  Alt. 2 for CORESET and Alt. 2 for NR-PDSCH for RMSI
  Alt. 2 for CORESET and Alt. 3 for NR-PDSCH for RMSI
    FFS: Details on signaling