## Slide 1: WF on conflicting PHICH handling for short processing time with 1ms TTI
Sharp, …
3GPP TSG RAN1 #89
Hangzhou, China, 15th – 19th May 2017
Agenda Item: 6.2.1.1.2
R1-1709634

## Slide 2: Background (1/3)
DL subframe
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
NACK
UL subframe
Collision with PUSCH scheduled by UL grant with n+3 timing
Agreements in RAN1#88bis :
  If the UE receives conflicting PHICH with n+4 timing and UL grant with n+3 timing scheduling PUSCH for the same UL subframe of a carrier, only the PUSCH scheduled by UL grant with n+3 timing is transmitted.
  Note: This might not have specification impact
UL
Grant
n+3

## Slide 3: Background (2/3)
Possible behaviors of the UE which does not detect ACK via PHICH with n+4 timing on subframe n:
  UE behavior 1
    Layer 1 delivers NACK to MAC layer in subframe n, regardless of UL grant detection in subframe n+1.
  UE behavior 2
    Layer 1 suspends delivery of ACK/NACK to MAC layer until subframe n+1
      If UL grant with n+3 timing is detected in subframe n+1, Layer 1 delivers ACK for the PHICH-associated HARQ process,
      If UL grant with n+3 timing is not detected in subframe n+1, Layer 1 delivers NACK for the PHICH-associated HARQ process.

## Slide 4: Background (3/3)
In the current MAC spec, PUSCH dropping after NACK delivery is defined only for the collision between the PUSCH and measurement gap.
  If colliding with measurement gap, autonomous non-adaptive PUSCH retransmission has to be performed.
DL subframe
8
9
0
1
2
3
0
1
2
3
4
5
6
7
8
9
0
1
2
3
0
1
2
3
4
5
6
7
NACK
UL subframe
Collision with Gap
Figure 1: Autonomous non-adaptive PUSCH retransmission after a collision between a non-adaptive PUSCH retransmission and measurement gap

## Slide 5: Proposal (1/2)
Clarify RAN1’s understanding on UE behavior when the UE does not detect ACK via PHICH with n+4 timing on subframe n:
  Alternative 1
    Layer 1 delivers NACK to MAC layer in subframe n, regardless of UL grant detection in subframe n+1.
  Alternative 2
    Layer 1 suspends delivery of ACK/NACK to MAC layer until subframe n+1
      If UL grant with n+3 timing is detected in subframe n+1, Layer 1 delivers ACK for the PHICH-associated HARQ process,
      If UL grant with n+3 timing is not detected in subframe n+1, Layer 1 delivers NACK for the PHICH-associated HARQ process,

## Slide 6: Proposal (2/2)
If taking alternative 1,
  Clarify RAN1’s understanding on whether or not Autonomous non-adaptive PUSCH retransmission is adopted.
  Inform RAN2 of RAN1’s understanding on the above 2 issues.