## Slide 1
3GPP TSG RAN WG1 Meeting #90bis R1-1718818
Prague, P.R. Czechia, 9th – 13th, October 2017
Agenda item: 7.1.1
Summary on Supporting Multiple SCSs for SS Block
Samsung, MediaTek, AT&T, NTT DoCoMo, CMCC, T-Mobile, China Telecom, KT, KDDI, LGE, ZTE, Sanechips, Nokia, InterDigital, ITL, Sharp, Fujitsu, Sony, ETRI

## Slide 2: Background (1/2)
The following agreements were made in RAN1 regarding the numerology of SS block

## Slide 3: Background (2/2)
R1-1715373 (R4-1709187) Reply LS on NR minimum carrier bandwidth
RAN4 has identified issues with respect to this incoming LS after careful studies. RAN4 has agreed 5MHz and 50MHz to be applicable minimum carrier bandwidths for many Sub-6GHz and mmWave NR bands. However, for bands where these minimum bandwidths are required, there is also need on higher SS SCS due to either LTE-NR co-existence or wider minimum CH BW deployment need. Hence the support of 10MHz and 100MHz minimum carrier bandwidths associated with 30kHz and 240kHz SS SCS for these bands is unclear from RAN4 perspective.
RAN1 is asked to find a solution how to support the following cases:
  Minimum required channel BW and SS SCS for a Sub-6GHz band are 5MHz and 15kHz, respectively. An operator plans to operate with 10MHz bandwidth 30kHz SCS in order to deploy NR/LTE DL co-existence within the same band.
  For bands above 6GHz, the minimum required channel BW and SS SCS are 50MHz and 120kHz, respectively. An operator who has at least 100MHz contiguous spectrum, plans to operate with 240kHz SS SCS within the same band.
  RAN1 is asked to find a solution that shall support the ability for a UE to perform initial access to the NR cells operating with the above carrier bandwidth/SS SCS combinations.

## Slide 4: Discussion (1/4)
Proposals [RAN1 NR-AH3]:
  Alt 1: Redesign the SS block design, i.e., reduce PBCH BW to 12 PRBs so that UE minimum BW does not exceed 5 MHz for sub6GHz and 50MHz for over6GHz, regardless of the selected subcarrier spacing
  Alt 2: RAN4 is allowed to select up to two SCS values for SS/PBCH and the corresponding UE minimum BW for each band of a limited set of bands

## Slide 5: Discussion (2/4)
Multiple default SCSs request | Revising PBCH design (12 RBs)
Band n5, n66 | As current agreed SU for 5MHz (30kHz) is 11 RB, even revising PBCH as 12 RB, with 5MHz CHBW still cannot support 30kHz. Meanwhile revising PBCH required to extend PBCH symbols (from 2 to 4 or 5 symbols), then even with 30kHz SCS, operator cannot apply TDM operation for UL co-existence. Conclusion: Not solve problems, even make more worse
Band n41, n77, n78 | FFS situations still pending on operators initial deployment plan difference. Current CHBW already allow deploy either 15kHz or 30kHz SS numerology.
Mm Wave bands | Possible can be resolved, since with revising PBCH, 240kHz can be applied for 50MHz CHBW.
Observation: Even after truncating the PBCH bandwidth, multiple numerologies may still be needed. Hence, Alt1 is not a complete solution.

## Slide 6: Discussion (3/4)
Observation: If truncating the NR-PBCH bandwidth from 24 PRB to 12 PRB, at least two additional symbols are required for each SS block to achieve similar performance to current design, which may lead to lots of redesigns and further issues.
  The mapping of 6-symbol SS block into a slot may not avoid the collision with control channels
  URLLC 1ms latency requirement cannot be met if using 6-symbol SS block
Hence, Alt1 is not a realistic solution.
Evaluation results from R1-1717576 (Samsung)

## Slide 7: Discussion (4/4)
For the potential sync raster issue, there are multiple solutions.
  For example, the most problematic is for NR band N77, N78 (3.5GHz band) and band 41, with 30 kHz SCS and 10MHz minimum channel bandwidth. The following schemes can efficiently reduce the number of sync rasters:
    Alt1: Revising minimum channel bandwidth starting with 15MHz or above
    Alt2: Introduce multiple numerologies for SS block pending on channel bandwidth, for 10MHz carrier only allowed 15kHz SS Block
    Alt3: Truncating the NR-PBCH bandwidth
  RAN4 can try to solve the issue using Alt1 or Alt2 without the need of changing the SS block design in RAN1

## Slide 8: Clarification on Alt 2
For UE initial access to the concerned frequency bands mentioned in RAN4 LS, 120khz and 240khz SS block numerologies can be supported for above-6GHz; 15khz and 30khz SS block numerologies can be supported for below-6GHz.
  To minimize the impact on UE complexity and power consumption, the following options are recommended for support from RAN1 perspective, e.g.,
    Restrict the number of frequency bands and sync rasters with two SS block numerologies for detection
    Operator settings in the UE may provide operator’s used SCS information for prioritized cell search.
    The delay requirement for initial access is relaxed according to the number of numerologies per frequency band for detection without assistance information (e.g., operator settings information), if defined in RAN4.
For the idle and connected mode UEs, there is no blind detection of the SS block numerologies for the stand-alone carrier.
  For the intra-frequency case, SS block numerology is assumed same as the camping cell.
  For the inter-frequency case, the single SS block numerology shall be signaled by the network.